## Slide 1: SM Power Save for 11ay
Date: 2017-08-30
Authors:

## Slide 2: Abstract
This presentation proposes to extend the SM power save mechanism to 11ay.

## Slide 3: Motivation
11ay EDMG STAs are expected to be equipped with multiple receive chains in order to support MIMO configuration.
An EDMG STA consumes power on all active receive chains, even though they are not necessarily required for the actual frame exchange.
11n/11ac defines the spatial multiplexing power save (SM Power Save) mechanism, which enables the STA in an infrastructure BSS to operate with only one receive chain for a significant portion of time.
This contribution proposes to extend the SM power save mechanism to EDMG STAs, with some necessary changes to accommodate the new features introduced in 11ay.

## Slide 4: SM power save in 11n/11ac
There are two modes for SM power save:
  Static SM power save mode: the STA maintains only a single receive chain active.
  Dynamic SM power save mode: the STA enables its multiple receive chains when it receives the start of a frame exchange sequence addressed to it. An RTS/CTS sequence may be used for this purpose.
  The STA may use the SM Power Save frame to communicate its SM power save state.
A STA in dynamic SM power save mode cannot distinguish between an RTS/CTS sequence that precedes a MIMO transmission and any other RTS/CTS and, therefore, always enables its multiple receive chains when it receives the RTS addressed to it.
  This rule will cause unnecessary activations of multiple receive chains if the RTS is followed by a SISO transmission, therefore incurring additional power waste on multiple receive chains.

## Slide 5: SM power save in 11ay
11ay introduces the channel access rules for MIMO transmissions.
  MIMO indication is included in the control trailer appended to RTS or Grant or CTS-to-self frame prior to MIMO transmission.
  This indication enables EDMG STAs to avoid unnecessary activations of other receive chains if the RTS/Grant/CTS-to-self frame is followed by SISO transmission, therefore is more efficient in terms of saving power on multiple receive chains.
  However, an EDMG STA may need some time to activate and stabilize the other receive chains. It also needs some time (in the order of a probe delay) to detect active transmission for NAV observation and perform MIMO CCA for channel access.
  If an EDMG STA in SM power save mode maintains only one active chain and receives an RTS/CTS-to-self frame with MIMO indication, it may not have enough time to perform MIMO CCA for channel access.

## Slide 6: Proposal
If an EDMG STA is in dynamic SM power save mode, another STA shall transmit a Grant frame with a control trailer prior to initiating a MIMO transmission with it.
  The control trailer indicates the upcoming transmission will be MIMO, so that the EDMG STA knows it needs to activate its multiple receive chains.
  The Grant frame indicates the time it will attempt to initiate channel access for MIMO transmission, and this time offset shall be at least in the order of a probe delay, so that the EDMG STA has enough time to stabilize its multiple receive chains and perform MIMO CCA for later MIMO channel access.
  Even if the Grant Required field of the STA is set to 0 in the EDMG Capabilities element, as long as the STA is in dynamic SM power save mode, other STAs shall transmit a Grant frame prior to the actual MIMO channel access with this STA.
  The same as in 11n/11ac, the STA may use the SM Power Save frame to communicate its SM power save state to other STAs.

## Slide 7: Conclusions
This contribution extends the SM power save mechanism to EDMG STAs.
Some changes are proposed for more efficient power save, and to accommodate the unique features of 60GHz so that it can be applied to 11ay environment.

## Slide 8: Straw Poll
Do you agree to include the text proposed in [11-17-1213-00-00ay-draft-text-for-sm-power-save-for-11ay.docx] into the 802.11ay draft spec?

## Slide 9: References