## Slide 1: 802.11ba Architecture Discussion
Date: 2017-08-11
Authors:

## Slide 2: Abstract
This presentation continues considerations for a discussion between TGba and ARC SC, on any adjustments/additions needed to 802.11 architecture to support 802.11ba.
The intention is to propose some approaches to any such adjustments/additions that might be needed to support the 11ba architecture.

## Slide 3: Questions/topics discussed with TGba, at Berlin F2F
Is the WUR an independent PHY? Yes, it is a fully independent PHY. Coexistence/cooperation aspects have been built-in, to allow channel sharing with traditional 802.11 PHYs.
Is the WUR an independent MAC? Probably/possibly. Note, however, it is not “standalone”. The WUR MAC is a “companion” MAC/PHY that can only operate under the control of negotiation that takes place over the “main” MAC/PHY.
Is the WUR always physically collocated with an 802.11 AP or STA? Yes.
Does the WUR have an address? Or, does it “share” the collocated STAs address? The WUR MAC/PHY do not have a separate MAC Address. There is a WUR identifier, with local negotiation and scope only, however. WUR does not associate with the BSS.

## Slide 4: Questions/topics discussed with TGba, at Berlin F2F
Does the WUR MAC connect to/integrate with the 802.11 MAC? Yes. Per above, around negotiation with peer(s), and addressing. And, power on/off is coordinated between the MACs.
OR… Does the WUR ‘wake’ the device, and the device contains independent WUR and an 802.11 MAC/PHY, and some ‘host function’ between them? Some debate on this, perhaps. For now, assuming the model is MAC <-> MAC connection.
Perhaps related/duplicate: Does the introduction of the WUR impact the behavior of a collocated/integrated STA’s MAC/PHY?

## Slide 5: More advanced questions/topics discussed briefly in Berlin F2F
Does a WUR associate to a BSS? No.
If yes, the same BSS as any collocated/integrated STA, or a separate ‘overlay’ BSS of WUR devices? NA
Does the WUR work with all 802.11 PHYs e.g. a, b, g, n, ac, ad, ah, ax, ay? WUR only runs in 2.4/5 GHz. But, can work with all PHYs (maybe?).
Does the WUR work with mesh STAs? IBSS? OCB? Mesh, IBSS, OCB uses are TBD in the future, not now

## Slide 6: TGba architecture new questions (from Berlin Wed AM1 ARC)
Does every WUR stack have an individual “ID” (“WUR address”)? Or, could a given WUR stack be only addressed using a “group ID” in some scenarios?
How are WUR ID’s made globally unique, or are they? What about overlapping WUR coverage? Prevented using the same solution as security protections? Prevented through selection of different sub-carriers?
How does the WUR stack become aware of ongoing NAV protections? RX doesn’t need to know. What about the TXr?
For protection – how much of a legacy frame header is sent? Just PHY header? Some MAC header (addresses? NAV? Etc)
Is there any sharing (necessarily, as part of the design, not implementation choice) of RF front-end?

## Slide 7: TGba architecture new questions (from Berlin Wed AM1 ARC)
What happens when the Main stack wakes up? Does it still have an association? Is it in some power save state (which)?
“Yes, fully independent PHY” – is that for the RX side, or the TX side?
What about error recovery? STA goes out of range? What if the AP changes (DFS, ITS, etc)?

## Slide 8: TGba architecture assumptions (to be confirmed/discussed)
WUR RX doesn’t need to know about NAV or other medium-related state. For TXr, the Main stack runs the usual medium access, and waits until it has a TxOp, then triggers the WUR to TX.
On the RXr, only one stack (WUR or Main) is active at a given point in time. During WUR Mode doze, legacy ‘scheduled’ activities are suspended (details TBD).
On the RXr, when the Main stack is woken up by the WUR stack, it still has an association and is in an existing mechanism power save state (WNM Sleep Mode, U-APSD, etc.?). Upon wakeup, the Main stack TXs to its AP, which is the indication that the wakeup was successful and completed.
On the WUR RX STA (the sleeping node), the WUR can be 100% RX with no TX capability at all. There is a TXr on the master node, so the nodes are therefore (potentially) different architecturally.
The WUR “wakeup” frame does not NAV protect to cover the sleeping device’s Main radio waking up and TXing.

## Slide 9: Current 802.11 architecture concepts
There is no “STA” with more than one PHY
  Need to investigate implications of a “companion” PHY (let alone MAC)
A “STA” is a singly addressable instance of a MAC and PHY
  This is still true with WUR. Still only one MAC Address for the “pair” of Main stack and WUR stack.

## Slide 10: Current 802.11 architecture concepts
A STA has a single MAC, single PHY, and Mgmt, per Figure 4-19

## Slide 11: Adding WUR concepts …
A dozing STA has two, cooperating, MACs and PHYs
WUR PHY is RX only, is WUR MAC also RX only? (Probably)

## Slide 12: Adding WUR concepts …
For sake of independent operation, probably has (at least some) Management Entities dedicated to the WUR operation

## Slide 13: Adding WUR concepts …
Note: No MAC SAP (no data frames); shared SME; shared 802.1X mgmt (even relevant?)

## Slide 14: Adding WUR concepts …
Need definitions of:
MLME SAP for WUR (probably pretty simple)
WUR MLME <-> Main MLME primitives (also: to/from SME or direct?)
WUR PHY SAP and PLME SAP (RX only, any other difference from ‘normal’?

## Slide 15: Adding WUR concepts …
On transmitter (master) side:
Is WUR TX really a separate stack, or a “mode” of the Main? (What band/channel are they each on? (Main does channel access for WUR?))
Is WUR stack TX only, or TX/RX?
Different primitives Main MLME <-> WUR MLME (channel access stuff, instead of wakeup stuff). Anything else?
Any other differences (from RX model, or from legacy STA)?