## Slide 1: Discussion on Rank Adaptation
Date: 2017-08
Authors:

## Slide 2: Background
MIMO transmission is supported in 802.11ay. For SU-MIMO transmissions, up to 8 data streams are supported. Rank adaptation procedure for SU-MIMO transmission should be considered. Corresponding signaling and mechanisms should be designed to enable rank adaptation in an efficient way.

## Slide 3: Example Rank Adaptation Procedure

## Slide 4: Problems
Is that possible to transmit data using a lower rank and perform full rank training using TRN field?
A TX sector combination index was signaled in a Grant frame
The MIMO channel corresponding to the index does not have full rank, based on the measurement performed in the MIMO phase of BF training
Data is transmitted in a lower rank, i.e. NSTS < min(NTX, NRX)
Beam tracking initiator wants to check whether channel has changed or all the MIMO sectors are available for transmission
Without aggregating a BRP frame, TRN field has to be transmitted with the same number of streams as data NSTS
Beam tracking initiator cannot take advantage of increased rank if channel has changed

## Slide 5: Proposed changes
Add a field “Number of TRN transmit chains” in EDMG Header-A for SC/OFDM PHY SU PPDU
Field | Number of bits | Description
Number of TRN transmit chains | 3 | The value of this field + 1 indicates the number of transmit chains used in the transmission of the TRN field of the PPDU. This field is reserved when the EDMG TRN Length field is 0

## Slide 6: Straw Poll
Do you agree to include the changes described in 11-17-1254-00-00ay?