## Slide 1: WUR Mode Operation Procedures
Date: 2017-11-8
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
WUR STA can operate WUR mode and PM mode simultaneously.
  WUR STA operates WUR mode and PS mode simultaneously according to 4.5 of 11ba SFD [1].
  When WUR STA operates WUR mode and active mode simultaneously, its PCR behaves exactly as in active mode.
When WUR STA does not operate in WUR mode, it just follows PM mode operation.
WUR Mode Operation

## Slide 3
According to 11ba SFD [1], WUR mode signaling shall be defined for the WUR STA to enter the WUR mode by explicit signaling
  Wake-up operating parameter is notified in WUR mode signaling
  Example wake-up operating parameters:
    WUR Beacon interval,
    WID (WUR receiver identifier),
    Duty cycle schedule of WUR receiver,
    …
Implication:
  WUR STA can enter WUR mode by a WUR mode entry procedure incorporating WUR negotiation
WUR Mode Entry (1/2)
Wake-up operating parameters

## Slide 4
According to 11ba SFD [1], WUR Action frame shall be defined to enable WUR negotiation
Implication:
  WUR STA can enter WUR mode via a WUR negotiation procedure, followed by a WUR mode entry procedure
  In this case, it is unnecessary to negotiate wake-up operating parameters during the WUR mode entry procedure
WUR Mode Entry (2/2)
Wake-up operating parameters

## Slide 5
Why Separate WUR Negotiation and WUR Mode Entry Procedures are Necessary?
WUR negotiation may be incorporated into the association procedure and the WUR mode entry procedure can be performed later.
  WUR Mode element can be put into the Association Request/Response frame.
When WUR STA re-enters WUR mode, if wake-up operating parameters does not change, WUR negotiation is not required.
Frame exchange for the WUR mode entry procedure can be different from that for the WUR mode entry procedure incorporating WUR negotiation
  WUR mode entry procedure:
    WUR Mode Request frame + Ack frame
  WUR mode entry procedure incorporating WUR negotiation:
    WUR Mode Request frame + Ack frame + WUR Mode Response frame + Ack frame
In summary, separate WUR negotiation and WUR mode entry procedures can improve MAC efficiency.

## Slide 6: WUR Mode Exit
WUR STA can exit WUR mode via a WUR mode exit procedure.
Wake-up operating parameters
Wake-up operating parameters

## Slide 7: Proposal: WUR Action Frame
In addition to WUR negotiation, WUR Action frame shall also enable
  WUR mode entry
  WUR mode entry incorporating WUR negotiation
  WUR mode exit
Merit: simplified 11ba specification
The WUR Action field identifies different WUR Actions
  WUR Mode Request, WUR Mode Response, etc.
The WUR Mode element contains wake-up operating parameters

## Slide 8: Example WUR Mode element
Name | Action Type value
WUR negotiation | 0
WUR mode entry | 1
WUR mode entry incorporating WUR negotiation | 2
WUR mode exit | 3
Reserved | 4-255
When Action Type is 0 or 2, wake-up operating parameters related fields are present. Otherwise they are not present.

## Slide 9: Summary
Various procedures related to WUR mode operation are addressed.
WUR Action frame is suggested to enable all the procedures related to WUR mode operation.

## Slide 10: Reference
11-17-0575-05-00ba-spec-framework
11-17-0342-04-00ba-wur-negotiation-and-acknowledgement-procedure-follow-up
11-17-0379-04-00ba-sfd-mac-proposal
11-17-0071-00-00ba-high-level-mac-concept-for-wur.pptx

## Slide 11: SP
Do you support to modify R.4.2.A in 11ba SFD as follows?
  R.4.2.A: Define WUR Action frame to enable WUR negotiation and WUR mode signaling
    – Note that WUR Action frame is sent through primary connectivity radio
Result: Y:15/N:0/A:19

## Slide 12: Motion
Move to modify the following text in 11ba SFD
  R.4.2.A: Define WUR Action frame to enable WUR negotiation and WUR mode signaling
    – Note that WUR Action frame is sent through primary connectivity radio
  Move: Lei Huang Second:
  Result: