## Slide 1: WUR Mode Signaling
Date: 2017-09-11
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have decided to adopt explicit mode signaling in SFD
  If an WUR STA wants to change its operating mode, it will use explicit mode signaling
  However, we don’t have any detailed operation of explicit signaling in our current SFD
In this submission, we will address details of explicit mode signaling

## Slide 3: Signal type of WUR mode signaling
One-Way signaling
Two-Way signaling
Three-Way signaling

## Slide 4: One-Way signaling
Pros.
  Simple and lowest overhead
Cons.
  AP cannot indicate or change STA’s operating parameter
  WUR negotiation procedure shall be performed in advance for handshaking WUR parameter

## Slide 5: Two-Way signaling
Pros.
  AP can indicate or change STA’s operating parameter (WUR negotiation procedure doesn’t have to performed in advance)
Cons.
  Higher overhead
  If an AP couldn’t receive ACK, the AP will retransmit WUR Mode response frame to the STA but the STA will operate in WUR mode

## Slide 6: Three-Way signaling
Pros.
  STA can revise its operating parameter after receiving WUR mode response frame from AP
Cons.
  Highest overhead

## Slide 7: Proposal
We propose that baseline signal type is one-way signaling
  One-way signaling has minimum overhead and it is very simple
And we propose that two-way signaling can be used optionally
  An AP may want to change WUR parameter for a STA in some cases
  Detail condition for two-way signaling is TBD

## Slide 8: Signaling Omission
It may be a huge overhead to perform an explicit WUR Mode signaling whenever an WUR STA changes its operation mode
So we propose that explicit WUR mode signaling can be omitted in certain conditions to reduce signaling overhead

## Slide 9: Mode change case
Case 1: Active mode → WUR mode
  Case 1-1: Initial mode transition after association
    A STA shall use explicit signaling in this case because an AP cannot be aware of the STA’s operating mode without signaling
  Case 1-2: Return to WUR mode after data reception and WUR parameter isn’t changed
    Explicit signaling can be omitted in this case because an AP can assume that the STA will operate in WUR mode after data reception without any parameter change
  Case 1-3: Return to WUR mode after data reception and WUR parameter is changed
    A STA shall use explicit signaling in this case because WUR parameter shall be negotiated by WUR negotiation procedure

## Slide 10: Mode change case
Case 2: WUR mode → Active mode
  Case 2-1: For DL data reception (WUP has been received)
    We have defined that a STA should send a response frame to the AP after receiving a unicast wake-up packet
    The response frame is one of explicit signaling
  Case 2-2: Instant active mode for UL data transmission (it will return to WUR mode as case 1-2)
    Explicit signaling can be omitted in this case because the STA will transmit UL data and will return to WUR mode
  Case 2-3: Permanently change to active mode
    A STA shall use explicit signaling in this case because the STA will not return to WUR mode again

## Slide 11: Signaling omission case

## Slide 12: Summary
In this submission, we proposed two items to define detail operation of WUR mode signaling
  Frame sequence
  Signaling condition

## Slide 13: Straw poll 1
Which options do you prefer for WUR Mode signaling?
  Option 1: one-way signaling
  Option 2: two-way signaling
  Option 3: three-way signaling

## Slide 14: Straw poll 2
Do you agree to add following text in the SFD?
  WUR Mode signaling is performed following sequence
    An WUR STA may send WUR Mode Request frame to indicate WUR mode signaling

## Slide 15: Straw poll 3
Do you agree to add following text in the SFD?
  WUR Mode signaling is performed following sequence
    An WUR STA may send WUR Mode Request frame to indicate WUR mode signaling
    An AP that received WUR Mode Request frame may send WUR Mode Response frame under TBD condition (e.g. WUR Parameter modification)

## Slide 16: Straw poll 4
Do you support explicit Mode signaling omission in following cases ?
  Case 1: Return to WUR mode after data reception and WUR parameter isn’t changed
  Case 2: Instant active mode for UL data transmission (It will return to WUR mode)

## Slide 17: Straw poll 5
Do you agree to add following text in SFD?
  An STA can change its operating mode into WUR mode without explicit WUR mode signaling if all of following conditions are met
    The STA received data frame and More Data subfield in the data frame equals to 0
    Just before receiving data frame, the STA had woken from WUR mode by receiving Wake-up packet
    WUR operating parameter doesn’t change

## Slide 18: Straw poll 6
Do you agree to add following text in SFD?
  An STA can change its operating mode from WUR mode without explicit WUR mode signaling if all of following conditions are met
    The STA will transmit data frame
    After transmitting all buffered data frame, the STA will change its operating mode into WUR mode
    WUR operating parameter will not change