## Slide 1: Vendor Specific WUR Frame Follow Up
Date: 2018-01-xx
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Dan Bravo |  |  |  | 
Noam Ginsburg |  |  |  | 
Robert Stacey |  |  |  | 

## Slide 2: Abstract
We have agreed to have a entry in the type field to indicate vendor specific frame [1] that can carry vendor specific information
We also have agreed to put OUI1, which is the 12 MSBs of the OUI, in Address field of WUR frame [1]
We provide follow up for the design for vendor specific frame

## Slide 3: Proposal
The TD control field of vendor specific frame carries 12 LSBs of OUI
  It is optional for a STA to support vendor specific frame
    Note that support of non-zero length Frame body is already optional

## Slide 4: Straw Poll
Do you support to add the following texts in SFD and D0.1?
  The TD control field of vendor specific frame carries 12 LSBs of OUI

## Slide 5: Motion
Move to add the following texts in SFD and D0.1
  The TD control field of vendor specific frame carries 12 LSBs of OUI
Move:
Second:

## Slide 6: Reference
[1] 11-17-0575-08 Spec Framework