## Slide 1: WUR Preamble SYNC Field Design
Date: 2017-07-09
Authors:

## Slide 2: Introduction
In previous contributions[1, 2], the design of dual SYNC sequences are proposed to facilitate mode or rate signaling
We propose the design of dual SYNC sequences and evaluate the performance

## Slide 3: Recap: Dual WUR SYNC Design
Two possible SYNC sequences: SYNC1 and SYNC2
  Receiver tries to detect both SYNC sequences
  If SYNC1 is detected, one set of mode/rate is used for WUR Data
  If SYNC2 is detected, the other set of mode/rates is used for WUR Data
  One example: SYNC1 signals lower rate, SYNC2 signals higher rate
    To achieve better reliability for low-rate mode, prefer longer sequence
    To achieve better efficiency for high-rate mode, prefer shorter sequence
LSTF
LLTF
LSIG
WUR SYNC1
WUR Data
BPSK
Symbol
LSTF
LLTF
LSIG
WUR SYNC2
WUR Data
BPSK
Symbol

## Slide 4: SYNC Design Criteria
SYNC1 and SYNC2 have good autocorrelation (AC) properties, including the 6 legacy 20MHz symbols
  low correlation for all offsets
  Find the SYNCs with smallest offset correlation ratio:
SYNC1 and SYNC2 have low mutual cross correlation(CC), including the 6 legacy 20MHz symbols
  low cross correlation for all offsets
  Find the SYNCs with smallest cross correlation ratio:
pair

## Slide 5: Dual SYNC Design
M-sequence is a good candidate, which satisfies the autocorrelation property [3, 4]
  M-sequence is of length 2^N-1, which is not of zero DC
  Add one 0/1 to make length of 2^N, with good autocorrelation property
Similar to Gold sequence pair design, pick two M-sequences that meet the cross-correlation criteria
  With SYNC1 and SYNC2 length (N1, N2) design, find all M-sequence pair associated with different prime polynomials
  Add one 0/1 to make length of 2^N1 and 2^N2
  Find the pair with the least cross-correlation ratio

## Slide 6: Candidate Dual SYNC Sequences
S1 length | S2 length | SYNC1/SYNC2 | AutoCorr Max Ratio | CrossCorr Max Ratio
16 | 16 | 1 0 0 1 1 0 1 0 1 0 1 1 1 0 0 0 | 0.1250 | 0.2500
 |  | 1 1 0 1 0 1 1 0 0 1 0 0 0 1 0 1 | 0.1250 | 0.1875
32 | 16 | 1 0 1 1 0 0 0 0 1 1 1 0 0 1 1 0 1 0 1 1 1 1 0 1 0 0 0 1 0 0 1 0 | 0.1250 | 0.1250
 |  | 1 1 1 0 0 0 1 0 0 1 1 0 1 0 1 0 | 0.1250 | 0.250
32 | 32 | 1 0 1 1 0 0 1 1 1 0 0 0 0 1 1 0 1 0 1 0 0 1 0 0 0 1 0 1 0 1 1 1 | 0.0938 | 0.1250
 |  | 0 0 1 0 1 1 1 1 0 1 1 1 0 0 0 1 0 1 0 1 1 0 1 0 0 0 0 1 1 0 0 1 | 0.0938 | 0.1250
64 | 16 | 1 1 0 0 1 1 1 1 0 1 1 1 0 1 0 1 1 0 1 0 0 1 1 0 1 1 0 0 0 1 0 0 1 0 0 0 0 1 1 1 0 0 0 0 0 1 0 1 0 1 1 1 1 1 0 0 1 0 1 0 1 0 0 0 | 0.0938 | 0.1875
 |  | 1 0 1 0 1 1 0 0 1 0 0 0 1 0 1 1 | 0.1250 | 0.1875
64 | 32 | 1 0 1 1 0 0 1 0 1 1 0 1 0 1 1 1 0 1 1 1 1 0 0 1 1 0 0 0 1 0 1 0 1 0 0 1 0 1 1 1 1 1 0 1 0 0 0 0 0 1 1 1 0 0 0 0 1 0 0 1 0 0 0 1 | 0.1250 | 0.0938
 |  | 1 0 1 1 0 0 1 1 1 0 0 0 0 1 1 0 1 0 1 0 0 1 0 0 0 1 0 1 0 1 1 1 | 0.1250 | 0.1563
64 | 64 | 0 1 1 0 1 1 1 0 1 1 0 0 1 1 0 1 0 1 0 1 0 1 1 1 1 1 0 0 0 0 0 1 0 0 0 0 1 1 0 0 0 1 0 1 0 0 1 1 1 1 0 1 0 0 0 1 1 1 0 0 1 0 0 1 | 0.0938 | 0.0938
 |  | 1 1 1 0 0 1 0 1 0 1 0 0 0 1 1 0 0 1 1 1 1 0 1 1 1 0 1 0 1 1 0 1 0 0 1 1 0 1 1 0 0 0 1 0 0 1 0 0 0 0 1 1 1 0 0 0 0 0 1 0 1 0 1 1 | 0.1406 | 0.1406

## Slide 7: Simulation Settings
Packet
  WUR signal uses center 4MHz in 20MHz bandwidth
  2ms noise before the WUR packet
  Payload: 24 bits, Manchester Coding
SNR defined on 20MHz noise
CFO = 20ppm, fc = 2.4GHz, No phase noise
Receiver
  5th order 4MHz butterworth filter with 2.5MHz cutoff frequency
  Simple AGC based on 6 legacy 20MHz symbols
  20MHz sampling rate with in-phase path
  Local cross-correlator template has 1 for bit 1, and -1 for bit 0
LSTF
LLTF
LSIG
WUR SYNC
WUR Data
BPSK
Symbol
2ms noise

## Slide 8: Channel: DNLOS

## Slide 9: Channel: DNLOS (32-4us, 16-4us)

## Slide 10: Channel: DNLOS (64-2us, 32-2us)

## Slide 11: Summary
Dual SYNC sequence design is an appealing design
The sequence pair can be designed from M-sequences with minimum auto-correlation and cross-correlation
False SYNC sequence detection rate is low
For dual SYNC design to signal one low rate and one high rate
  Longer SYNC1 sequence plus shorter SYNC2 sequence is preferred

## Slide 12: Reference
[1] IEEE 802.11-17/0679r2, “Preamble Design for WUR WLAN”
[2] IEEE 802.11-17/1345r0, “PHY frame format discussions”
[3] IEEE 802.11-17/0997r0, “preamble-options”
[4] IEEE 802.11-17/0991r0, “preamble-design-and-simulations”