## Slide 1: Symbol Structure
Date: 2017-09-11
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We agreed to use the data rates of 62.5Kbps and 250Kbps
In this contribution, we investigate possible symbol structures for each data rate and compare PER performance among them

## Slide 3: Symbol Structures for 62.5Kbps (1/2)
Structure 1
  ON + OFF + ON + OFF / OFF + ON + OFF + ON
Structure 2
  ON + ON + OFF + OFF / OFF + OFF + ON + ON
Structure 3
  ON + OFF / OFF + ON with BCC using the code rate of 1/2
Both ON- and OFF-signals have a 4us length
Two options are considered for the ON-signal
  Option 1 : 0.8us CP + 3.2us signal
  Option 2 : 0.8us Null CP + 3.2us signal
  Option 1 and 2 have the same total power, and thus, the 3.2us signal part of option 2 has more power than that of option 1
  In this contribution, we assume that 3.2us signal is obtained from performing IFFT after applying 13-length sequence which is optimal in terms of the PAPR to contiguous 13 subcarriers with the subcarrier spacing of 312.5KHz as shown in [1]
To decode the symbol, we use the whole signal (four 4us signals) or four 3.2us signal portions for option 1 and just four 3.2us signal portions for option 2

## Slide 4: Symbol Structures for 62.5Kbps (2/2)
Following cases are compared
  Case 1 : Structure 1 w/ option 1 and using the whole signal for decoding
  Case 2 : Structure 1 w/ option 1 and using 3.2us signal portions for decoding
  Case 3 : Structure 1 w/ option 2 and using 3.2us signal portions for decoding
  Case 4 : Structure 2 w/ option 1 and using the whole signal for decoding
  Case 5 : Structure 2 w/ option 1 and using 3.2us signal portions for decoding
  Case 6 : Structure 2 w/ option 2 and using 3.2us signal portions for decoding
  Case 7 : Structure 3 w/ option 1 and using the whole signal for decoding
3.2us ON-signal
4us OFF-signal
0.8us CP
0.8us Null CP
Case 1, 2
Case 3
Case 4, 5
Case 6

## Slide 5: Simulation Results for 62.5Kbps
TGnD Channel
UMi NLoS Channel
PER performance

## Slide 6: Discussion
Case 7 (i.e., using BCC) is the best in terms of the PER performance but it may lead to high power consumption
As for the ON-signal, option 2 (i.e., null CP) is slightly better than option 1
  The 3.2us signal part for option 2 has more power than that of option 1
  Nulling the CP and using 3.2us signal portions for decoding can overcome the ISI (Inter-Symbol Interference) or intra-symbol interference
Structure 1 and 2 have a similar performance for the TGnD channel whereas structure 2 (i.e., ON + ON + OFF + OFF / OFF + OFF + ON + ON) is better for the UMi NLoS channel
  Two OFF-signals can be affected by the ISI or intra-symbol interference in structure 1 while only one OFF-signal is distorted in structure 2
Note that the trend is similar even if we apply the 13-length sequence which reuses STF sequence [1] as shown in Appendix B

## Slide 7: Symbol Structures for 250Kbps (1/2)
Structure 1
  2us ON + 2us OFF / 2us OFF + 2us ON
Structure 2
  0.8us null CP + 1.6us ON + 1.6us OFF / 0.8us null CP + 1.6us OFF + 1.6us ON
Three options are considered for the 2us ON-signal in structure 1
  Option 1 : No Null + 2us signal
  Option 2 : 0.4us Null + 1.6us signal
  Option 3 : 0.8us Null + 1.2us signal
  All options have the same total power (i.e., 2us, 1.6us and 1.2us signal parts have the same power for option 1, 2 and 3, respectively)
  We assume that 2us/1.6us/1.2us signals are obtained by choosing a certain part which has the lowest PAPR within 3.2us signal used for the data rate of 62.5Kbps
As to decoding the symbol in structure 1, we use the whole signal (two 2us signals), two 1.6us signal portions and two 1.2us signal portions for option 1, 2 and 3, respectively
For structure 2, we just use two 1.6us signal portions for decoding

## Slide 8: Symbol Structures for 250Kbps (2/2)
Following cases are compared
  Case 1 : Structure 1 w/ option 1 and using the whole signal for decoding
  Case 2 : Structure 1 w/ option 2 and using 1.6us signal portions for decoding
  Case 3 : Structure 1 w/ option 3 and using 1.2us signal portions for decoding
  Case 4 : Structure 2 w/ 0.8us Null CP and using 1.6us signal portions for decoding
1.6us ON-signal
1.2us ON-signal
2us OFF-signal
0.8us Null
0.4us Null
2us ON-signal
1.6us OFF-signal
Case 2
Case 3
Case 1
Case 4

## Slide 9: Simulation Results for 250Kbps
TGnD Channel
UMi NLoS Channel
PER performance

## Slide 10: Discussion (1/2)
Case 1 (i.e., no null within 2us on-signal) can be affected by ISI and intra-symbol interference and thus using the whole signal for decoding can lead to performance degradation
  In spite of using two 1.6us or two 1.2us signal portions for decoding in case 1 , its performance is not as good as that of case 2 especially for the TGnD channel as shown in Appendix C due to much lower power of 1.6us and 1.2us signal portions in case 1 than that of 1.6us signal part in case 2
Case 4 (i.e., 0.8us null CP + 1.6us ON + 1.6us OFF / 0.8us null CP + 1.6us OFF + 1.6us ON) is quite vulnerable to intra-symbol interference because there is no guard between 1.6us ON- and OFF-signals and thus its performance is not good especially for the UMi channel

## Slide 11: Discussion (2/2)
Case 2 and 3 (i.e., 0.4us/0.8us null within 2us on-signal) seem robust to ISI and intra-symbol interference, and thus, they have a better performance than the others
  Case 2 and 3 have a similar performance in the UMi NLoS channel whereas case 2 has a slightly better performance in the TGnD channel
  On the other hand, if we use the STF sequence for the 13-length sequence, case 3 is better than case 2 for both TGnD and UMi NLoS channels as shown in Appendix D
  Note that, regardless of the 13-length sequence, the null portion is helpful to a performance

## Slide 12: Conclusion
For the data rate of 62.5Kbps
  In consideration of the power consumption issue, a 16us symbol without BCC may be favorable
  Given the PER performance, it may be advisable to use OFF+OFF+ON+ON / ON+ON+OFF+OFF as the symbol structure with 4us length for both ON and OFF
  Nulling the CP within the ON-signal is also beneficial to the PER performance
For the data rate of 250Kbps
  Given the PER performance, it may be advisable to use ON + OFF / OFF + ON with a null portion at the front of the ON-signal as the symbol structure with 2us length for both ON and OFF
  The length of the null portion needs to be further investigated

## Slide 13: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  Symbol structure of the data rate of 250Kbps for each information is as follows
Information 0 | Information 1
2us ON + 2us OFF | 2us OFF + 2us ON

## Slide 14: Straw Poll #2
Do you agree to take the following waveform coding as an optional feature of WUR frame format?
  2usec ON-signal for the data rate of 250Kbps is composed of a TBD usec null portion and a 2-TBD usec signal part
  The TBD usec is non-zero
  Indication of capability to handle the proposed waveform is TBD
  The proposed waveform is for the payload and is not applied to the WUR preamble SYNC symbols and TBD indication bit(s)

## Slide 15: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  Symbol structure of the data rate of 62.5Kbps for each information is as follows
Information 0 | Information 1
4us ON + 4us ON + 4us OFF + 4us OFF | 4us OFF + 4us OFF + 4us ON + 4us ON

## Slide 16: Straw Poll #4
Do you agree to add the following to the 11ba SFD?
  4us ON-signal for the data rate of 62.5Kbps is composed of a 0.8us null CP and a 3.2us signal part
    3.2us signal can be computed by performing IFFT after applying 13-length sequence to contiguous 13 subcarriers with the subcarrier spacing of 312.5KHz

## Slide 17: Motion
Move to add the following to the 11ba SFD
  Symbol structure of the data rate of 250Kbps for each information is as follows
  For 2us ON-signal, there is always energy.
  Moved by :
  Seconded by :
  Results
Information 0 | Information 1
2us ON + 2us OFF | 2us OFF + 2us ON

## Slide 18: References
[1] IEEE 802.11-17/0964r4 Signal Bandwidth and Sequence for OOK Signal Generation

## Slide 19: Appendix

## Slide 20: Appendix A - Simulation Assumptions
48 symbols in payload
CFO [3], Phase noise [4] applied
No timing error
Butterworth filter
  2.5MHz cut off frequency, second order
20MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz and 5GHz
SNR defined in 20MHz

## Slide 21: Appendix B – PER Performance for 62.5Kbps Using STF sequence for 13-Lenth Sequence
TGnD Channel
UMi NLoS Channel
PER performance

## Slide 22: Appendix C – PER Performance for 250Kbps According to Signal Portions Used for Decoding
PER performance
TGnD Channel
UMi NLoS Channel

## Slide 23: Appendix D – PER Performance for 250Kbps Using STF sequence for 13-Lenth Sequence
PER performance
TGnD Channel
UMi NLoS Channel