## Slide 1: Duty cycle mode STA’s PS follow-up
Date: 2017-09-10
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
During the previous September meeting, we agreed that
  AP indicates a BSS parameter update by incrementing a counter in the wake-up frame[1]
  By a counter value, a STA can decide whether or not the STA updates the BSS parameter
    E.g.,) If the STA receives the same counter as its stored counter, the STA doesn’t have to attempt the BSS parameter update
AP can send a broadcast wake-up frame before sending broadcast data [2] as well as for indicating BSS parameter update [3]
In this contribution, we proposes for an AP to send a broadcast wake-up frame before sending a broadcast data and the corresponding power saving procedures

## Slide 3: Proposal
AP has to inform STAs whether the broadcast WUR frame is sent for BSS parameter update or broadcast data
AP includes Broadcast Data (BD) presence field in a WUR frame
  BD presence indicates the presence of broadcast data (it’s same as Bit 0 (AID0) of Bitmap Control field of TIM element in legacy WLAN [4])
If a STA receives a broadcast WUR frame including BD presence set to 1, the STA may attempt to receive the broadcast data
  Ex1) The STA may enter the doze state until DTIM Tx time
  Ex2) The STA may re-enter the WUR mode right after receiving the broadcast data
AP may send the same B-WUR frame several times for more reliability
  In this case, AP includes sequence number for broadcast data in B-WUR frame for STAs to avoid unnecessary wake-up for duplicate B-WUR frame receptions
  STA can ignore the B-WUR frame with the same sequence number as the previous

## Slide 4: Conclusion
AP can send a broadcast wake-up frame before sending broadcast data as well as for indicating BSS parameter update
AP includes the information for indicating broadcast data presence (e.g., Broadcast Data (BD) presence field) in a broadcast WUR frame
  In this case STA can return to WUR mode right after receiving broadcast data
AP may includes sequence number in B-WUR frame for STAs to avoid unnecessary wake-up for duplicate B-WUR frames

## Slide 5: Reference
[1] 17/1368r2, BSS parameters update notification
[2] 17/124r4, WUR MAC and Wakeup Frame
[3] 17/978r2, Power saving operation for WUR STAs in duty cycle mode
[4] 802.11-2016

## Slide 6: Straw Poll 1
Do you agree the following?
  A broadcast wake-up frame includes the information for indicating the group addressed frame transmission through PCR

## Slide 7: Straw Poll 2
Do you agree the following?
  If a STA receives a broadcast wake-up frame indicating a group addressed frame TX through the PCR, the STA may attempt to receive a group addressed frame through PCR
  After the STA receives the group addressed frame in the PCR, the STA may enter the Doze state without sending any WUR mode signaling frame to AP through PCR