## Slide 1: Capability on Doppler Mode
Date: 2017-09-12
Authors:

## Slide 2: Introduction
Midamble was proposed in [1-4] to address the Doppler scenario for 11ax.
This presentation discusses several issues with the proposed design and propose the suggested modifications:
  Midamble duration and Rx processing time
  Midamble Rx Max NSTS

## Slide 3: Capability on HE-LTF Type – Processing Time
4X data symbol sometimes needs another 4X data symbol duration processing time after the reception, e.g., 4X Data-9 in the figure below.
When Midamble duration is comparably short, e.g., Two 1X HE-LTF with 0.8us GI (8us in total), there may not be enough time for FFT, channel estimation and pre-processing before the processing of 4X Data-10. Further averaging the CHEST of the midabmle and previous CHEST may take more time.
Hence, the midamble duration should be longer than some threshold so that the Rx has enough time to proceed the channel estimation and pre-processing before the decoding of the next symbol after the midamble:

## Slide 4: Capability on HE-LTF Type - FFT Size Switch
For simplicity, another option is to restrict 1X/2X HE-LTF type, for example, forbid using 1X/2X HE-LTF for Doppler mode. Becuz 4X HE-LTF will ensure at least 13.6us duration for midamble field.
Whilst we do see gains for using short HE-LTF with the simulation results in [2][3], hence here we propose to have a capability bit for 1X/2X HE-LTF in Doppler mode.
Another factor we need to consider is FFT size switch between midamble and data when midamble has 1X/2X HE-LTF. The Rx needs to switch between large FFT size (4X) and small FFT size (1X/2X), which leads to complexity for the Rx.
  May still use 4X FFT size for 1X/2X HE-LTF, whilst it depends on implementation and will leads to more delay and leads to the issues discussed in slide 3.
Considering both reasons, here we propose to have a capability bit for 1X/2X HE-LTF in Doppler mode:
  B68 of HE PHY Capabilities Information field changes from Reserved to Midamble with 2x and 1x HE-LTF Support:
    When Doppler Rx subfield is set to 1, indicates support for receiving Midambles with 2x HE-LTF, and 1x HE-LTF

## Slide 5: Capability on Midamble Rx Max NSTS
Another factor that affects the Rx’s complexity handling the midamble is the number of space-time streams (Nsts). Larger Nsts needs either more processing time or more buffer/hardware.
Moreover, from the STA’s type or application point of view, some Rx may prefer a more robust transmission with low Nsts (mobile phone, IoT devices), whilst some Rx may need a higher data rate with high Nsts (backhaul, TV etc.).
Hence it is better to have a capability field so that when Doppler Rx field is set to 1, the STA can indicate the maximum number of space-time streams supported for reception when midamble is used in the Data field.

## Slide 6: SP1
Do you support to have a capability bit for 1X/2X HE-LTF in Doppler mode:
  B68 of HE PHY Capabilities Information field changes from Reserved to Midamble with 2x and 1x HE-LTF Support:
    When Doppler Rx subfield is set to 1, indicates support for receiving Midambles with 2x HE-LTF, and 1x HE-LTF (if the “HE SU PPDU And HE ER SU PPDU With 1x HE-LTF And 0.8 us GI” subfield is set to 1)
  Y
  N
  Abs

## Slide 7: SP2
Do you support to have a capability bit for Midamble Rx Max NSTS:
  B15-16 of HE PHY Capabilities Information field changes from Reserved to Midamble Rx Max NSTS:
    When Doppler Rx field is set to 1, indicates the maximum number of space-time streams supported for reception when midamble is used in the Data field.
    Set to 0 for 1 space-time stream
    Set to 1 for 2 space-time streams
    Set to 2 for 3 space-time streams
    Set to 3 for 4 space-time streams
  Y
  N
  Abs

## Slide 8: References
[1] 11-17-0995-00-00ax-Doppler-comment-resolutions
[2] 11-17-0734-01-00ax-doppler-discussions
[3] 11-17-0773-02-00ax-thoughts-on-doppler-design-in-802-11ax
[4] 11-17-1021-00-00ax-usage-of-doppler-bit-in-11ax