## Slide 1: Considerations for WUR Response
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
According to a current specification framework for 11ba[1], a mechanism to wake up multiple WUR mode STAs is supported
  R.4.6.4.A: IEEE 802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs (e.g., multi-user wake-up frame)
  R.4.6.3.B: A STA should send a response frame to the AP using primary connectivity radio after receiving a unicast wake-up packet.
  R.4.6.1.B: The AP can send a Trigger Frame in 11ax to solicit response frames from one or more STAs after sending a wake-up packet to the STA(s).
However, SFD still does not consider any in-depth method to wake up multiple WUR STAs

## Slide 3: Problem Definition
If numerous STAs are requested to wake up at the same time, collision can occur due to the simultaneous WUR response frames from the STAs and it results severe power consumption
  Even though we have UL MU transmission scheme in 11ax, collision by response frame still can be problem
Multicast WUF
AP
WUR
PCR
STA1:
WUR
STA2:
WUR
STA3:
WUR
STA4:
: Contention Window
: Random Backoff
Collision
Collision
PCR
PCR
PCR
Hence, WUR response frames should be distributed to avoid channel collision

## Slide 4: Possible Solution
Option 1: AC differentiation for WUR response
  AP adjusts access category for WUR responses according to a certain condition
  It can be adopted by explicit signaling or implicit signaling
    For explicit signaling, common AC indicator is included in WUR frame in order to adjust corresponding STAs’ WUR response at that time
    Alternatively, implicit signaling by means of Type of WUR frame is possible if there is pre-defined parameter
  Explicit signaling can fine-tune AC according to, for example, the number of STAs but it has much overhead
  Implicit signaling has no overhead but it cannot delicately adjust ACs

## Slide 5: Possible Solution
Option 1: AC differentiation for WUR response
  Explicit method
WUF
AP
WUR
Main radio
STA1:
WUR
Main radio
STA2:
: Contention Window
: Random Backoff
WUF
AP
WUR
Main radio
STA1:
WUR
Main radio
STA2:
: Contention Window
: Random Backoff
WUR
Main radio
STA3:
WUR
Main radio
STA4:
WUR response using Common AC Indicator (i.e., AC_VO)
Contention win
PS-Poll
DATA
ACK
Contention win
DATA
ACK
WUR response using Common AC Indicator (i.e., AC_BE)
PS-Poll
Common AC Indicator
Frame Body
MAC Header
FCS

## Slide 6: Possible Solution
Option 1: AC differentiation for WUR response
  Implicit method
WUF
AP
WUR
Main radio
STA1:
Indicate that this WUF is for Unicast
: Contention Window
: Random Backoff
WUF
AP
WUR
Main radio
STA1:
WUR
Main radio
STA2:
Indicate that this WUF is for Multi-Broadcast
: Contention Window
: Random Backoff
WUR
Main radio
STA3:
WUR
Main radio
STA4:
DATA
ACK
Take high-priority AC or No waiting
PS-Poll
DATA
ACK
Take low-priority AC
PS-Poll
Frame Body
MAC Header
FCS
Address
= (Partial) BSSID
Frame Control
TD Control
Type

## Slide 7: Possible Solution
Option 2: Wakeup delay method
  An WUR STA waits for a randomly chosen period in WUR mode before waking up PCR
    If an WUR STA gets Additional Wakeup Delay Window value in multicast wake-up packet, it will wait for a randomly chosen moment within the value before waking up
  It can achieve more power efficiency compared to option 1 because differentiation of WUR response is conducted in WUR mode

## Slide 8: Possible Solution
Option 2: Wakeup delay method
WUF
AP
WUR
Main radio
STA1:
WUR
Main radio
STA2:
: Contention Window
: Random Backoff
WUF
AP
WUR
Main radio
STA1:
WUR
Main radio
STA2:
: Contention Window
: Random Backoff
WUR
Main radio
STA3:
WUR
Main radio
STA4:
Wakeup PCR
DATA
ACK
DATA
ACK
PS-Poll
: Wakeup Delay
: Wakeup Delay
PS-Poll
Wakeup PCR
Shorter Additional Wakeup Delay Window
Longer Additional Wakeup Delay Window
Additional Wakeup Delay Window
Frame Body
MAC Header
FCS

## Slide 9: Summary
We have discussed in-depth methods to wake up multiple WUR STAs for avoiding collisions and achieving power efficiency
It is convenient that AC differentiation method just reuse existing 802.11 parameters
  However, it can causes power consumption for additional backoff compared to wake up delay method
Wake up delay method needs a new parameter but it can effectively distribute WUR responses and achieve more power efficiency compared to AC differentiation method

## Slide 10: Straw Poll
Do you agree to add the text in SFD as follows?
  IEEE 802.11ba spec shall support a mechanism to avoid collisions caused by WUR response frames sent by multiple STAs.

## Slide 11: References
[1] 11-17/0575r3, “Spec framework,” Po-Kai Huang