## Slide 1: BSS parameters update notification
Date: 2017-09-10
Authors:

## Slide 2: Introduction
Primary functions of a WUR Beacon is proposed in [1-5] are
  Advertize the presence of AP
  Synchronize between AP and the STA when the STA’s primary connectivity radio (PCR) is off
  Provide the WUR STA the minimal necessary set of information
  Here we consider PCR’s BSS parameters update info as one minimal necessary set of information
  Some battery powered STA’s PCR may sleep for several days or months with the help of wake up receiver
  However, BSS Parameters may change during the sleep time of the STA’s PCR, such as channel and EDCA parameters

## Slide 3: Motivation
It can help the STA’s PCR make a correct transmission to provide BSS parameters update info
However, it is impossible to provide each changed BSS parameter through the WUR beacon
  Size of the WUR Beacon needs to be controlled due to low PHY rate (e.g., 250Kbps)
  Each BSS parameter occupies multiple bytes, such as 20 bytes EDCA Parameter Set element, requiring 640 us for transmission

## Slide 4: BSS parameters update notification
Generally, the STA knows all the necessary Info after association
When there are changes in some BSS parameters which can not be conveyed by using the WUR beacons due to size limitation, we propose to use a simple indication to alert the STA in WUR mode get on synch with new Info
  Propose to use a change number (CN) indication (4 or 8 bits) carried in WUP and WUR beacon
  After being informed the changed BSS parameters, the STA can either wake up to decode the 802.11 beacon at TBTT
  Or retrieve updated information by using probe request
  Some similar designs were provided for 11ah devices and TIM STAs
  Change sequence field in short beacon frame was proposed to provide 11ah STAs the change of system info
  Check beacon field in broadcast TIM frame was proposed to provide TIM STAs the critical updates on BSS parameters

## Slide 5: BSS parameters update notification
  Initialize CN to 0 at the beginning, and increase by one when a critical update occurs to any PCR’s BSS parameters
  a) Inclusion of Channel Switch announce element
  b)Inclusion of Extended Channel Switch announce element
  b) Modification of the EDCA parameters
  c) Inclusion of a Quiet element
  e) Modification of the HT Operation element
  f) Inclusion of an Operating Mode Notification element
  g) Inclusion of a Quiet Channel element
  h) Modification of the VHT Operation element …
  When the STA receives a change number that is different from the local stored change number, it may
  queue for transmission by sending a Probe Request frame when it is awake and wait for Probe Response frame which contains updated BSS parameters or receive the next beacon frame
  and update the local stored change number
Beacon
(CN=3)
Probe request
Probe response
Local CN=2
AP
STA
Ack
Ack

## Slide 6: Reference
[1] 11-16-1445-00 Overall MAC Procedure for WUR
[2] 11-16-1504-00 Discussion of WUR Packets Design
[3] 11-16-1217-00 WUR-based Broadcast Reference Signal
[4] 11-16-1501-00 AP Discovery using WUR
[5] 11-17-0343-03 ba WUR Beacon

## Slide 7: SP1
  Do you agree that AP indicates a BSS parameter update by incrementing a counter in the wake up packet?
Y
N
A

## Slide 8: Motion
Move the following to add to the TGba SFD:
  AP indicates a BSS parameter update by incrementing a counter in the Wake Up frame
  Moved by : Ming Gan
  Seconded by: Yunsong Yang
  Results: passed by unanimous consent