## Slide 1: Power save state transition
Date: 2017-09-10
Authors:

## Slide 2: Introduction
The power save state transition between PCR state and WUR state is first proposed in [1]
A WUR state signal is proposed to enter WUR state from PCR state [1-2]
  One form of the WUR state signaling is WUR request frame proposed in [2]
Note: here the relationship between PCR state and WUR state in WUR mode is like the active state and doze state in power save mode

## Slide 3: WUR state signaling
The STA may request to enter WUR state for low power operation by using the WUR state signaling in WUR mode
After receiving the Ack to the WUR state signaling, the STA enters the WUR state
  Turn on the WURx and turn off main radio
In this contribution, we are discussing about how to go back to PCR state for the STA and its behavior
AP
STA
Inform the AP that the STA is entering the WUR state
Ack
WUR state Signaling
WURx on
PCR off
WURx
MR
PCRon
WURx off

## Slide 4: PCR state signaling
Several factors may trigger the STA in the WUR state to go back to PCR state
  A successful wake up packet reception
  The WUR beacon is not detected for a predefined time, e.g., beyond the coverage of AP
  Self wake up due to uplink traffic
  Note: PCR state is defined as PCR in active state no matter whether the WURx is on or off
  We propose not to turn off WURx immediately after a successful wake up packet reception
  The wake up packet transmitter (e.g., AP) is not informed before receiving the wake up response frame if the STA turns off the WURx immediately after a successful wake up packet reception
  It is hard for AP to make a correct transmission, wake up packet or .11 packet?
  From another angle, keeping WURx on for a while does not waste much energy

## Slide 5: Issues discussion (1/2)
  Some issues will happen if the STA turns off the WURx immediately after a successful wake up packet (WUP) reception
  Other WUPs may be sent during the WUR time out period before receiving the wake up response frame from the STA
  May be different from the previous one, containing the new info, such TSF, BSS parameters update notification and is transmitted
  Without info contained in the missed WUP, the STA may make wrong transmission by its PCR
Unicast WUP to STA1
broadcast WUP or unicast WUP to STA1
AP
Timeout Interval
WURx off
PCR on
WURx
MR
PCR off
WURx on
transition
STA
new info, such as TSF, BSS parameters update notification

## Slide 6: Issues discussion (2/2)
  Some issues will happen if the STA turns off the WURx immediately after a successful wake up packet (WUP) reception
  Other WUPs may be sent during the WUR time out period before receiving the wake up response frame from the STA
  10 ms transition time is too long, anything may happen within this period
  May be used to doze the STA’s PCR or negotiate another wake up time due to traffic control or other high priority traffic needs to be handled first
  without info contained in the missed WUP, the STA may not execute the AP’s command correctly
Unicast WUP to STA1
Unicast WUP to STA1
(change wake up time or doze STA’s main radio)
AP
Timeout Interval
WURx off
PCR on
WURx
MR
PCR off
WURx on
transition
STA
Due to traffic control or other high priority traffic

## Slide 7: Turn off WURx
  A successful frame exchange between AP and the STA is proposed as the condition to turn off WURx after entering PCR state
  E.g., An acknowledgement or data to the wake up response frame, e.g., Ps-poll, is received
  Adopt the same philosophy of the power save mode change condition
  To change power management modes a STA shall inform the AP by completing a successful frame exchange
The acknowledgement is required before turning off WURx when the received wake up packet solicits wake up response frame
  Follow the same design philosophy of WUR state signaling
  Turning off WURx at this stage does benefit power save
AP
STA
Ack
WUP
WURx on
transition
PCR on
PCR off
WURx off
WURx
MR
wake up response frame

## Slide 8: Reference
[1] 11-16-1445-01 Overall MAC Procedure for WUR
[2] 11-17-0071-00 High level MAC concept for WUR

## Slide 9: SP 1
Do you agree that the STA may turn off the WURx after a successful frame exchange with AP, which informs the AP that the STA is the awake state, through its PCR in WUR mode