## Slide 1: CP Replay Attack Protection
Date: 2017-09-11
Authors:

## Slide 2: CP Replay Attack Protection
Components:
Encryption of LFT base sequence
  Consideration to PAPR of the time domain signal may be required
Modify cyclic prefix to remove repetition in training signal
  Replace CP with zeroes, or
  Replace CP with encrypted training signal
Conveying of encryption key for LTF and CP (if encrypted)
  Convey in field after the LTF, e.g. in packet extension
  Convey prior to LTF
    Encrypted, or
    Non-encrypted

## Slide 3
Modification of the CP

## Slide 4: Nulling of CP
Null CP
Channel estimate will become a little distorted
First tap appears largely to remain in the same position
  At least for cases with reasonably high SNR and even more so for cases with a strong LOS path
If desired, channel estimation could account for nulled CP
  E.g. used receiver with larger FFT size exploiting nulled CPs surrounding the core LTF symbol as in [1].

## Slide 5: Performance with Nulled CP

## Slide 6: Performance with Nulled CP

## Slide 7: Performance with Nulled CP
Hmm…. Why do we get better performance with nulled CP? Statistical anomaly?

## Slide 8: Performance with Nulled CP

## Slide 9: Pseudo Random CP
Again:
Channel estimate will become a little distorted
First tap appears largely to remain in the same position
  At least for cases with reasonably high SNR and even more so for cases with a strong LOS path
Channel estimation could make use of modified CP signal

## Slide 10: Performance with Randomized CP

## Slide 11: Performance with Randomized CP
Why do we get better performance with randomized CP? Statistical anomaly? Only 100 packets simulated here.

## Slide 12: Performance with Randomized CP
With 300 packets simulated the regular CP is better than the randomized CP.

## Slide 13: Performance with Randomized CP

## Slide 14: Performance with Randomized CP
Why do we get better performance with randomized CP? Statistical anomaly? Only 100 packets simulated here.

## Slide 15
Conveying of encryption key

## Slide 16: Conveying of Key in Packet Extension
Modulate packet extension as legacy portion of packet
Convey LTF encoding key in packet extension
  No need to encrypt key as the packet extension come after the encoded LTF

## Slide 17
CP Replay Attack Protection for 802.11az NDP based Ranging

## Slide 18: CP Replay Attack Protection for 802.11az NDP based Ranging
No data in NDP packet => Channel estimate not needed for demodulation

## Slide 19
CP Replay Attack Protection for 802.11REVmc evolution

## Slide 20: CP Replay Attack Protection for 802.11REVmc evolution
For HT/VHT ranging
  Require ranging measurements to be made on HT/VHT-LTF(s)
  Encrypt HT/VHT-LTF(s)
  Modify CP (nulled or randomized)
  Restrict MCS level in FTM, and implicitly in the ACK so that the payload can be decoded despite the modified CP
  LTF key conveying:
    Add packet extension and convey LTF encryption key in it, or
    Convey LTF key prior to ranging measurement packets

## Slide 21
Need for PHY Security

## Slide 22: Need for PHY Security
PHY security is primarily needed to protect against spoofing attacks
Spoofing location is considerably more difficult than spoofing proximity
  Spoofing location requires spoofing the ranging measurements from multiple (>=3) anchor stations
  Location measurements also usually, for reliability reasons, have a lot of redundancy build in into its process => Makes it yet harder to spoof
  Proximity measurements may only require spoofing of a single ranging measurement => Much more sensitive to spoofing

## Slide 23: Selective PHY Security
Modifying the CP may have effect on the ranging performance
At high SNR and low delay spread the effects is likely small
Spoofing security only needed in a limited number of use cases
Complete, loss-less, complication free and general protection against CP replay attacks may be difficult to realize
Enable selective security against CP replay attacks to be turned on for vulnerable use cases.

## Slide 24: Proposed Solutions
Encrypt LTF
Add the option to null or encrypt the CP of LTFs used for ranging to protect against CP replay attacks.
  Optionally use receiver that exploits modified CP, or use regular receiver.
    E.g. use receiver with larger FFT size exploiting nulled CPs surrounding the core LTF symbol as in [1].
    However, losses with regular receiver does not seem to be prohibiting.
Convey encryption key prior to ranging or non-encrypted in packet extension
For 802.11REVmc FTM evolution ((V)HT):
  Require that ranging measurements are performed on the (V)HT-LTF
  Restrict MCS level to ensure decoding of payload

## Slide 25: References
[1] “Zero padded waveform”, Mingguang Xu, John Dogan, SK Yong, Qi Wang, Kyle Brogle and AJ Ringer IEEE 802.11-17/1378r2.

## Slide 26
Thank You!