## Slide 1: PHY Security FRD and SRD Text
Date: 2017-09-06
Authors:

## Slide 2: FRD (424r6) Recap
2.1.6 Security and Privacy
TGaz R35 The 11az positioning protocol shall have at least one secured mode that meets all of the following security requirements in the associated state:[Ref-11]
Authentication - Mutual authentication of initiator and responder.
Encryption Algorithm - The cryptographic cipher combined with various methods for encrypting the message* used in 11az-positing protocol.
Key Management - Create, distribute and maintain the keys.
Message Integrity - Ensures that the encrypted message* has not been tampered with.
(* Message refers to frame and/or field(s) within the frame.)
TGaz R36 The 11az positioning protocol shall have at least one secured mode that meets all of the following security requirements in the unassociated state:[Ref-11]
Authentication - Mutual authentication of initiator and responder (provided there is a prior security context established).
Encryption Algorithm - The cryptographic cipher combined with various methods for encrypting the message* used in 11az-positing protocol.
Key Management - Create, distribute and maintain the keys.
Message Integrity - Ensures that the encrypted message* has not been tampered with.
(* Message refers to frame and/or field(s) within the frame.)

## Slide 3: FRD (424r6) Recap – Cont’d
2.1.6 Security and Privacy
TGaz R37 The 11az protocol shall have at least one secured mode that protects against adversaries with capabilities as specified by R1 to R4 below and with the following response time.[Ref-11]
Type A Adversary is assumed to have response time to standard-specified OTA events or scenario dependent fields of 1 msec or longer.
Type B Adversary is assumed to have response time to known OTA events or known pre-defined fields of 1usec or longer (up to 1msec).
Note: the STA capabilities is TBD (for both types of adversaries).
An adversary may have at least one or more of the following capabilities and limitations:
[R1] An adversary that uses commercial NIC/Sniffer;
[R2] At most, the adversary may deploy/use two non-co-located Tx and Rx chains;
[R3] The adversary shall be TOA and TOD capable on all received/transmitted frames;
[R4] The adversary shall be able to compose and transmit any 802.11 packet or part of it.

## Slide 4: Proposed FRD Text
  TGaz R37: The 11az protocol shall have at least one secured mode that protects against adversaries with capabilities as specified by R1 to R4 below and with the following response time.[Ref-11]
    Type A Adversary (targeting VHT/HE/DMG/EDMG operation) is assumed to have response time to standard-specified OTA events or scenario dependent fields of 1 msec or longer.
    VHT/HE Type B Adversary is assumed to have response time to known OTA events or known pre-defined fields of 1usec or longer (up to 1msec).
    DMG/EDMG Type B Adversary is assumed to have response time to known OTA events or known pre-defined fields of 10nsec or longer (up to 1msec).

## Slide 5: SFD (0462r5) Recap
6. Security [May 2017]
(1) The security setup to be negotiated in a separate optional step prior to the 802.11az protocol parameter negotiation
  Note that in lieu of security negotiation, keys derived using an out-of-band mechanism may be used to secure the exchange between the initiator and the responder [May 2017]
(2) The REVmc, HEz, and VHTz FTM modes, the fields over which range measurements are performed shall be protected against a Type B adversary attack [May 2017]

## Slide 6: Proposed SFD Text
(2)The REVmc, HEz and VHTz FTM modes, the fields over which range measurements are performed shall be protected against a VHT/HE Type B adversary attack (TGaz R37)
(3)The DMGz and EDMGz FTM modes, the fields over which range measurements are performed shall be protected against a DMG/EDMG Type B adversary attack (TGaz R37)
(4) In the PHY Security mode (VHTz, HEz, DMGz, EDMGz), the field used for channel/ToA measurement shall not include any form of repetition in time domain or structure that is predictable

## Slide 7: Straw Poll 1
Do you support to add the proposed text as shown in slide 4 to the FRD?
Result: Y: 14 N: 1 A: 4
SK Yong and Mingguang Xu, Apple

## Slide 8: Straw Poll 2
Do you support to add the proposed text as shown in slide 6 to the SFD?
Result: Y: 11 N: 1 A:7

## Slide 9: Motion
Move to incorporate text as shown in slide 4 to the FRD
Result: Y: N: A:

## Slide 10: Motion
Move to incorporate text as shown in slide 6 to the SFD
Result: Y: N: A: