## Slide 1: Zero-Padded Waveform for Secure Channel Estimation
Date: 2017-09-11
Authors:

## Slide 2
Abstract (1)
Security is one of the most important features in 11az.
  To achieve secure ranging, the waveform used for channel estimation needs to be protected against attackers.
FRD [1] describes Type A and Type B adversaries that are characterized according to attacker’s response time.
  Adversary goal: to spoof the range of STA.
  Type A: 1 msec response time.
  Type B: 1 usec response time.
  A few security threat models are listed in [2]-[3].

## Slide 3
Abstract (2)
In CP-replay threat model [3], attacker can exploit all waveforms with repetition or any predictable structure to perform an attack.
  E.g., cyclic prefix (CP), Golay sequence, etc.
  Can be realized by a Type B adversary.
We propose a framework of zero-padded waveforms for protecting against CP-replay threat.

## Slide 4
Zero-Padded Waveform (1)
Requirements for ranging waveform.
  To protect against CP-replay attack:
    The waveform used for channel estimation should not contain any form of repetition and structure that is predictable (e.g, CP, Golay sequences).
  For the purpose of performance and implementation:
    Channel estimation can be implemented in an efficient way.
    Ranging performance difference as compared to existing waveform of CP-OFDM should be acceptably small.
A proposal: zero-padded waveform.
  Guard interval should be present and padded with zero.
  Choose FFT/IFFT analysis window at Tx/Rx side to enable distortionless channel estimation.
    Guard interval after each symbol may be needed.

## Slide 5
Zero-padded waveform is composed of three parts: zero prefix, core symbol, and zero postfix.
  Zero prefix
    Guard internal (GI) needs to be inserted to remove inter-symbol interference.
    Zero signal needs to be transmitted in GI.
  Core symbol
    Core symbol is composed by the training sequence, which is random.
  Zero postfix (when necessary)
    Zero signal is appended to each symbol if waveform is followed by non-zero signal.
    Zero postfix enables transform-domain channel estimation without any distortion if FFT/IFFT analysis window is chosen correctly.
Zero-Padded Waveform (2)

## Slide 6
Example 2: Waveform for three symbols.
  The prefix of next symbol can be viewed as the postfix of the current symbol.
  The postfix for each symbol is omitted except the last one.
Example 1: Waveform for one symbol.
  Zero postfix needs to be appended if core symbol to be followed by non-zero signal.
Zero-Padded Waveform (3)

## Slide 7: Zero-Padded Waveform (4)
“Overlap-add” processing:
Subject to replay attack.
  Can be viewed as the dual of CP-replay attack.

## Slide 8
FFT/IFFT analysis window:
  When the received signal corresponding to zero postfix is included in the FFT/IFFT analysis window
  Linear convolution with multi-path channel is turned into cyclic convolution, and
  Transform-domain channel estimation can be applied without any distortion.
    Pilot sequences (in frequency) is the frequency-domain response of core symbol padded with zeros.
    For better performance can use advanced channel estimation methods.
FFT/IFFT size:
  Can be the same as the sum of the lengths of core symbol and zero postfix.
  Or can be larger by adding more zeros onto received signals for efficient FFT/IFFT operation (e.g., power of 2, or split-radix FFT).
Zero-Padded Waveform (5)

## Slide 9
Training sequence loaded in core symbol.
  Needs to be random and different across different symbols.
  The resulting constellation points can be loaded in frequency domain or time domain.
    Frequency domain: OFDM like.
    Time domain: Similar to single-carrier PHY in 11ad/ay.
  For better performance on channel estimation, may consider shifted modulation, e.g., pi/2-BPSK or pi/4-QPSK.
    Potentially less dips on the magnitude of pilot sequences in frequency between subcarriers.
Zero-Padded Waveform (6)

## Slide 10
Zero-padded waveform requires to ramp up/down signals quickly.
  Time needed to ramp up/down signal?
  Performance impact for non-ideal signal ramping up/down.
  Other RF impairments?
PAPR of core symbol.
Beyond transform-domain channel estimation.
  Efficient methods of channel estimation to deal with non-ideal effective pilot sequences (in freq), i.e., magnitudes of pilot sequences are not flat.
Discussion

## Slide 11
Summary
Zero-padded waveforms can protect against CP-replay threat with proper signal processing at both Tx/Rx sides.
  Distortionless and efficient channel estimation can be achieved if FFT/IFFT analysis window and sizes are delicately chosen.
More investigation on the details about length of core symbol, FFT/IFFT size, training sequences, etc.
More to come for advanced channel estimation methods.
  High resolution.
  MMSE based on conjugate gradient methods.
  …

## Slide 12
References
[1] IEEE 802.11-16/424R5, 11az FRD.
[2] IEEE 802.11-17/0120r2: “Intel secured location threat model”, B. Abramovsky, O. Bar-Shalom, and C. Ghosh, January 2017.
[3] IEEE 802.11-17/1122r0: “CP-replay threat model for 11az”, M. Xu, J. Dogan, K. Brogle, A.J. Ringer, SK Yong, and Q. Wang, July 2017.