## Slide 1: Examining 802.11ba Usage Models for Mainstream Devices
Date: 2017-09-12
Sept 2017
Apple
Name | Affiliations | Address | Phone | email
Guoqing li | Apple |  |  | Guoqing_li@apple.com
Oren Shani |  |  |  | 
Chris Hartman |  |  |  | 
Jarkko Kneckt |  |  |  | 
Minyoung Park | Samsung |  |  | 
Bin Tian | Qualcomm |  |  | 
Alfred Asterjadhi |  |  |  | 
Hongyuan Zhang | Marvell |  |  | 
Liwen Chu |  |  |  | 
Po-Kai Huang | Intel |  |  | 
Shahrnaz Azizi |  |  |  | 
Robert Stacey |  |  |  | 
Ross Yu | Huawei |  |  | 
Vinko Erceg | Broadcom |  |  | 
Bo Sun | ZTE |  |  | 

## Slide 2
Name | Affiliations | Address | Phone | email
James Yee | MediaTek |  |  | 
Chaochun Wang |  |  |  | 
James Wang |  |  |  | 

## Slide 3: Introduction
Most of the use cases described in 802.11ba Usage model document [1] are targeting IoT market, and we think that current design in 802.11ba will benefit such IoT devices
However, we believe that, to make 802.11ba a truly successful standard, it needs to bring significant benefit for mainstream devices to adopt it as well
  Note that 802.11ba is a new radio for main stream devices. Integrating such a new radio takes huge amount of effort on HW integration, SW integration, new co-existence management and connection management, intensive HW/SW testing etc.
  Therefore, the benefits brought by 802.11ba have to be significant enough in order to be adopted by mainstream devices
This contribution examines the benefits and issues of using 802.11ba on main stream devices such as smart phones, and proposes new use cases that can be (almost) readily enabled by 802.11ba which can bring more significant benefits for mainstream devices

## Slide 4: Introduction
802.11ba is targeting at saving Wi-Fi power consumption during the no-real-traffic period without sacrificing the delay performance when real traffic arrives
The power saving mainly comes from two factors:
  Beacon reception during Idle period
  Wi-Fi main radio may be put to deep sleep mode or turned off completely
Sept 2017
Slide 4
Main radio
Main radio
11ba
Beacon
Beacon
Sleep
Sleep
Case 1: without 11ba
Case 2: with11ba
Sleep or off
802.11ba power

## Slide 5: 802.11ba for Main Stream Devices
First of all, for main stream devices, the main radio cannot be turned off completely due to many factors such as
  Maintain association status, maintain encryption/authentication status
  Maintain internal configuration parameters
  Background activities and background interactions with the host for various applications
In order to maintain the various parameters/status on main stream devices, the main radio has to keep certain memory, clocks and processing on, which consumes power, and we call it retention power
The more sophisticated the device is, the more memory is needed, and the higher the retention power is consumed
For main stream devices, the retention power can be higher than 802.11ba radio, and such power cannot be eliminated even if 802.11ba is used
As a consequence, the power saving benefits for mainstream devices mainly come from Beacon reception elimination

## Slide 6: 802.11ba for Main Stream Devices (cont.)
Secondly, mainstream devices have much higher battery capacity than IoT devices, and thus the percentage of power saving brought by 802.11ba for mainstream devices would be much smaller than for IoT devices
For example, using the power parameters in 802.11ax simulation scenario document [2], assume 3m Beacon reception time, 900ms Beacon reception interval, 3000mAh battery [3], 3.6V, assume WUR consumes 110uW, assume Wi-Fi spent 10 hours Idle in a day, then the power saving benefit is
  Legacy operation: average power = (3/900*Rx power+897/900*Sleep power)=0.45uW
  Total battery saving=(0.45mW-0.1mW)*10hours/(3000mAh*3.6V)=0.03%
In legacy mode, the average/max latency is 450/900ms. This latency may be too long for some IoT applications, but is considered acceptable for most applications on mainstream devices
Note that a different implementation architecture may result in different power saving percentage. However, due to the large battery and the loose latency requirements on mainstream devices, we do not expect very significant power saving benefit for mainstream devices
  Note that the gain for IoT devices can be quite significant due to much smaller battery capacity and more stringent latency requirement

## Slide 7: 802.11ba for Main Stream Devices (cont.)
However, as we are defining the new standard targeting at power saving, we would like to see that this technology can bring more power saving benefits for mainstream devices without introducing complex mechanism
In fact, current 802.11ba design is (almost) ready to save more power

## Slide 8: What Other Power Can be Saved by 802.11ba?
To save more power, we have to look for power reduction from activities other than Beacon reception. An example is below.
[1] pointed out the AP re-discovery issue in Usage Model 3, i.e., STA moves out of the range of current AP, and thus needs to discover other APs
Currently, discovering nearby APs on main radio requires the STA to do passive or active scan which consumes quite some power
In fact, there are many background scans on mainstream devices, which consumes much higher power than the Beacon reception power itself
Since WUR is an ultra-low power receiver, offloading some of the passive background scans to WUR can significantly save even more power
In other words, enabling WUR to scan for unassociated APs not only saves power on passive scanning, but also addresses the AP re-discovery problem introduced by WUR itself

## Slide 9: Usage Model x: Smart Scanning
Use case 1: Ultra-low power location scan
Mobile devices sometimes scan through multiple channels for nearby APs, and use the measured Wi-Fi signal strength for improved location services. Scanning on main radio consumes higher power than WUR radio. In addition, scanning on main radio has the risk of conflicting with regular data exchange.
In WUR-facilitated location scan, the mobile device scans through the channels using the WUR receiver, and uses the signal strength measured from WUR packets received from adjacent APs to provide additional information to the location services on the mobile device. In other words, some of the location scan on main radio can be offloaded to WUR radio.
Because WUR consumes much less power than main radio, WUR facilitated location scan provides an ultra-low power location scan mechanism.
Use case 2: Ultra low power roam scan
Mobile devices sometime scan for roaming purposes. These roam scan sometimes is triggered when link quality degrades. These roam scan takes time because the scan is typically done on multiple channels, and on each channel the device either conducts active scan during which it sends a probe request and typically stays awake until it receives a probe response, or passive scan during which it dwells on each channel for at least a Beacon interval to receive a Beacon. As a consequence, scanning through multiple channels introduces roaming latency and consumes power. Sometimes, it runs into conflict with regular data exchange.
In WUR-facilitated roam scan, the mobile device passively scans through multiple channels using WUR, and collects basic information about nearby APs. The collected info can be used to facilitate the devices’ roaming decisions.
Because WUR consumes much less power than main radio, WUR-facilitated roam scan provides an ultra-low power roam scan. In addition, due to the low power operation, WUR scan can be performed quite frequently in the background, and thus roaming information can be readily available whenever needed, i.e., it reduces roaming latency.
Sept 2017

## Slide 10: Two Basic Requirements
802.11ba should define frame format (or one type of frame format) that allows unassociated STAs to interpret the AP’s identity
  The transmission frequency of such frames do not need to be frequent, 10s of seconds should be enough, since Wi-Fi devices have low mobility
For frames that can be decoded by unassociated STAs, the AP’s identifier should have very low collision probability
When these two basic requirements are met, WUR is ready to be used to solve the AP re-discovery problem while saving more power on main radio passive scan

## Slide 11: Strawpoll
Do you agree to include page 8 into 802.11ba usage model document?
  Yes
  No
  Abs

## Slide 12: Strawpoll
Do you agree to define a type of WUR frame that can be decoded by unassociated STAs?
  Yes
  No
  Abs

## Slide 13: Reference
[1] 11-17-0029-07-00ba-wur-usage-model-document
[2] 11-14-0980-10-00ax-simulation-scenarios
[3] http://www.pocket-lint.com/news/133069-15-smartphones-with-3-000mah-batteries-or-larger-made-to-last-longer
Sept 2017