## Slide 1: Discussion of possible BCCs for WUR
Date: 2017-09-12
Authors:

## Slide 2: Abstract
Using the 802.11 BCC for WUR has been proposed [1]
Concerns has been expressed regarding the decoding complexity [2]
In this contribution we discuss two means to address this complexity concern:
  Using a less complex code and study performance impact
  Using a systematic code to allow for implementations without a Viterbi decoder

## Slide 3: The codes under consideration
The 802.11 rate ½ code
  Const. length 7, polynomial = [133, 171], nr. memory elements 6
A lower complexity rate ½ code
  Const. length 4, polynomial = [17, 13], nr. memory elements 3
  This is the BLE long range code
Systematic versions of the two above codes
  Wi-Fi: Constraint length 7, polynomial = [1, 171/133]
  BT: Constraint length 4, polynomial = [17/13, 1]

## Slide 4: Decoding complexity
Decoding is typically done with a Viterbi decoder
Therefore, the decoding complexity scales proportionally with the number of states in the trellis
The number of states in the trellis are , where is the number of memory elements in the encoder
In [1], the energy to decode a 100 bit payload is
  , thus

## Slide 5: Systematic vs Non-Systematic Codes
For systematic codes, the information bits are part of the code word
  Ex. non-systematic Ex. systematic
The receiver may read the message without using a convolutional decoder
Input: …}
Input: …}
Output: …}
Output: …}
Output: …}
Output: …}

## Slide 6: Simulation Results
The lower complexity code performance is about 0.3 dB worse than the Wi-Fi code in TGnB and TGnD
The systematic versions of all codes perform identically to the non-systematic codes in terms of PER
5 dB

## Slide 7: Straw Poll
Do you support the use of a lower complexity convolutional code than the Wi-Fi [133, 171]?
Y/N/A: 0/0/0

## Slide 8: Straw Poll
Do you support the use of a systematic convolutional code?
Y/N/A: 0/0/0

## Slide 9: References
[1] Steve Shellhammer and Bin Tian, “WUR Data Rates,” IEEE 802.11-17/0990r2, July 2017
[2] Eunsung Park et al., “Symbol Structure,” IEEE 802.11-17/1347r1, Sept. 2017