## Slide 1
Asymmetric beamforming training procedure enhancements
Authors:
Name | Affiliation | Address | Phone | Email
Ilya Bolotin | Intel | Turgeneva 30, Nizhny Novgorod, 603024, Russia | +7 (831) 2969444 | ilya.bolotin@intel.com
Alexander Maltsev | Intel |  |  | alexander.maltsev@intel.com
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com

## Slide 2: Abstract
This presentation introduces changes for asymmetric beamforming training procedure and addresses CIDs 186, 187, 188, 371, 439, 440, 513.

## Slide 3: Current state
Currently Asymmetric beamforming training procedure considers the following steps:
Adding TRN-R subfields to DMG Beacon frames transmitted in the BTI;
Beamforming training between the PCP/AP and non-PCP/non-AP STAs which is performed in scheduled beamforming training allocation in DTI

## Slide 4: Current state
The beamforming training allocation in DTI considers two consecutive phases:
AP performs sweeping through all sectors in the listening mode with the same duration of listening on each sector. Several space-time slots are provided for STAs responses in each sector
AP transmits acknowledgements for each sector

## Slide 5: Probability of STA appearance in specific sector for dense 11ay scenarios (The antenna array with 8x32 elements which has N = 256 sectors in 2D DFT Codebook was considered )
Statistics of sectors load
The system level simulations have shown that in dense 11ay scenarios there are a lot of sectors which are free of STAs and listening of them for several timeslots is a waste of time.
Sector specific approach should be used for beamforming training allocation scheduling

## Slide 6
Sector specific approach for beamforming training allocation
The comparison between two approaches was held:
  Legacy approach. AP provides the same number of space-time slots for each sector
  Sector specific approach. The number of space-time slots provided per each sector is based on the load of this sector
The simulation results demonstrate significant gains of sector specific approach in collision probability and the total duration of asymmetric beamforming training
Probability for STA to get into collision vs. number of space-time slots in beamforming training allocation
(Collision happens when two or more STAs choose the same space-time slot for transmitting their response)

## Slide 7: Changes for asymmetric beamforming training procedure
Considering the sector specific approach we propose the following changes for the procedure of asymmetric beamforming training:
The beamforming training allocation is scheduled per sector. Only one DMG Beacon frame carries information about this beamforming training allocation
The beamforming training allocation describes the period of AP listening in this specific sector and the following Sector ACK frame transmission.

## Slide 8: Changes for asymmetric beamforming training procedure
Considering these changes, to perform asymmetric beamforming training for all (N) sectors we need to schedule N beamforming training allocation. This will not provide any additional signaling overhead as far as signaling for these allocations is performed in a sector specific manner. This provides more flexibility to AP – it can allocate different number of space-time slots for different sectors or skip any sectors at all, e.g. performing asymmetric beamforming training only in some specific sector.

## Slide 9: Signaling of Number of STS per sector
Propose to add a field in the EDMG Extended Schedule element to signal the number of STS in a specific sector.
  The value NSTS indicates the number of space-time slots allocated in this sector for asymmetric beamforming training.
  Based on the sector specific signaling, the EDMG ESE transmitted in different sectors can configure this value in order to allocate different number of space-time slots for different sectors.
 | B0 | B1 | B2 B9 | B10 | B11 B19 | B20 B24 | B25 B26 | B27 B31 | B32 B151
 | Scheduling Type | Channel Aggregation | BW | Asymmetric Beamforming Training | Receive Direction | N STS | Nmax STS | Reserved | Allocation
Bits: | 1 | 1 | 8 | 1 | 9 | 5 | 2 | 5 | 120
Figure: Channel Allocation field format when Scheduling Type is 1.

## Slide 10: Sector ACK Transmission
MBIFS after the PCP or AP completes listening for all space-time slots, it shall transmit a Sector ACK frame on the same combination of sector and DMG antenna which was used for listening.
  If several SSW frames have been received from a STA, the Sector ACK refers to the SSW frame which was received with best quality. The determination of which packet was received with best quality is implementation dependent.
  If multiple STAs transmit SSW frames in the same DMG antenna and sector, only a single Sector ACK frame is needed and able to acknowledge multiple STAs in the same sector (see the proposed Sector ACK frame format for details).

## Slide 11: Sector ACK Frame
Define it as a control frame, and the proposed format is as follows:
 | Frame Control | Duration | RA | TA | Number of Sector Feedback Fields | Sector Feedback 1 | Sector Feedback 2 | … | Sector Feedback N | FCS
Octets | 2 | 2 | 6 | 6 | 1 | 14 | 14 | … | 14 | 4
 | RA | SSW Feedback | BRP Request | Beamformed Link Maintenance
Octets | 6 | 3 | 4 | 1
If the value of Number of Sector Feedback fields is 1, the RA field contains the MAC address of the STA that is the
intended destination of the Sector ACK frame. If the value of Number of Sector Feedback fields is more than 1, the RA
field is set to the broadcast MAC address.
Table: Proposed Sector ACK frame format
Table: Proposed Sector Feedback field.

## Slide 12: Conclusions
We presented a complete flow of asymmetric beamforming after incorporating the enhancements.
The proposed enhancements:
  Make asymmetric beamforming more flexibility. AP may allocate different number of space-time slots for different sectors or skip any sectors at all, providing benefits in collision probability and duration of asymmetric beamforming training.
  Simplify the STA behavior during the asymmetric beamforming training.
  Resolve CIDs 186, 187, 188, 371, 439, 440, 513.

## Slide 13: Straw Poll
Do you agree to include the text changes proposed in (11-17-1422-00-00ay-Draft text for asymmetric beamforming training procedure enhancements) to the spec draft?