## Slide 1
Issues on Wake-up V2P radio
Date: 2017-09-11
Authors:

## Slide 2: Introduction
In the wake-up radio usage model [1], the Wake Up Vehicle-to-Pedestrian (V2P) Radio case has been agreed
  It may be used in 5.9GHz band, which has coexistence issue
  802.11- outside the context of a BSS (OCB) traffic
On the other hand, the features of V2P scenario should be considered in order to operate in V2P usage model
  IEEE 802.11p/WAVE standard defines the operation of ITS traffic in 5.9GHz band, with other bandwidth
In this presentation, several issues on V2P radio application are discussed

## Slide 3: Recap: Wake Up Vehicle-to-Pedestrian (V2P) Radio
Environment
Vehicles, Road Infrastructure and Pedestrian/Cyclist carried device.
Applications
Trigger other devices to turn on (or off) automotive safety radio operation
Transmit Intelligent Transportation Systems (ITS) related information to very low power devices
Traffic Conditions
802.11- outside the context of a BSS (OCB) traffic, 802.11 traffic depending on channels used
Use Case
1.Pedestrian/cyclist approaches dangerous intersection or moving vehicle. Infrastructure or vehicle sends wake up packet. Pedestrian/cyclist carried device turns on automotive safety radio operation (802.11-OCB).
2.Vehicle approaches pedestrian/cyclist. Vehicle transmits wake up packet. Pedestrian/cyclist receives ITS related information.
Challenges and requirements
Operation outside the context of a BSS
Addressing as broadcast/unicast
If used in 5.9Ghz band, coexistence, channel choice
Vendor Specific element an option in WUR Wakeup Trigger Frame

## Slide 4: Issues on ITS applications of wake-up radio: WUR channel for V2P radio in 5.9GHz PCR
According to FCC CFR 47 part 90.377[4], the assigned channels in 5.9 GHz band are defined in 10MHz bandwidth
  The Control Channel(CCH) should be 10MHz bandwidth
To support the use of V2P transmission in 5.9GHz band, the WUR can be transmitted in the Control Channel(CCH) of 5.9GHz
Ch 172
Ch 174
Ch 176
Ch 178
Ch 180
Ch 182
Ch 184
SCH
safety
SCH
safety
CCH
SCH: may used in 20MHz
SCH: may used in 20MHz

## Slide 5: Wake-up frame in 5.9GHz band
Transmission of wake-up packet in Control channel:
  If the wake-up frame is transmitted in Control Channel(CCH), the legacy devices use 10MHz bandwidth
  However, according to the SFD, the wake-up packet consists of 20MHz non-HT preamble and WUR payload
  → In this case, the preamble can be sent in 10MHz bandwidth, for better coexistence with IEEE 802.11p

## Slide 6: Issues on ITS applications of wake-up radio: 802.11-OCB traffic in ITS
The vehicle may inform the approach to pedestrian directly
The vehicle may not be associated with the AP
  In 5.9GHz band, the OCB traffic transmission is available
  → The vehicle to pedestrian message can be OCB traffic

## Slide 7: STA-STA transmission scenario with OCB traffic
According to the spec framework[3], the identifiers in wake-up frame is not MAC address
  The identifier of transmitter and/or receiver in a wake-up frame shall not be the MAC address
  The identifier may not be defined unless the STA is associated
The WUR operation in OCB has not been decided
  The wake-up radio negotiation is not available
  The transmitter may not know whether the STA is in WUR power save state
  The transmitting STA should implement the transmitter of Wake-up frame, which cause more complexity

## Slide 8: STA-STA transmission scenario with OCB traffic
To resolve the identifier problem, the use of WUR can be limited to the broadcast traffic
  In this case, the wake-up ID is the broadcast address
To work with OCB in wake-up radio, the additional procedure is needed
  The use of fixed values in WUR in 5.9GHz band
  The vehicles always transmits the wake-up packet before the transmission of information packet
Notes: OCB traffic의 사용을 동의하기 위해서는

## Slide 9: Conclusion
In this presentation, we discussed the issues of ITS usage model of wake-up radio, especially in 5.9GHz bands
The issues of wake-up radio in V2P usage model can be:
  WUR Channel with IEEE 802.11p PCR, especially in 5.9GHz bands
  OCB traffic without association in wake-up radio
Further optimization can be added in order to resolve the issues

## Slide 10: Reference
[1] IEEE 802.11-17/0029r9 “WUR Usage Model Document”
[2] IEEE 802.11-17/0406r4 “Use Cases for WUR in ITS”
[3] IEEE 802.11-17/0575r3 “Spec framework”
[4] Electronic Code of Federal Regulations