## Slide 1: Deterministic Backoff
Author:
Name | Affiliation | Address | Phone | Email
Menzo Wentink | Qualcomm | Utrecht, The Netherlands | +31-65-183-6231 | mwentink@qualcomm.com

## Slide 2: Deterministic Backoff – Introduction
Deterministic Backoff is a backoff mechanism which dynamically tries to find a round robin scheduling order in a distributed way
In the round robin order, the backoff at each node is deterministic, based on the number of interruptions counted during the prior deterministic backoff
  each interruption represents another node
  the actual backoff count at each node will be different, so each node will access the channel at a different moment (round robin, no collisions)
  clearly, the collision-free situation exists only under specific conditions, but deterministic backoff performs better than exponential backoff in other conditions as well (channel access is much more regular)
When two subsequent collisions occurred, a small random backoff is selected to find an idle slot

## Slide 3: Deterministic Backoff – Rules
If retrycount < 2
  backoff = 10 + IPT slots
    IPT = number of backoff interruptions counted during the latest deterministic backoff
      backoff interruptions are CCA busy events
If retrycount ≥ 2
  backoff = random between 0 and 6 slots
    IPT is not updated after a random backoff
  retrycount is reset every 7 retries
    this causes deterministic backoffs to occur also when many consecutive collisions occur (like when many nodes start up simultaneously)
Note: the interruption count IPT is only reset to 0 after a succesful transmission
  therefore, after a series of consecutive collisions and random backoffs, the IPT will still have the value counted during the deterministic backoff that preceded the random backoffs

## Slide 4: Simulation 1: 2x7 APs
Simulation 1 settings
  2 clusters
  7 APs per cluster
  Contended downlink, no contended uplink
  Full buffer traffic
  5 m distance, 10 dBm Tx power (no hidden nodes)

## Slide 5: Sim 1: 2x7 APs Deterministic Backoff

## Slide 6: Sim 1: 2x7 APs Exponential Backoff

## Slide 7: Simulation 2: 10x7 APs
Simulation 2 settings
  10 clusters
  7 APs per cluster
  Contended downlink, no contended uplink
  Full buffer traffic
  20 m distance, 10 dBm Tx power

## Slide 8: Sim 2: 10x7 APs Deterministic Backoff

## Slide 9: Sim 2: 10x7 APs Exponential Backoff

## Slide 10: Simulation 3: Mixing Deterministic and Exponential
Simulation 3 settings
  2 clusters
  7 APs per cluster (14 APs total)
  Contended downlink, no contended uplink
  Full buffer traffic
  5 m distance, 10 dBm Tx power (no hidden nodes)

## Slide 11: Sim 3: 14x Exponential

## Slide 12: Sim 3: 13x Exponential 1x Deterministic

## Slide 13: Sim 3: 7x Exponential 7x Deterministic

## Slide 14: Sim 3: 1x Exponential 13x Deterministic

## Slide 15: Sim 3: 14x Deterministic

## Slide 16: Simulation 4: 50 nodes (full buffer)
Simulation 4 settings
  1 cluster
  50 nodes (10 APs, 40 STAs - 4 STAs per AP)
  Contended uplink and downlink
  Full buffer traffic
  1 m distance, 10 dBm Tx power, no hidden nodes

## Slide 17: Sim 4: 50 nodes (full buffer) Deterministic Backoff

## Slide 18: Sim 4: 50 nodes (full buffer) Exponential Backoff

## Slide 19: Simulation 5: 50 nodes (Poisson arrivals)
Simulation 5 settings
  1 cluster
  50 nodes (10 APs, 40 STAs - 4 STAs per AP)
  Contended uplink and downlink
  Poisson arrivals
  1 m distance, 10 dBm Tx power, no hidden nodes

## Slide 20: Sim 5: 50 nodes (Poisson arrivals) Deterministic Backoff

## Slide 21: Sim 5: 50 nodes (Poisson arrivals) Exponential Backoff

## Slide 22: References
11-17-1721-00-coex-normative-text-for-deterministic-backoff
11-17-1720-00-coex-example-code-for-deterministic-backoff
11-15-1152-01-000m-moderated-backoff
  Moderated Backoff is a predecessor to Deterministic Backoff, with similar interruptions based adaptation, but with a random backoff
11-15-1437-00-000m-experimental-evaluation-of-moderated-edca-over-wmp
  Describes a real life implementation of Moderated Backoff based on interruptions
MAC Design on Real 802.11 Devices: from Exponential to Moderated Backoff
  WoWMon paper by Ilenia Tinnirello, Menzo Wentink, Domenico Garlisi, Fabrizio Giuliano, Giuseppe Bianchi (Universita ́ di Palermo, Qualcomm, Universita ́ di Roma Tor Vergata)