## Slide 1: Comments on Use Models
Date: 2017-09-11
Authors:

## Slide 2: Abstract
This document comments on corrections for usage models in the usage scenario document 11-15-0625r4
Notes: The TG documents are introduced in every meeting agenda

## Slide 3: Corrections on Usage Model Table
The summary table in slide 27 of the usage scenario document (11-15-0625r4) does not reflect correctly the parameters within the context
UC # | Indoor (I)/ Outdoor (O) | Environment | Throughput | Topology | Latency | Security | Availability | Applications and Characteristics
 |  | LOS/ NLOS |  |  |  |  |  | 
1 | I | <10cm | ~10Gbps | P2P | <100ms |  |  | -Static,D2D, -Streaming/Downloading
2 | I | <5m | >28Gbps | P2P | <5ms |  |  | -Uncompressed 8K UHD Streaming
3 | I | <5m | ~20Gbps | P2P | <100ms < 5ms |  |  | -Low Mobility, D2D -3D UHD streaming
4 | I | <10m < 5m | ~20Gbps | P2P/P2MP | <100ms < 50ms | C/I | 99.99% | -Indoor Backhaul with multi-hop*
5 | I | <100m | >20Gbps | P2P/P2MP | <100ms | C/I |  | -Multicast -Streaming/Downloading - Dense Hotspot

## Slide 4
UC # | Indoor (I)/ Outdoor (O) | Environment | Throughput | Topology | Latency | Security | Availability | Applications and Characteristics
 |  | LOS/ NLOS |  |  |  |  |  | 
6 | I/O | <100m | >20Gbps | P2P/P2MP | <100ms | C/I | 99.99% | -Multi-band -Multi-RAT operation Hotspot
7 | O | <200m | ~20Gbps | P2P/P2MP |  | C/I | 99.99% | -Fronthauling
8 | O | <1km with single hop <150m per hop with multiple hops | ~2Gbps | P2P/P2MP | <35ms | C/I | 99.99% | -Small Cell Backhauling - Single hop or multiple hop
9 | I | <3m | ~20Gbps | P2P/P2MP | <10ms |  |  | - Office docking
10 | O | <300m (street-poles) <1000m (rooftops) | >4Gbps /DN site >1Gbps /Home AP >2Gbps /Building AP | P2P/P2MP | < 15 ms (WTTH/B, WiFi AP BH) (e-t-e)** < 5 ms (5G Small cell BH) (e-t-e)** < 2 ms (per hop latency) | C/I | 99% | - mmWave distribution network
11 | I | <3m <0.2 m | ~20Gbps ~10Gbps | P2P/P2MP | <10ms |  |  | - USR wireless docking
Notes: - USR: ultra-short range

## Slide 5: Correction on Usage Model or Functional Requirement
The latency value (< 5 ms) in usage models #2 (8K UHD) and #3 (AR/VR Headsets) in the summary table do not match with the value (< 10 ms) in the functional requirement document (11-15-1074r0)
Summary of Key metrics in 11-15/0625r4
UC # | Indoor (I)/ Outdoor (O) | Environment | Throughput | Topology | Latency | Security | Availability | Applications and Characteristics
 |  | LOS/ NLOS |  |  |  |  |  | 
2 | I | <5m | >28Gbps | P2P | <5ms < 5ms or < 10 ms? |  |  | -Uncompressed 8K UHD Streaming
3 | I | <5m | ~20Gbps | P2P | <100ms < 5ms or < 10 ms? |  |  | -Low Mobility, D2D -3D UHD streaming
Notes: Check where PER range came from
Check actual 11ad PER

## Slide 6: References in Functional Requirement Doc
The reference in the functional requirements document is outdated
[3] “11-15-0328-04-ng60-ng-60-usage-models.ppt” need to be changed to “11-15-0625-05-00ay-ieee-usage-scenarios.pptx”
Notes: - Mention functional requirement are mentioned in

## Slide 7: References
[1] 11-15-0625-04-00ay-ieee-802-11-tgay-usage-scenarios
[2] 11-15-1074-00-00ay-11ay-functional-requirements