## Slide 1: History of PD and ED reviewed
Date: 2017-09-10
Authors:

## Slide 2: Abstract
In this document we analyze the historical background of Preamble Detection (PD) and Energy Detection (ED). We reveal that any statements declaring ED being an older technology than PD are unjustified.

## Slide 3: ALOHA
In 1971, the University of Hawaii operated ALOHAnet
  According to the ALOHA protocol devices do not apply Listen-before-talk (LBT) or related carrier sensing (CS) mechanisms
  Under the ALOHA protocol, devices transmit at will
  If another device transmits simultaneously, a device retransmit after a random period

## Slide 4: Ethernet
In 1973 to 1974, Bob Metcalfe invented Ethernet
  The initial standard was formed by Digital Equipment Corporation, Intel, and Xerox (DIX)
In 1980, IEEE formed project 802
  In 1983, an improved version of DIX became 802.3
Ethernet (802.3) applies Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
  Since today’s Ethernet solely relies on full-duplex communication CSMA/CD is no more needed or applied

## Slide 5: Ethernet Carrier Sensing (1)
Ethernet relies on CSMA
  Ethernet detects a Carrier signal
  “The MAC sublayer shall also monitor the value of carriersense to defer its own transmissions when the medium is busy.” [2]
  “Carrier On. This event indicates that the physical layer has detected a change in carrier sense from no carrier to carrier.” [2]
    This is equivalent to receiving data
  During a collision no data may be received
    The “Collision detect thresholds” defines the voltage thresholds for detecting collisions when two or more stations are transmitting simultaneously [2]

## Slide 6: Ethernet Carrier Sensing (2)
Carrier sensing ≠ Energy detection
  If carrier detected a station defers from transmitting
  This is similar to 802.11’s preamble detection
Collision detect threshold
  If no signal may be decoded the detect threshold indicates that two more stations transmit simultaneously
  This resembles 802.11’s Energy Detection (ED) although here it is used to detect collisions where as 802.11’s ED is used to prevent collisions

## Slide 7: 802.11
802.11 formed out of 802.3 resp. 802.4 [4]
  Carrying over CSMA idea after Token-based approach failed
802.11-1997 [7] defines three different PHYs
  Direct Sequence Spread Spectrum (DSSS)
  Frequency Hopping Spread Spectrum (FHSS)
  Infrared (IR)

## Slide 8: FHSS
CCA consists of two conditions
  Detection of an 802.11-compliant 1 Mb/s signal above a certain threshold
    Referred to as “CCA threshold (preamble)”
  Detection of an 802.11-compliant 1 Mb/s signal above a 20 dB higher threshold with random data
    Referred to as “CCA threshold (random data)”
No Energy Detection scheme defined or required

## Slide 9: DSSS
An implementation may chose from three different CCA modes
  CCA Mode1: Energy above threshold. CCA shall report a busy medium upon detecting any energy above the ED threshold.
  CCA Mode 2: Carrier sense only. CCA shall report a busy medium only upon the detection of a DSSS signal. This signal may be above or below the ED threshold.
  CCA Mode 3: Carrier sense with energy above threshold. CCA shall report a busy medium upon the detection of a DSSS signal with energy above the ED threshold.
Any of the three modes renders an 802.11 DSSS implementation compliant with the standard
Implementations seem to solely rely on carrier sensing (equivalent to preamble detection)
  “It is not clear how many 11b devices actually implement ED-CCA or solely use 11b preamble detect. However, because many (if not all) 11b devices use just CS, 11g OFDM transmissions must use protection mechanism that is usually a RST/CTS or CTS-to-self.” [5]
  “Normally, mode 2 is used.” [6]

## Slide 10: IR
First appearance of Energy Detect (ED)
  “The ED signal shall be set true when IR energy variations in the band between 1 MHz and 10 MHz exceed 0.001 mW/cm2. The ED shall operate independently of the CS.”
  Basically preventing a blinded station from transmitting
Carrier Sense (CS)
  “The CS shall be asserted by the PHY when it detects and locks onto an incoming PLCP Preamble signal.”
CCA
  “CCA shall be asserted ‘IDLE’ by the PHY when the CS and the ED are both false, […].”

## Slide 11: OFDM
[3] reviews the development process of 802.11a
Submissions [8] to 802.11 TGa indicate that preamble detection (PD) was developed first
  With OFDM a missed preamble causes the remaining part of a transmission to be undecodable
  A mitigation mechanism was needed
802.11a introduces a mechanism to deal with missed preambles
  Later renamed Energy Detect (ED)

## Slide 12: Conclusion
There are no sources that justify any statement that Energy Detection (ED) is an older approach than Preamble Detection (PD)
  Historical documents do not indicate any evidence for consideration of dissimilar technologies
  Self-centric development process, not targeting coexistence with other technologies
  802.11 developed PD first
  ED serves as complementary or generalized approach of PD

## Slide 13: References
N. Abramson, “Development of the ALOHANET,” IEEE Transactions on Information Theory, vol. 31, no. 2, Mar 1985. [Online]. Available: https://doi.org/10.1109/TIT.1985.1057021
IEEE, “IEEE Standards for Local Area Networks: Carrier Sense Multiple Access with Collision Detection (CSMA/CD) Access Method and Physical Layer Specifications,” ANSI/IEEE Std 802.3-1985, [Online]. Available: http://ieeexplore.ieee.org/servlet/opac?punumber=2381
G. R. Hiertz, J. S. Lee, and L. Cariou, “Co-chairmen notes on current status of 802.11ax Spatial Reuse ad hoc group,” IEEE 802.11 submission 11-15/1139, Sep. 2015. [Online]. Available: https://mentor.ieee.org/802.11/dcn/15/11-15-1139
C. A. Rypinski, “Retrospective on Development of Radio and Wire Data Communication,” IEEE 802.15 Wireless submission 15-06-0107, Mar. 2006. [Online]. Available: https://mentor.ieee.org/802.15/dcn/06/15-06-0107
G. Smith and B. Hart, “ED CCA for Clauses 16, 17,” IEEE 802.11 submission 11-14/1518r5, Oct. 2014. [Online]. Available: https://mentor.ieee.org/802.11/dcn/14/11-14-1518-05
R. Gummadi, D. Wetherall, B. Greenstein, and S. Seshan, “Understanding and mitigating the impact of RF interference on 802.11 networks.” In Proceedings of the 2007 conference on Applications, technologies, architectures, and protocols for computer communications (SIGCOMM '07), 2007.
IEEE, “Information technology—Telecommunications and information exchange between systems—Local and metropolitan area networks—Specific requirements—Part 11:Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) specification” IEEE 802.11-1997, June 1997. [Online]. Available: http://ieeexplore.ieee.org/servlet/opac?punumber=5258
IEEE 802.11, “IEEE 802.11 Archive Documentation,” Last accessed 2017-08-03. [Online]. Available: http://www.ieee802.org/11/Documents/DocumentArchives/