## Slide 1: Local MAC Addresses in the Overview and Architecture based on IEEE Std 802c
Date: 2017-09-11
Authors:
Name | Affiliations | Address | Phone | email
Roger Marks | EthAirNet Associates | Denver, CO, USA | 1-802-capable | roger@ethair.net

## Slide 2: Abstract
IEEE Std 802c was approved by the IEEE-SA Standards Board on 15 June 2017, amending the IEEE 802 Overview and Architecture to specify Local Medium Access Control (MAC) Address Usage. This slide set summarizes the changes and implications. It also summarizes a new revision, prepared in coordination with 802c, of the relevant tutorial of the IEEE Registration Authority (IEEE RA).

## Slide 3: The View from Silicon Valley
Dinesh: What are those devices? Those aren’t phones.
Gilfoyle: Look at that OUI prefix in these MAC addresses.
Richard: OK, so what are those?
Gilfoyle: Smart fridges. About 30,000 of them.
Silicon Valley (a fictional television comedy)
Season 4, Episode 10 (“Server Error”)
First aired on HBO, 2017-06-25

## Slide 4: What Gilfoyle saw

## Slide 5: What Gilfoyle saw
Is device_id a MAC addresses?
Are those OUI prefixes?
How was this data collected?
How could Gilfoyle recognize smart fridges?
Should we care?
How is 802c related?

## Slide 6: IEEE Std 802c: Key Facts
IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture – Amendment 2: Local Medium Access Control (MAC) Address Usage
Standard approved: 2017-06-15; published 2017-08-25
  802 pseudo-tutorial, 2014-11-03
  802.1 Local Address Study Group, Nov 2014 - July 2015
  PAR Authorized: 2015-01-11
  PAR Revised: 2016-12-07 (to add maintenance issues)
Scope in brief:
  provide an optional local MAC address space structure to allow multiple administrations to coexist
  designate a range of local MAC addresses for protocols using a Company ID (CID) assigned by the IEEE Registration Authority
  range of local MAC addresses will be designated for assignment by local administrators
  a range of local MAC addresses for use by IEEE 802 protocols

## Slide 7: Local Address: Example
M bit (I/G bit): as before, 1 for multicast
X bit (U/L) bit: as before, 1 for local
  Y and Z bits: new designations

## Slide 8: SLAP
Structured Local Address Plan (SLAP): An optional standardized specification for the use of local medium access control (MAC) address space entailing the use of
  Extended Local Identifier (ELI),
  Standard Assigned Identifier (SAI), and
  Administratively Assigned Identifier (AAI)
  addresses in specific disjoint ranges.

## Slide 9: Assignment Protocols
An address assignment protocol assigning local MAC addresses to devices on a LAN should ensure uniqueness of those addresses.
When multiple address assignment protocols operate on a LAN without centralized administration, address duplication is possible, even if each protocol alone is designed to avoid duplication, unless such protocols assign addresses from disjoint address pools.
Administrators who deploy multiple protocols on a LAN in accordance with the SLAP will enable the unique assignment of local MAC addresses within the LAN as long as each protocol maintains unique assignments within its own address subspace.

## Slide 10: SLAP Quadrants
SLAP quadrant | Y bit | Z bit | ZYXM | second hex digit | SLAP local identifier type | SLAP local identifier
01 | 0 | 1 | 1010 | A | Extended Local | ELI
11 | 1 | 1 | 1110 | E | Standard Assigned | SAI
00 | 0 | 0 | 0010 | 2 | Administratively Assigned | AAI
10 | 1 | 0 | 0110 | 6 | Reserved | Reserved
 | Y = 0 | Y = 1
Z = 0 | AAI | Reserved
Z = 1 | ELI | SAI
“A” for AAI and “E” for ELI would have been nice, but prior IEEE RA assignments put ELI in the “A” quadrant.

## Slide 11: ELI: Extended Local Identifier
like an EUI, but with a Company ID (CID) instead of an OUI
  CID has X = 1 (local space).
IEEE Registration Authority (RA) assigns CIDs, all in SLAP 01
  CID predates 802c
802c reserves 4 CIDs for the local administrator
second hex digit = A

## Slide 12: AAI: Administratively Assigned Identifier
AAI: Administratively Assigned Identifier
  second hex digit = 2
  Administrators who wish to assign local MAC addresses in an arbitrary fashion (for example, randomly) and yet maintain compatibility with other assignment protocols operating under the SLAP on the same LAN may assign a local MAC address as AAI.
Reserved quadrant can be used like AAI, with reservations:
  second hex digit = 6
  may be administratively used and assigned in accordance with the considerations specified for AAI usage, without effect on SLAP assignments. However, administrators should be cognizant of possible future specifications… that would render administrative assignment incompatible with the SLAP.

## Slide 13: SAI: Standard Assigned Identifier
second hex digit = E
Specification of the use of the SAI quadrant for SLAP address assignments is reserved for the standard forthcoming from IEEE P802.1CQ.
An SAI is assigned by a protocol specified in an IEEE 802 standard.
Multiple protocols for assigning SAI may be specified within various IEEE 802 standards. Coexistence of such protocols may be supported by restricting each to assignments within a subspace of SAI space.
In some cases, an SAI assignment protocol may assign the SAI to convey specific information. Such information may be interpreted by receivers and bridges that recognize the specific SAI assignment protocol, as identified by the subspace of the SAI. The functionality of receivers and bridges that do not recognize the protocol is not affected.

## Slide 14: P802.1CQ
IEEE Standard for Local and Metropolitan Area Networks: Multicast and Local Address Assignment
PAR authorized: 2016-02-05
Scope: This standard specifies protocols, procedures, and management objects for locally-unique assignment of 48-bit and 64-bit addresses in IEEE 802 networks. Peer-to-peer address claiming and address server capabilities are specified.
Need: Currently, global addresses are assigned to most IEEE 802 end station and bridge ports. Increasing use of virtual machines and Internet of Things (IoT) devices could exhaust the global address space. To provide a usable alternative to global addresses for such devices, this project will define a set of protocols that will allow ports to automatically obtain a locally-unique address in a range from a portion of the local address space. Multicast flows also need addresses to identify the flows. They will benefit from a set of protocols to distribute multicast addresses. Peer-to-peer address claiming and address server capabilities will be included to serve the needs of smaller (e.g. home) and larger (e.g. industrial plants and building control) networks.
Progress so far: little

## Slide 15: Address Block Sizes (48-bit addresses)
second hex digit | address type | Admin | Block Size | Subdivision | Subdivision Block Size
..00 (0,4,8,C) | EUI-48 | IEEE RA | 246 ≈ 7.0*1013 | MA-L (OUI) | 224 ≈ 1.7*107
 |  |  |  | MA-M | 220 ≈ 1.0*106
 |  |  |  | MA-S | 212 ≈ 4.1*103
..01 (2,6,A,E) | all local unicast |  | 246 ≈ 7.0*1013 |  | 
1010 (A) | ELI | IEEE RA | 244 ≈ 1.8*1013 | CID | 224 ≈ 1.7*107
1110 (E) | SAI | IEEE 802 | 244 ≈ 1.8*1013 |  | 
0010 (2) | AAI |  | 244 ≈ 1.8*1013 |  | 
0110 (6) | Reserved |  | 244 ≈ 1.8*1013 |  | 
How many is is 246?
  IEEE manages EUI-48 space to support unique identification of hardware anywhere in the world for 100 years.
  The SLAP gives IEEE 802 a space one quarter of that size to exploit for a LAN!

## Slide 16: Did Gilfoyle see OUIs?
The device_id looks like a 48-bit MAC address.
Second hex digits: 2, 6, A, E
  local MAC addresses
  all 4 SLAP types
These are not EUI-48s.
  There are no OUIs here.

## Slide 17: Did Gilfoyle see CIDs?
Six-digit prefixes are apparent.
Prefix 2A-C6-F7 looks like a CID
  not in public CID registry
  other prefixes are not CIDs
It seems that Gilfoyle saw, as the smart-fridge prefix, E2-09-F6, in the AAI quadrant.
  15 of the 25 devices
  [unclear how he counted 30,000]
Outside the ELI/CID quadrant, six-digit prefixes are not standard.

## Slide 18: Could Gilfoyle detect smart fridges?
In general, the MAC address is not forwarded past an IP router.
  However, it could be tracked and passed by a device on the LAN, and then be entered into a database.
  Devices could be programmed to send their addresses.
Smart-fridge OUIs could potentially be identified by OUI, if the EUI was assigned under a specific smart-fridge OUI.
Local addresses are not global and not normally permanent.
Smart-fridge addresses would typically not be identified by CID.
  CID is not definitively tied to the host hardware.
  For example, CID may identify an assignment protocol.
  It’s feasible for the manufacturer to assign an address to a device as an ELI using a manufacturer’s registered CID
    extension bits could be static or dynamic

## Slide 19: Would a fridge maker use an ELI?
Fridge manufacturer could register a CID and assign MAC address as an ELI
  could specify informative subfields
  e.g. could encode model number or serial number
This might be useful.
  for example, a smart home hub might be able to discover the fridge solely from its address
But it may also be dangerous
  fridge may be susceptible to attack based on characteristics inferred from its address

## Slide 20: Is fridge detection a good idea?
MAC addresses are visible on the LAN, and could be tracked outside the LAN.
  This could lead to a privacy violation.
  But it could offer opportunities
    Gilfoyle took advantage of a property of an address
    Other addresses can have other special properties
    Network management takes advantage of known addresses
If we keep informative addresses separate from flat (e.g. random) addresses, then we can support both types on the LAN.
If we don’t keep them separate, then we may see collisions.

## Slide 21: IEEE 802 is SLAP Happy
The SLAP offers:
  organizations a block of ~17M addresses for innovative ELI uses
  IEEE 802 a block of ~ 1.8*1013 addresses for innovative SAI uses
  administrators a block of ~ 1.8*1013 addresses to do what they want while avoiding collision with ELI and SAI users
The SAI block is a huge opportunity for IEEE 802!
Let’s use it!

## Slide 22: Annex 1: IEEE RA Tutorial – Guidelines for Use of EUI, OUI, CID

## Slide 23: IEEE RA Tutorial – Guidelines for Use of EUI, OUI, CID
IEEE Registration Authority assigns OUIs, CIDs, etc.
Provides tutorials on identifiers and policies:
  http://standards.ieee.org/develop/regauth/tut
Tutorial on EUI (referenced in IEEE Std 802):
Guidelines for Use of Extended Unique Identifier (EUI), Organizationally Unique Identifier (OUI), and Company ID (CID)
  Published August 2017, in coordination with 802c
  Supersedes:
    Guidelines for Use Organizationally Unique Identifier (OUI) and Company ID (CID)
    Guidelines for 48-Bit Global Identifier (EUI-48)
    Guidelines for 64-bit Global Identifier (EUI-64)

## Slide 24: Guidelines for Use of EUI, OUI, CID – more details
Published August 2017
  http://standards.ieee.org/develop/regauth/tut/eui.pdf
Covers local addresses, SLAP, CID, and ELI
Clarifies other policies; notably (unrelated to local addressing) regarding the multicast bit:
  The assignee of an OUI or OUI-36 is exclusively authorized to assign group MAC addresses, with I/G=1, by extending a modified version of the assigned OUI or OUI-36 in which the M bit is set to 1. Such addresses are not EUIs and do not globally identify hardware instances, even though U/L=0.
  The assignee of a CID may assign local group MAC addresses by extending a modified version of the assigned CID by setting the M bit to 1 (so that I/G=1). The resulting extended identifier is an ELI.

## Slide 25: Annex 2: Non-permanent Addresses

## Slide 26: Non-permanent Addresses
IEEE 802 is most familiar with permanent addresses
Local addresses are typically not permanent
  they may be assigned during use
Need to consider the ramifications

## Slide 27: Some Address Features
Uniqueness
  most fundamental property
  local (on the LAN), or universal
  relevant to identity
Permanence/Longevity
  relevant to trackability
  relevant to management
Structure and Information content
  Does the address convey information beyond identity?
  Can address convey location (e.g., IP)
  other possibilities

## Slide 28: Example: IPv4
IPv4 address can be globally routable
IPv4 address can be local
IPv4 address is hierarchical, with two components:
  prefix: identifies network or subnet
  host identifier: identifies interface
  must separately specify the prefix length to distinguish the two

## Slide 29: View from IETF: IPv6
For ideas on possible protocols, consider IETF.
• IPv6 unicast address (128 bits) includes:
  - subnet prefix (n bits, typically 64)
  - interface ID (IID) (128-n bits, typically 64)
    used to identify interfaces on a link
    formerly encouraged creation from IEEE EUI (e.g. RFC 4291)
    RFC 7136: various new forms of IIDs have been defined: including temporary addresses [RFC4941], Cryptographically Generated Addresses (CGAs) [RFC3972] [RFC4982], Hash-Based Addresses (HBAs) [RFC5535] …

## Slide 30: Some IPv6 IID Forms
temporary addresses [RFC4941]
  use with SLAAC; IID changes for privacy
Semantically Opaque Interface Identifiers [RFC7217]
  use with SLAAC; IID changes when subnet changes
  benefits of stable addresses can be achieved without sacrificing the security and privacy of users
Cryptographically Generated Addresses (CGAs) [RFC3972]
  verification of source address
Hash-Based Addresses (HBAs) [RFC5535]
  bind multiple addresses assigned to a single host
ISATAP addresses [RFC5214]
  IPv4 address embedded in IPv6 address

## Slide 31: Some Assignment Protocols
Stateful (per IETF)
  typically server-based
  example: DHCP
Stateless (per IETF)
  IPv6 “Stateless Address Autoconfiguration” (SLAAC)
    could be based on IEEE EUI
    requires Duplicate Address Detection (DAD)
claiming
  device claims an address by announcement, but:
    may probe first for addresses in use
    may check afterwards for collisions
P802.1CQ PAR mentions “peer-to-peer address claiming and address server capabilities”

## Slide 32: IETF: Temporary Addresses
SLAAC = “Stateless Address Autoconfiguration”
RFC 4941: Privacy Extensions for SLAAC in IPv6
  Sept. 2007
  …for interfaces whose interface identifier is derived from an IEEE identifier. Use of the extension causes nodes to generate global scope addresses from interface identifiers that change over time, even in cases where the interface contains an embedded IEEE identifier. Changing the interface identifier (and the global scope addresses generated from it) over time makes it more difficult for eavesdroppers and other information collectors to identify when different addresses used in different transactions actually correspond to the same node.

## Slide 33: Semantically Opaque Interface Identifiers
RFC 7217
  Apr. 2014
  temporary addresses can be challenging.... from a network-management point of view, they tend to increase the complexity of event logging, troubleshooting, enforcement of access controls, and quality of service.... some organizations disable the use of temporary addresses even at the expense of reduced privacy… may also result in increased implementation complexity
  …Interface Identifier changes when the host moves from one network to another. This method is meant to be an alternative to generating Interface Identifiers based on hardware addresses (e.g., IEEE LAN Media Access Control (MAC) addresses), such that the benefits of stable addresses can be achieved without sacrificing the security and privacy of users.

## Slide 34: IETF CGA
CGA = “Cryptographically Generated Address”
RFC 3972
  March 2005
  interface identifier is generated by computing a cryptographic one-way hash function from a public key and auxiliary parameters. The binding between the public key and the address can be verified by re-computing the hash value and by comparing the hash with the interface identifier. Messages sent from an IPv6 address can be protected by attaching the public key and auxiliary parameters and by signing the message with the corresponding private key. The protection works without a certification authority or any security infrastructure.
  includes collision count field based on duplicate address detection

## Slide 35: Example: CGA and Privacy can coexist
On a LAN, some devices strive for privacy
  may use a randomized address
On a LAN, some devices may not value privacy but put value on other features, such as verification
  example: servers should be easily found
  address may be structured for meaning
Both types of devices should be able to coexist
  random addresses should stay out of assigned space
  receiver can then determine the type of address and respond accordingly

## Slide 36: CGA/Privacy Coexistence

## Slide 37: CGA/Privacy Coexistence

## Slide 38: CGA/Privacy Coexistence

## Slide 39: CGA/Privacy Coexistence

## Slide 40: CGA/Privacy Coexistence

## Slide 41: CGA/Privacy Coexistence

## Slide 42: Summary
The local address space is huge and valuable.
The IEEE RA’s CID give companies a chance to innovate
  SLAP supports ELIs based on CID
  802 standards should not step on any company’s ELIs
SLAP specifies a reserved quadrant
  802 standards should not step on it
SLAP specifies an AAI quadrant
  802 standards should use the AAI quadrant in any way
SLAP offers a 44 bit SAI quadrant to IEEE 802 to exploit.
  802 standards should put SAI to use in an orderly fashion.
Let’s ensure protocol coexistence for best success.
Please participate in development of P802.1CQ.