## Slide 1: 11az Negotiation Protocol (update)
Date: 2017-09-11
Authors:

## Slide 2: Motivation/Background
Update document 11-17/591r2 with details from presentation we have listened to, since
  Develop corresponding SFD text
  Develop specification outline
Negotiation discussed in this presentation applies only to STA-initiated ranging scenario (iFTMR/iFTM)
  Excludes scalable ranging (e.g. CToA)

## Slide 3: Terminology
  Responder and Initiator
    FTM – Initiator sends iFTMR and Responder sends FTM
    Responder provides its LCI/Location Civic information
    Initiator estimates Range/Position
  Capabilities
    FTM Responder – the device can play the role of a responder for all supported ranging protocols – indicated by setting bit-70 of the Extended Capabilities element
    FTM Initiator – the device can play the role of an initiator for all supported ranging protocols – indicated by setting bit-71 of the Extended Capabilities element
  Ranging Protocols – Time of Flight (ToF) measurement; may be extended for others (needs more discussion)
    REVmc D8.0 Fine Timing Measurement Prototocol (FTM)
    VHT NDP Sounding-based .11az protocol (VHTz)
    HE NDP Sounding-based .11az protocol (HEz)
    Ranging protocol while operating in DMG/EDMG (EDMGz)
Notes:   Should the Capabilities bit(s) apply to all ranging protocols? Or should we allow for indications in the Beacon to indicate Initiator/Responder capabilities for each Ranging Protocol independently? What about Ranging Protocols that do not have a distinct Initiator/Responder?

## Slide 4: Terminology (Cont’d)
Ranging Id
  Association ID-like value assigned to an unassociated STA by an AP to facilitate the negotiation phase and subsequently the ranging phase.

## Slide 5: Negotiation
Security-specific parameters, if required are negotiated outside of (and ahead of) the negotiation phase described in this document
To each discovered Responder that the STA is interested in executing a Ranging Protocol with, the STA sends an initial FTM request (iFTMR) which includes at least one of:
  A FTM Parameters element as described in REVmc D8.0 which is a set of parameters that the STA proposes to use if it executes the FTM ranging protocol with the corresponding responder,
  A NGP Parameters element which is a set of parameters that the STA proposes to use (VHTz, HEz, EDMGz, etc.) – NGP Parameters elements includes at least one of VHTz , HEz and/or EDMGz subelement(s)

## Slide 6: Negotiation (cont’d)
The responder does one of the following:
  Chooses one of the ranging protocols and responds with the corresponding {FTM, NGP} parameters element in the initial FTM (in response to the initial FTM request),
    The included NGP Parameters element shall include one of VHTz, HEz or EDMGz subelement
  Rejects the initial FTM request and optionally includes {FTM. NGP} parameters element indicating the parameter set that it can potentially support (if included in a future iFTMR)
Notes: There is an implicit preference (operating band for a choice between 11AYz and {HEWz, VHTz and FTM}; HEWz, VHTz and FTM – do we still need a preference Indication?

## Slide 7: .11az Negotiation
Leverage FTM approach
  Initiator proposes, Responder approves/disapproves
  Upon successful negotiation with the Responder, use the resulting {FTM. NGP} parameters to execute the selected ranging protocol with the Responder
Proposed Representation
  Leave FTM Parameters element as is
  Define a new NGP Parameters element that includes parameters relevant to both VHTz, HEz and EDMGz ranging protocols
Notes:   Do we need a schedule parameter element? Or a schedule field in the ranging protocol specific sub-element?

## Slide 8: Initial FTM Request/Initial FTM Exchange
 | Category | Public Action | Trigger | LCI Measurement Request (optional) | Location Civic Measurement Request (optional) | Fine Timing Measurement Parameters (Mandatory) (optional) | NGP Parameters (optional)
Octets | 1 | 1 | 1 | variable | variable | 11 | 12
 | Status Indication | Value | Reserved | Number of Bursts Exponent | Burst Duration | Min Delta FTM | Partial TSF Timer
Bits | 2 | 5 | 1 | 4 | 4 | 8 | 16
 | Partial TSF Timer No Preference | ASAP Capable | ASAP | FTMs per Burst | Reserved | Format and Bandwidth | Burst Period
bits | 1 | 1 | 1 | 5 | 2 | 6 | 16

## Slide 9: NGP Parameters Element
 | Element ID (255) | Length | Element ID Extension | NGP Parameters | VHTz specific subelement (optional) | HEz specific subelement (optional) | EDMGz Specific subelement (optional)
Octets | 1 | 1 | 1 | 2 | <tbd> | <tbd> | <tbd>
 | Status Indication | Value | Reserved | Number of Antennas
Bits | 2 | 5 | 1 | 8

## Slide 10: VHTz Specific subelement
Fields included in both iFTMR and iFTM frames
  <none yet>
Fields only included in iFTM frame (reserved in iFTMR)
  Response: Immediate or Delayed
  if Response == Delayed
    MinToaReady and MaxToaAvailable
      the results (ToA/ToD) are delivered within the successive sounding sequence

## Slide 11: HEz Specific Subelement
Fields included in both iFTM and iFTMR frames
  Periodic Availability Window schedule
Fields included in only iFTM frame (reserved in iFTMR)
  Response: Immediate or Delayed
    If Response == Immediate
      results are provided in the same or next Availability Window based on a dynamic indication during the measurement phase
    If Response == Delayed
      results are of the measurements performed in the previous Availability Window
  Included only when Status is Successful
    Ranging ID assigned to the initiator (463r1)

## Slide 12: EDMGz Specific Subelement
<TBD>

## Slide 13: Status and Value fields (from IEEE 80211-2016)
Status: 2 bits
  0: Reserved
  1: Successful
  2: Incapable forever
  3: Incapable for the duration in Value field
Value: 6 bits
  Valid only when the Status field is set to 3
Propose to reuse these fields for the NGP Parameters element also

## Slide 14: .11az Negotiation
Initial FTM Request includes at least one of
  FTM Parameters element
  NGP Parameters element
The Trigger
  Trigger set to 1
Initial FTM frame includes one of FTM, NGP Parameters element
Optionality of FTM Parameters element in iFTMR and iFTM is new in .11az
  FTM Parameters element is optional only when both ends support .11az
Use this exchange to pick a protocol to be used for Ranging
  In a different submission

## Slide 15: SFD Text
Move to adopt the following details to the NGP Parameters element structure for .11az FTM negotiation and include it in the 802.11az SFD (Cl. 8 Frame Formats), granting the SFD Editor editorial license:
The NGP Parameters element if included in the initial FTM Request includes
  At least one of VHTz-specific Subelement, HEz-specific subelement or EDMGz-specific subelement
    Note: if the rSTA has not advertised support for the corresponding protocol it will ignore it if at least one supported protocol specific subelement is specified; otherwise the iFTM will have a status Field in the FTM or NGP Parameters element is not SUCCESSFUL
The NGP Parameters element if included in the initial FTM with the status Field in the FTM or NGP Parameters element is set to SUCCESSFUL, includes
  One of VHTz-specific Subelement, HEz-specific subelement or EDMGz-specific subelement
The Status and Value fields in the iFTM shall be set as defined in IEEE802.11-2016

## Slide 16: SFD Text (Cont’d)
The VHTz-Specific subelement when included in the iFTMR shall include
  <nothing defined yet>
The VHTz-specific subelement when included in the iFTM with the status Field in the FTM or NGP Parameters element is set to SUCCESSFUL shall include
  Response: Immediate or Delayed
  if Response == Delayed
    MinToaReady and MaxToaAvailable
      the results (ToA/ToD) are delivered within the successive sounding sequence

## Slide 17: SFD Text (Cont’d)
The HEz-Specific subelement when included in the iFTMR shall include
  Periodic Availability Window schedule
The HEz-specific subelement when included in the iFTM with the Status Field in the FTM or NGP Parameters element is set to SUCCESSFUL shall include
  Response: Immediate or Delayed
    If Response == Immediate
      results are provided in the same or next Availability Window based on a dynamic indication during the measurement phase
    If Response == Delayed
      results are of the measurements performed in the previous Availability Window
  Included only when Status Field in the FTM or NGP Parameters element is set to SUCCESSFUL
    Ranging ID assigned to the initiator

## Slide 18: Motion-2
Move to adopt the following Text and include it in the 802.11az SFD (Section-1 Definitions), granting the SFD Editor editorial license:
  Ranging Protocols – Time of Flight (ToF) measurement; may be extended for others (needs more discussion)
    REVmc D8.0 Fine Timing Measurement Prototocol (FTM)
    VHT NDP Sounding-based .11az protocol (VHTz)
    HE NDP Sounding-based .11az protocol (HEz)
    Ranging protocol while operating in DMG/EDMG (EDMGz)
  Ranging ID
    Association ID-like value assigned to an unassociated STA by a rSTA to facilitate the negotiation phase and subsequently the ranging phase
Moved: Feng Jiang Seconded: Chao Chun Wang
Y: 11 N: 0 A: 1 Result: Motion Passes

## Slide 19: References
17-0591r2: Ranging Protocol Parameter Negotiation Protocol
17-1305r2: SU Sounding Measurement Exchange and Feedback
17-1455r1: MU Measurement and Feedback Scheduling

## Slide 20: Backup Material

## Slide 21: Motion-2
Move to adopt the following high level frame structure for .11az FTM negotiation and include it in the 802.11az SFD (Cl. 8 Frame Formats), granting the SFD Editor editorial license:
Initial FTM Request includes
  at least one of
    FTM Parameters element
    NGP Parameters element (optional subelements for ranging protocol-specific parameters)
  Optionally LCI and/or Location Civic Measurement Request element
  Trigger Field
    Trigger field set to 1 (for 802.11-2016 FTM backward compatibility)
Initial FTM frame includes
  one of FTM, NGP Parameters element
  Optionally LCI and/or Location Civic Measurement Report element
Moved: Ganesh Venkatesan Seconded: SK Yong
Result: Y: 10 N: 0 Abstain: 2 Motion Passes

## Slide 22: .11az Negotiation
Performed with one of more discovered Responders
Initial FTM Request contains:
  Trigger
  [FTM , NGP] Parameters element contain proposed parameters to execute FTM, VHTz or HEz Ranging protocols
  Location Civic and/or LCI Request elements
Initial FTM frame contains
  Responder’s LCI, location civic if iFTMR included corresponding request elements
  A Neighbor List if iFTMR included a Neighbor Report Request element
  Either FTM or NGP Parameters to execute the Ranging protocol chosen by the responder
    NGP Parameters element includes a ranging protocol specific subelement

## Slide 23: How does all this work? -- an example
STA discovers ranging capability of the environment
  STA listens to Beacons from a set of Responders
  STA selects a subset based on the ranging capabilities supported by each of the Responders
STA initiates Negotiation with one or more of the discovered responders
STA executes the negotiated Ranging protocol with one or more of the responders with which it successfully completed the negotiation