## Slide 1: CCA Sensitivity
Date: 2018-01-15

## Slide 2: Abstract
All OFDM-based PHYs in 2.4 GHz and 5 GHz have the same basic requirement for CCA sensitivity, though with significantly different surrounding definitions.
There are some problems: the definitions are unsatisfactory in various ways, especially for the case where there is significant interference.
This presentation outlines the problems and proposes an outline of the form of a solution.
CIDs addressed: 77

## Slide 3: HT CCA requirements—HT and ERP PPDUs
“CCA requirements for non-HT PPDUs in the primary channel are described in 17.3.10.6 (CCA requirements) and 18.4.6 (CCA performance).”
“For an HT STA with the operating channel equal to 20 MHz, the start of a valid 20 MHz HT PPDU at a receive level greater than or equal to the minimum modulation and coding rate sensitivity of 82 dBm shall cause the PHY to set PHY-CCA.Indication(Busy) with probability > 90% within 4 ms.”
—TGmd draft 0.1, sections 19.3.19.5.2, .3 (pp. 2579-80)

## Slide 4: HT CCA requirements—questions
Questions:
Do these requirements apply to PPDUs received over the air?
Do these requirements apply in the presence of interference?
The current text is clear: the answer to both questions is Yes
The requirements are worded as blanket statements, without exclusions or restrictions
Thus, if there exists any combination of circumstances (interference, multipath) under which a device does not detect the start of a valid 20 MHz HT PPDU with probability > 90%, the device is not compliant with the IEEE specification

## Slide 5: HT CCA requirements—comments
It seems that this requires the impossible:
Net interference can be up to –62 dBm without triggering ED
So the SINR may be as low as –20 dB

## Slide 6: VHT CCA requirements—VHT PPDU
“CCA sensitivity
… in an otherwise idle … channel …
“With >90% probability, the PHY shall detect the start of a PPDU that occupies at least the primary 20 MHz of the channel under the conditions listed in Table 21-27 … within a period of aCCATime … and hold the CCA signal busy … for the duration of the PPDU.”
“The start of a 20 MHz NON_HT PPDU in the primary 20 MHz channel as defined in 17.3.10.6 (CCA computation)
“The start of an HT PPDU under the conditions defined in 19.3.19.5 (CCA sensitivity)
“The start of a 20 MHz VHT PPDU in the primary 20 MHz channel at or above -82 dBm”
—TGmd draft 0.1, section 21.3.18.5 (p. 2772)

## Slide 7: VHT CCA requirements—questions
Questions:
Do these requirements apply to PPDUs received over the air?
Do these requirements apply in the presence of interference?
For the first question, the current text is unclear
“For tests in this subclause, … [e]ach output port of the transmitting STA shall be connected through a cable to one input port of the Device Under Test”
  —TGmd draft 0.1, section 21.3.18 (p. 2769) (emphasis added)
For the second question, the current text is clear: the answer is No
“… in an otherwise idle … channel”

## Slide 8: VHT CCA requirements—comments
If we interpret all Clause 21.3.18 requirements as defined under cabled conditions (which seems to be the intention), then there are essentially no requirements to detect VHT preambles over the air
A device that measures channel activity and, if interference is detected, applies its own discretion for CCA is compliant with the IEEE specification—at least if a VHT PPDU is received
But we don’t even benefit from the relaxed requirement, because if a non-VHT PPDU is received, then the requirements of Clauses 17, 18, or 19 apply: if any combination of interference and channel result in probability of detection < 90%, the device is not compliant with the IEEE specification
  In any case, a VHT STA is also an HT STA, etc.

## Slide 9: Summary and candidate solution
A characterization of the problem:
  Deployed devices seem to work just fine—the problem is bringing the specification into alignment with normal behaviour
  The “spirit” of the current -82 dBm threshold should be maintained, while not giving devices an impossible task
  This is tricky, because interference in its most general forms cannot be assumed to fit any given model (unlike thermal noise in the receiver)
Candidate solution:
  Require initial CCA busy if RSSI > -82 dBm and a reference detector would detect the beginning of a VHT/HT/etc. PPDU within 4 ms (> 90%)
    Reference detector an autocorrelator with given bitwidth, with suitably low a priori probability of signal present (to provide implementation margin)
  Change each of clauses 17, 19, 21 accordingly (& require for all PPDUs)

## Slide 10: Straw poll
Clearly there isn’t time to specify this fully before the end of this week
A comment will be submitted in the letter ballot
In the meantime, it would be useful to have a
Straw poll
Do you agree with the solution outline described in slide 9?
  Yes
  No
  Unsure / need more information / abstain