## Slide 1: Issues for clarification related to “paused COT” in EN 301 893
16 October 2017
Authors:
Name | Company | Phone | email
Matthew Fischer | Broadcom |  | matthew.fischer@broadcom.com
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: EN 301 893 should be clarified so it is clear a device can only make a single attempt to access a “paused COT”
Situation?
EN 301 893 includes a “paused COT” feature that allows a UE to continue an eNB’s COT after a pause
Complication?
There is contention in 3GPP RAN1 on the meaning of the rules related to the “paused COT”
Answer?
The correct interpretation is that a device can only make a single attempt to access a “paused COT”
Next steps?
EN 301 893 should be clarified so it is clear a device can only make a single attempt to access a “paused COT”

## Slide 3: EN 301 893 includes a “paused COT” feature that allows a UE to continue an eNB’s COT after a pause
  EN 301 893 includes an adaptivity clause that specifies an LBT mechanism that is mostly aligned with EDCA in 802.11
  One difference is that it allows a “paused COT” (COT = Channel Occupancy Time, like a TxOP)
    An initiating device obtains a COT in the normal way using LBT mechanism
      Specified in EN 301 893, clause 4.2.7.3.2.6
    The initiating device may authorise a responding device to continue the COT
      Specified in EN 301 893, clause 4.2.7.3.2.7 & with COT lengths in 4.2.7.3.2.4
    The COT continuation can occur immediately, after at most 16us
      This mode is often used by 802.11
    The COT continuation can occur after a pause
      This feature was put in place to account for a problem that LAA UEs, unlike 802.11 devices, cannot respond immediately to a grant from an eNB
      The general idea is that the eNB will specify a grant to the UE at a particular time, but the UE must execute a 25µs LBT before taking up the grant
      If the medium is not free at the grant time then the grant is lost

## Slide 4: The key elements of the “paused COT” are specified in EN 301 893, clause 4.2.7.3.2.7

## Slide 5: The length of COTs that are paused is specified in EN 301 893, clause 4.2.7.3.2.4
Note: Table 8 contains similar rules for Supervised Devices

## Slide 6: There is contention in 3GPP RAN1 on the meaning of the rules related to the “paused COT”
  There have been discussions in 3GPP RAN1 about the interpretation of the “paused COT” feature
  It is reported that some RAN1 participants have plans to allow a UE (in Releases 14 & 15) to make multiple attempts to extend a “paused COT”
    A eNB issues multiple grants to share a COT to the same UE
    The UE then attempts to gain access using the 25µs LBT mechanism at each grant time
    If the UE fails at the first grant time, then it retries at subsequent grant times
  It is also reported that that other RAN1 participants believe that a UE can only make a single attempt to extend a “paused COT”
    A eNB issues a single grant to share a COT to a particular UE
    The UE then attempts to gain access using the 25µs LBT mechanism
    If the UE fails at the grant time, it then loses the grant and must wait for the eNB to send it another grant

## Slide 7: The correct interpretation is that a device can only make a single attempt to access a “paused COT”
Reasons
  Reason 1: the text as written is clear that only a responding device can only make a single attempt to access a “paused COT”
  Reason 2: the multiple attempt interpretation allows access at any time and any number of times, which is not the intent
  Reason 3: discussion in ETSI BRAN at the time highlighted that only a single grant per device was intended

## Slide 8: The correct interpretation is that a device can only make a single attempt to access a “paused COT”
Reason 1: the text as written is clear that only a responding device can only make a single attempt to access a “paused COT”
  The text in 4.2.7.3.2.7 is clear in that an initiating device can only send a single grant to a responding device
    The first paragraph refers to a singular authorisation per responding device
    The first paragraph equates an authorisation to a grant
  The text in 4.2.7.3.2.7 is relatively clear in that a responding device can only receive a single grant from an initiating device
    1) refers only to a single grant
    It is possible that this text refers to each example of a grant, but this is unlikely as there is no evidence elsewhere of the possibility of multiple grants to a responding device

## Slide 9: The correct interpretation is that a device can only make a single attempt to access a “paused COT”
Reason 2: the multiple attempt interpretation allows access at any time and any number of times, which is not the intent
  Suppose the rules in EN 301 893 allowed initiating device to authorise a responding device to retry attempts to access a “paused COT” by sending multiple grants
  Now suppose those multiple grants were for access every 1ns
    While this is not possible for LAA for other reasons, EN 301 893 is written to be technology neutral and so what LAA can do is not relevant
  This would mean that the responding device could have access to the medium at any time it could find the medium free for 25µs
    “any time” is constrained by other rules in 4.2.7.3.2.4 related to “paused COTs”
  It is clearly not the intent of the text in EN 301 893 to provide access to the medium at any time

## Slide 10: The correct interpretation is that a device can only make a single attempt to access a “paused COT”
Reason 3: discussion in ETSI BRAN at the time highlighted that only a single grant per device was intended
  The inclusion of the “paused COT” was agreed in ETSI BRAN in December 2015
  It was suggested as a result a complaint by a LAA stakeholder that a UE could not share an eNB’s COT because LTE’s design meant the UE could not respond immediately to a grant
  During discussion of the “paused COT” it was made very clear that if the medium was not free at the grant time, the single grant was lost
    A Wi-Fi stakeholder explained multiple times that the UE would only have one opportunity at the grant time; he also asserted the LAA stakeholders were “nuts” (direct quote) for proposing a solution that did not appear to be helpful to LAA
    The LAA stakeholders all acknowledged the situation and stated the feature was useful and acceptable to LAA

## Slide 11: EN 301 893 should be clarified so it is clear a device can only make a single attempt to access a “paused COT”
  An interpretation of EN 301 893 to allow multiple grants per device to access a “paused COT” risks fair sharing
  As a starting point, ETSI BRAN should be asked to make it clear only a single grant per device is allowed