## Slide 1: Defense Against Multi-Channel Man-in-the-Middle (MITM)
Date: 2017-10-30
Authors:
Name | Affiliations | Address | Phone | Email
Nehru Bhandaru | Broadcom Ltd. | 190 Mathilda Place, Sunnyvale, CA 94086 | +1 408 922 5924 | nehru.bhandaru@broadcom.com
Thomas Derham | Broadcom Ltd. |  |  | thomas.derham@broadcom.com
Mathy Vanhoef | KU Leuven |  |  | mathy.vanhoef@cs.kuleuven.be

## Slide 2: Introduction
Recent IV Reset attacks against 802.11 RSN
  Mathy Vanhoef Paper
      CVE-2017-12968, CVE-2017-13077 CVE-2017-13079 CVE-2017-13080 CVE-2017-13081 CVE-2017-13084 CVE-2017-13086 CVE-2017-13087 CVE-2017-13088
  Other exchanges (e.g. FTM, FILS) can be attacked
Attacker relays frames
  Channel based MITM
  Masquerades as STA against legitimate AP on Channel A
  Masquerades as AP against legitimate STA on Channel B
Generic defense against MITM requires
  Authentication
  Verification of protocol attributes
Need protocol robustness against generic multi-channel attacks
‹#›

## Slide 3: Channel-based MITM
‹#›
Attacker
AP
Attacker
STA
AP
STA
Channel A
Channel B
PTK/GTK Handshake, FTM
PTK/GTK Handshake, FTM
Attacker
uses AP MAC address on Channel A, STA MAC address on Channel B
relays frames between AP and STA
may buffer frames, drop ACKs and cause retransmissions

## Slide 4: Possible RSN defense for multi-channel MITM
Advertise operating channel validation in RSNE
  Capability OCVC, Policy OCVR (Required)?
Add operating channel information to RSN handshakes
  Similar to RSNE to protect against cipher downgrade
  Operating Channel Information (OCI) KDE
    Country, Operating Class, Channel Number or their Hash
OCI KDE, under MIC protection included in
  M2 and M3 of 4-way handshake
  G1 and G2 of GTK handshake
Receiver compares current operating channel information with that received in KDE
  Discard on mismatch if OCVC peer
  Discard on absence if OCVR device
‹#›

## Slide 5: Related Topics - FT, FILS, FTM
Do FT handshakes need this protection?
  Initial FT association uses 4-way handshake
  Reassociation MIC does not include channel information
    VHT/HT Operation Elements from AP → non-AP STA
      Non-HT ? non-AP STA→ AP
    Include channel information as optional Subelement in FTE
      FTE is already validated via MIC
      Channel information needs to be validated if OCVC
Do FILS handshakes need this protection?
  Association frames protected by MIC
  EAPOL frames protected by AEAD
    Include channel information KDE
No change to FTE in TPK handshake
Should 11az provide this protection?
  Authenticate channel information along with LMR feedback?
‹#›

## Slide 6: Related Topics - Channel Switch
Channel switch during 4-way or GTK handshake?
  Unlikely, but M1 and M4 need to be validated to be on the same channel as M3 and M2 respectively
BSS Transition okay
  FT Action is protected
  Reassociation and key confirmation
Channel Switch Announcements
  Beacons, Unprotected or Protected Dual of Public Action
  Recommend using Protected announcements
  Attacker may block even protected CSA and assume MITM position
    Attack window open until next handshake
    When peer STA supports OCVC initiate an SA Query?
      SA Query and Response frame extension to include channel information
      Channel information validation on SA query receipt
      Disassociate if validation fails
‹#›

## Slide 7: Related Topic - Same Channel MITM
AP and STA are within range of each other
  Hard to attack reliably
  Buffering and replay not effective
AP and STA are out of range, but in range of the attacker
  Is there anything that can be done here?
‹#›

## Slide 8: Strawpoll(s)
802.11 specification should define a mechanism to protect against multi-channel MITM
Y: N: A:
RSNE should advertise operating channel validation capability and policy
Validation: Require: None:
Operating channel information should be included and MIC protected in RSN key exchanges - Pairwise and Group Key handshakes
Y: N: A:
Operating channel information should consist of one of
  Country, Operating Class and Channel(s)
  Hash of Operating Channel Information
  Other
‹#›