## Slide 1: WUR SYNC Preamble Design
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1][2], WUR preamble with two different SYNC sequences was proposed for data rate signaling as well as packet detection and timing synchronization
  No signaling field is required
On the other hand, [3] considered that WUR preamble consists of one type of SYNC filed (packet acquisition) and a signaling field (data rate indication)
Due to the additional signaling field, the proposal in [3] needs a longer packet than that in [1][2]
Whereas, the proposal in [1][2] needs to conduct cross-correlation twice at the receiver to identify what data rate is applied to the WUR payload part, and thus the receiver complexity may be high
In this contribution, we propose WUR preamble with two different SYNC sequences which requires to conduct cross-correlation only once
  As a consequence, we can achieve low receiver complexity and comparable overhead as well as reliable performance

## Slide 3: Proposal for Two SYNC Sequences (1/2)
In [4][5], SYNC sequences which have an equal number of ones and zeros were proposed based on MLS or Golay sequences
We propose to use one of them in [4][5] for SYNC1 and its complement sequence (i.e., 10, 01) for SYNC2
  SYNC1 and SYNC2 are used for the SYNC preamble in the WUR packet with the payload part’s data rate of 62.5Kbps and 250Kbps, respectively
By doing so, the receiver only needs to perform cross-correlation once by using either SYNC1 or SYNC2 in order to identify the data rate as well as detect the packet and recover timing
  Packet acquisition is determined by the maximum magnitude of the cross-correlator output
  Data rate for the payload part is determined by judging the sign of the cross-correlator output which has the maximum magnitude

## Slide 4: Proposal for Two SYNC Sequences (2/2)
For example, consider the following case
  SYNC1: [1 0 0 1]
  SYNC2: [0 1 1 0]
  Receiver conducts cross-correlation by using SYNC1 sequence with changing ‘0’ to ‘-1’, i.e., [1 -1 -1 1] (SYNC1)
  Cross-correlation between SYNC1 and SYNC1 with the maximum magnitude: 2
  Cross-correlation between SYNC2 and SYNC1 with the maximum magnitude: -2
  The maximum magnitude is the same but the sign is different
  By using this property, we can indicate the data rate and acquire timing at the same time

## Slide 5: Simulation Assumption
WUR packet
  SYNC: 32 length MLS sequence with 4us bit duration
    SYNC1 for 62.5Kbps in [5]
    [0,1,0,0,0,0,1,0,1,0,1,1,1,0,1,1,0,0,0,1,1,1,1,1,0,0,1,1,0,1,0,0]
    SYNC2 for 250Kbps
    [1,0,1,1,1,1,0,1,0,1,0,0,0,1,0,0,1,1,1,0,0,0,0,0,1,1,0,0,1,0,1,1]
  Payload: 48 symbols
Cross-correlation at the receiver
  Cross-correlation between undersampled (i.e., 4MHz sampling) ED values and SYNC1
    SYNC1 is computed by changing ‘0’ to ‘-1’ of SYNC1 sequence and aligning the sequence length with the sampling rate
Others are shown in Appendix A
Legacy Preamble
A BPSK Symbol
SYNC
Payload

## Slide 6: False Alarm and Miss Detection
CCDF and CDF of the maximum magnitude of the cross-correlator output during 2ms in both TGnD and UMi NLoS channels
  Cross-correlation between SYNC1 and only noise during 2ms for false alarm rate
  Cross-correlation between SYNC1 and noise + WUR packet during 2ms for miss detection rate at -3dB SNR
  We do not see difference between the miss detection rates for WUR packets with SYNC1 and SYNC2 in both TGnD and UMi NLoS channels
  Although the receiver performs cross-correlation using only SYNC1, our proposal does not cause any problem on timing acquisition
TGnD channel
UMi NLoS channel

## Slide 7: Threshold for Detection and Timing
To achieve the false alarm rate of 1%, the following threshold is considered for further simulation
  Note that the threshold comes from the false alarm rate which is only dependent on the noise and the noise variance is set to 1 in the simulation
  Whatever SYNC preamble (either SYNC1 or SYNC2) the packet consists of, the miss detection rate is the same at a given threshold in each channel
 | TGnD | UMi NLoS
Threshold for packet acquisition | 25.7 | 25.7
Miss Detection Rate at -3dB SNR | 10% | 7%

## Slide 8: Simulation Results for 62.5Kbps (SYNC1)
TGnD channel
UMi NLoS channel
Miss Probability : the maximum magnitude of the cross-correlator output is lower than the threshold
Signaling Error Rate : the sign of the cross-correlator output which has the maximum magnitude is –
PER w/ real timing : Miss Probability + Signaling Error Rate + Payload Packet Error Rate

## Slide 9: Simulation Results for 250Kbps (SYNC2)
TGnD channel
UMi NLoS channel
Miss Probability : the maximum magnitude of the cross-correlator output is lower than the threshold
Signaling Error Rate : the sign of the cross-correlator output which has the maximum magnitude is +
PER w/ real timing : Miss Probability + Signaling Error Rate + Payload Packet Error Rate

## Slide 10: Comparison among Various SYNC Proposals
 | One SYNC + Signaling field [3] | Two SYNCs [1][2] | Our Proposal
Receiver Complexity | Medium (one cross-correlator + signaling field decoder) | High (two cross-correlators*) | Low (one cross-correlator)
Overhead (Packet Length) | High | Medium (62.5Kbps) Low (250Kbps) Medium (overall)** | Medium
Packet & Timing Acquisition | Similar and comparable performance except SYNC2 in [1][2] |  | 
Data Rate Signaling | Worse than other proposals | Similar and good performance | 
* Assuming SYNC2 has a half length of SYNC1, maximum 50% increase in computational complexity compared to one cross-correlator
** Please see Appendix C

## Slide 11: Conclusion
We have proposed two SYNC sequences for data rate signaling
  SYNC1 and SYNC2 have an equal number of zeros and ones with good auto-correlation property (such as MLS and Golay) and SYNC2 is the complement sequence of SYNC1
Receiver is required to conduct cross-correlation using only SYNC1 sequence (SYNC 1)
  We don’t see any problem on packet and timing acquisition because there is no difference between miss detection rates for PPDU with SYNC1 and SYNC2
Receiver can identify the data rate applied to the payload part according to the sign of the cross-correlator output which has the maximum magnitude
  Data rate signaling error is very low
We have showed that PER performance is comparable

## Slide 12: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  For data rate indication, 11ba uses two different SYNC sequences
Y/N/A :

## Slide 13: Straw Poll #2
Do you agree to add the following to the 11ba SFD?
  Two different SYNC sequences have the same size
    The size is TBD
Y/N/A :

## Slide 14: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  11ba uses two SYNC sequences as follows
    SYNC1 and SYNC2 are used for 62.5Kbps and 250Kbps, respectively
    SYNC1 and SYNC2 have an equal number of ones and zeros
    SYNC2 is the complement sequence of SYNC1 i.e., it is computed by changing coefficients of SYNC1 from ‘1’ to ‘0’ and from ‘0’ to ‘1’
      Specific coefficients, sequence length and bit duration are TBD
Y/N/A :

## Slide 15: References
[1] IEEE 802.11-17/1343r0 WUR Preamble SYNC Field Design
[2] IEEE 802.11-17/1345r5 11ba PHY Frame Format Proposal
[3] IEEE 802.11-17/1326r0 Signature Sequence Follow-up
[4] IEEE 802.11-17/1352r0 Consideration on WUR SYNC Preamble
[5] IEEE 802.11-17/1355r1 WUR Preamble Evaluation

## Slide 16: Appendix

## Slide 17: Appendix A – Simulation Assumptions
No CFO, Phase noise applied
Butterworth filter
  2.5MHz cut off frequency, second order
4MHz sampling rate
TGnD and UMi NLoS channels in 2.4GHz
SNR defined in 20MHz
OOK symbol generated by the 13-length sequence which is optimal in terms of the PAPR

## Slide 18: Appendix B – Simulation Results for Golay Sequence Based Preamble (1/3)
SYNC1 for 62.5Kbps in [4]
  [1,1,1,1,1,0,1,0,0,0,1,1,1,0,0,1,1,1,0,0,1,0,0,1,0,0,0,0,1,0,1,0]
SYNC2 for 250Kbps
  [0,0,0,0,0,1,0,1,1,1,0,0,0,1,1,0,0,0,1,1,0,1,1,0,1,1,1,1,0,1,0,1]
False Alarm and Miss Detection
TGnD channel
UMi NLoS channel

## Slide 19: Appendix B – Simulation Results for Golay Sequence Based Preamble (2/3)
TGnD channel
UMi NLoS channel
Miss Probability : the maximum magnitude of the cross-correlator output is lower than the threshold
Signaling Error Rate : the sign of the cross-correlator output which has the maximum magnitude is –
PER w/ real timing : Miss Probability + Signaling Error Rate + Payload Packet Error Rate
62.5Kbps

## Slide 20: Appendix B – Simulation Results for Golay Sequence Based Preamble (3/3)
Miss Probability : the maximum magnitude of the cross-correlator output is lower than the threshold
Signaling Error Rate : the sign of the cross-correlator output which has the maximum magnitude is +
PER w/ real timing : Miss Probability + Signaling Error Rate + Payload Packet Error Rate
250Kbps
TGnD channel
UMi NLoS channel

## Slide 21: Appendix C – Overhead Comparison
We consider the following case Shahrnaz suggested for Simulation Scenario and Evaluation Methodology Document
  A case with 60 WURs which receives unicast wake-up packet every 30 minute and a WUR beacon every 10 seconds transmitted at the lowest data rate
We further assume that the chances of unicast wake-up packet with 62.5Kbps and 250Kbps are even
Then, there are 420 (360 for beacon / 60 for unicast) and 60 (unicast only) transmissions per an hour for wake-up packet with 62.5Kbps and 250Kbps, respectively
Preamble and payload (48 bits) lengths are considered as follows
Hence, total overheads per an hour are 391.68ms (896us*420+256us*60) and 395.52ms (896us*420+320us*60) for two syncs in [1], [2] and our proposal, respectively
  The overhead gain for two syncs in [1], [2] is negligible (only 1.1% gain)
 | 62.5Kbps |  |  | 250Kbps |  | 
 | Preamble | Data | Total | Preamble | Data | Total
Two syncs in [1], [2] | 128us | 768us | 896us | 64us | 192us | 256us
Our proposal | 128us | 768us | 896us | 128us | 192us | 320us