## Slide 1: Symbol Structure Follow-up
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In our previous contribution [1], various symbol structures for data rates of both 62.5Kbps and 250Kbps were investigated
For the data rate of 62.5Kbps, we compared the performance between the symbol structures of ON+ON+OFF+OFF and ON+OFF+ON+OFF for TGnD and UMi channels
Even though we verified that the ON+ON+OFF+OFF structure can overcome large delay spread, some members expressed their concerns about the coexistence problem of this structure

## Slide 3: Coexistence Problem
802.11 and non-802.11 devices can perform transmission after sensing the channel to be idle during a certain duration T
  802.11 devices use DIFS or AIFS or EIFS before transmission
  LAA uses minimum 25us before transmission [2]
WUR packet with ON+ON+OFF+OFF structure for 62.5Kbps can have a 16us OFF-duration and some members thinks it can have coexistence problem
  Transmit power limitation or a deep fading channel can lead to a low received power even for the ON-duration, and thus it is possible that a longer OFF-duration can be caused at some receivers
  Also, it is possible that a certain range including 16us OFF-duration has a low average energy which is below a certain threshold (e.g. energy detection level)
  In this case, some devices can determine that the channel is idle for the duration of T, and then can perform backoff procedure
    Some of them can send a signal and consequently interrupt WUR packet transmission

## Slide 4: ON+OFF+ON+OFF Structure
On the other hand, WUR packet which consists of ON+OFF+ON+OFF structure has just a maximum 8us OFF-duration, and thus it is much less probable that receivers determine the channel to be idle during T
As for the performance, even though its performance is worse than that of ON+ON+OFF+OFF for the UMi NLoS channel, the performance gap is small (within 1dB) at 10% PER as shown in [1]
  Also, if the null CP is applied, the gap further decreases
  For the TGnD channel, their performance is similar
Hence, the symbol structure of ON+OFF+ON+OFF may be a good candidate for the data rate of 62.5Kbps in consideration of the coexistence issue as well as its comparable performance

## Slide 5: Straw Poll #1
Do you agree to add the following to the 11ba SFD?
  Symbol structure of the data rate of 62.5Kbps for each information is as follows
    4us ON signal has always energy
Y/N/A : 30/0/10
Information 0 | Information 1
4us ON + 4us OFF + 4us ON + 4us OFF | 4us OFF + 4us ON + 4us OFF + 4us ON

## Slide 6: Motion
Move to add the following to the 11ba SFD
  Symbol structure of the data rate of 62.5Kbps for each information is as follows
    For 4us ON-signal, there is always energy
Move : Eunsung Park
Second :
Y/N/A :
Information 0 | Information 1
4us ON + 4us OFF + 4us ON + 4us OFF | 4us OFF + 4us ON + 4us OFF + 4us ON

## Slide 7: References
[1] IEEE 802.11-17/1347r3 Symbol Structure
[2] IEEE 802.11-16/1114r0 Coexistence Mechanism for Wakeup Radio Signal