## Slide 1: 13-Length Sequence for OOK Waveform Generation
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In our previous contribution [1], we dealt with various 13-length sequences which are applied to 13 subcarriers to generate OOK waveform of wake-up packet
However, any sequence was not approved by the group
  Each member had a different preference on the sequence and some members even thought that the sequence does not need to be defined in the spec since it may not affect the receiver behavior
In this contribution, we present reasons why the 13-length sequence needs to be defined in the 11ba spec
Finally, we propose the 13-length sequence

## Slide 3: Reasons for Defining 13-Length Sequence
If the choice of the 13-length sequence is considered as the implementation issue, the OOK waveform of each WUR transmitter can be different and this leads to a variable performance for WUR
This makes it hard for the group to determine details of OOK symbols or preamble structures
Also, this blocks the possibility that the receiver exploits the actual transmitted waveform when conducting cross-correlation for better detection and timing recovery
Furthermore, when we consider and define an advanced WUR in the future, a variable waveform of 11ba will cause complex problems (e.g. coexistence, packet classification)
Thus, it is advisable to define the 13-length sequence which characterizes the OOK waveform

## Slide 4: 13-Length Sequence (1/2)
In [1], we presented various options as follows
  Option 1 : Optimized sequence in terms of the PAPR
    [1,1,1,-1,-1,-1,0,-1,1,-1,-1,1,-1]
  Option 2 : Reuse the conventional L-STF sequence by choosing coefficients at tones of all multiples of 4 from -24 to 24 [2]
    [1,-1,1,-1,-1,1,0,-1,-1,1,1,1,1] * (1+j)/sqrt(2)
  Option 3 : Reuse the conventional L-LTF sequence by choosing coefficients at tones from -6 to 6 [3]
    [1,-1,1,1,1,1,0,1,-1,-1,1,1,-1]
  Option 4 : Optimized sequence in terms of the average power between CP and signal portions (similar average power between them) [4]
    [-1,-1,-1,1,1,-1,0,-1,-1,-1,1,-1,1]

## Slide 5: 13-Length Sequence (2/2)
We propose to use option 1 or option 2 which have low PAPR
  High PAPR can lead to that the signal passes through a nonlinearity region of power amplifier which results in a serious performance degradation
  PAPR reduction can enhance the efficiency of power amplifier and reduce the implementation cost
If it is premature to determine the sequence and we need further investigation, we suggest at least to use a null center tone whatever the location of 13 subcarriers
  In consideration of the adjacent channel interference, it is good to place 13 subcarriers on the center of 20MHz
  In this case, the center tone of 13 subcarriers is located at DC of 20MHz, and thus we need a certain sequence with a null center tone
  On the other hand, we can also avail of multiple 4MHz channels within each 20MHz bandwidth for flexibility and choose one of them for wake-up packet transmission
  Even in this case, we propose to use the same 13-length sequence (i.e., a null center tone) for simplicity and unification of the 13-length sequence

## Slide 6: Conclusion
We have presented the reasons why the 13-length sequence needs to be defined in the 11ba spec
We have proposed to use the sequence which has low PAPR or at least use a null center tone regardless of the location of 4MHz bandwidth

## Slide 7: Straw Poll #1
Do you agree to define the 13-length sequence which is applied to 13 subcarriers to generate the OOK waveform of WUR PPDU in the 11ba spec?
Y/N/A : 10/8/25

## Slide 8: Straw Poll #2
Do you agree to modify the text in the 11ba SFD as follows?
  R.3.3.C: When a single band is used for transmission of WUR PPDU, the OOK waveform of WUR PPDU is generated by using contiguous 13 subcarriers with the subcarrier spacing of 312.5 kHz:
    The center subcarrier is TBD null.
Y/N/A : 19/0/15

## Slide 9: Straw Poll #3
Do you agree to add the following to the 11ba SFD?
  The following sequence is applied to 13 subcarriers to generate OOK waveform
    [1,1,1,-1,-1,-1,0,-1,1,-1,-1,1,-1]

## Slide 10: Motion
Move to modify the text in the 11ba SFD as follows
  R.3.3.C: When a single band is used for transmission of WUR PPDU, the OOK waveform of WUR PPDU is generated by using contiguous 13 subcarriers with the subcarrier spacing of 312.5 kHz:
    The center subcarrier is TBD null.
Move : Eunsung Park
Second : Suhwook Kim
Y/N/A : 22/0/10

## Slide 11: References
[1] IEEE 802.11-17/0964r4 Signal Bandwidth and Sequence for OOK Signal Generation
[2] IEEE 802.11-17/0656r0 WUR PHY Performance Study with Phase Noise and ACI
[3] IEEE 802.11-17/373r1 Performance Investigations on Single-carrier and Multiple-carrier-based WUR
[4] IEEE 802.11-17/0676r1 WUR Link Budget Analysis Follow-up : Data Rates and SIG Bits Protection