## Slide 1: Dual Sync Designs
Date: 2017-11-03
Authors:

## Slide 2: Goals
Two Sync Designs: Short and Long
The Short Sync is used with the High Data rate
The Long Sync is used with the Low Data rate
In one design the Sync for the High and Low data rates are the same duration (but we still use “Long” and “Short” for consistency)
Based on previous simulations [1] a Long sync duration of 128 µs is sufficient. We expect that we can use a shorter duration for the high data rate given the higher SNR
The design of these Dual Syncs must support three requirements
  Packet Detection
  Symbol Timing Recovery
  Identification of Sync type (short or long) to indicate the data rate of the Data Field

## Slide 3: Correlation Metrics
Introduce auto and cross correlation metrics for the Long and Short Sequences, like in [2]. The larger the metric the lower the false alarm rate and the better the timing estimate
Autocorrelation Metric
Where is the sequence output of the Short Sync Detector with an input of a Short Sync
Similar definition for
Cross Correlation Metric
Where is the sequence output of the Short Sync Detector with the input of a Short Sync and is the sequence output of the Short Sync Detector with the input of a Long Sync
Similar definition for

## Slide 4: Design Summary
Will Show Three Sync Designs
Equal Duration Sync Fields for High and Low Data Rates
  1. Equal Duration Sync Fields
Unequal Duration Sync Fields for High and Low Data Rates
  2. Dual Correlators and Aggregator
  3. Correlator and Dual Aggregators

## Slide 5: Equal Duration Sync Field Design
One approach to the dual sync designs is use two sequences of the same length, which are logical complements of one another
Let S = [0, 1, 1, 1, 0, 1, 0, 1, 0, 0, 0, 0, 1, 0, 0, 1, 0, 1, 1, 0, 0, 1, 1, 1, 1, 1, 0, 0, 0, 1, 1, 0]
  Here indicates the bit-wise logical complement of
  In this design the Long Sync and Short Sync are the same duration. We will call them Long and Short to be consistent with other designs in this presentation
The Sync Bit duration in this case is 4 µs
The duration of both the Long Sync and the Short Sync is 128 µs

## Slide 6: Equal Duration Sync – Correlation Metrics
Metric | Value
ACMetric(Short) | 5.3
CCMetric(Short, Long) | 8
ACMetric(Long) | 5.3
CCMetric(Long, Short) | 8
Correlation Plots provided in Backup

## Slide 7: Simulation
Receiver Sampling Rate = 4 MHz
Data Field Low Data Rate = 62.5 kb/s
  One
  Zero
Data Field High Data Rate = 250 kb/s
  One
  Zero
  No BCC
Normalized the correlator output, dividing by the average signal power
Sync Detection False Alarm rate = over 2 ms interval
Data field is 100 bits
Simulated both
  Ideal Sync Detection and Timing
  Real Sync Detection and Timing

## Slide 8: Equal Duration Sync – PER Sim: Low Rate, Model D
AWGN and UMi PER plots provided in Backup
Loss due to real Sync Detection and Timing = 0.87 dB

## Slide 9: Equal Duration Sync – PER Sim: High Rate, Model D
Loss due to real Sync Detection and Timing = 0.40 dB

## Slide 10: Equal Duration Sync – Computational Complexity
Parameter | Value
Duration of Correlator (µs) | 128
Sampling Rate (MHz) | 4
Length of Correlator (Samples) | 512
Number of Adds each Sample Time | 512
Number of Adds Per Second | 2048 Million

## Slide 11: Unequal Duration Sync – Dual Correlators and Aggregator
2 µs Sync Bit Duration
16-bit sequence and 16-bit Sequence
The
  Duration of Short Sync is 32 µs
The
  Duration of Long Sync is 128 µs
Select and to have good autocorrelation and cross correlation properties between Long and Short Sync Designs

## Slide 12: Dual Correlator/Aggregator – Correlation Metrics
Metric | Value
ACMetric(Short) | 8
CCMetric(Short, Long) | 4
ACMetric(Long) | 4
CCMetric(Long, Short) | 8
Correlation Plots provided in Backup

## Slide 13: Dual Correlator/Aggregator – PER Sim: Low Rate, Model D
Loss due to real Sync Detection and Timing = 1.01 dB

## Slide 14: Dual Correlator/Aggregator – PER Sim: High Rate, Model D
Loss due to real Sync Detection and Timing = 1.28 dB

## Slide 15: Dual Correlator/Aggregator – Sync Detection
The Short Sync is just the sequence and hence can be detected at the output of the correlator
The Long Sync consists of a concatenation of versions of and
The Long Sync can be detected by combining delayed version of the and correlator output, in what we call an Aggregator (it aggregates peaks out of the correlators)

## Slide 16: Dual Correlator/Aggregator – Low Complexity Long Sync Detector

## Slide 17: Dual Correlator/Aggregator – Aggregator
and are 16 bit long. Each bit is 2 µs in duration
Hence and are each 32 µs in duration
For 4 MHz sampling that corresponds to 128 samples

## Slide 18: Dual Correlator/Aggregator– Computational Complexity
Parameter | Value
Duration of S Correlator (µs) | 32
Sampling Rate (MHz) | 4
Length of S Correlator (Samples) | 128
Number of Adds in S Correlator | 128
Number of Adds in T Correlator | 128
Number of Adds in Aggregator | 4
Total Number of Adds Per Sample Time | 260
Number of Adds Per Second | 1040 Million

## Slide 19: Unequal Duration Sync – Correlator plus Dual Aggregator: Design Approach
Here we use a sequence with good correlation properties
We also have a short sequence for padding which we call
The short and long preambles are constructed by concatenating replicas of its complement , or the padding sequence
The benefit of this approach is to use a correlator for at the receiver, for detecting both the short and long preambles, to minimize power consumption and complexity at the receiver
The use of the pad bits , provide a different spacing between the correlator output peaks for the long and short syncs

## Slide 20: Correlator/Dual Aggregators
2 µs Sync Bit Duration
The Short Sync will be selected to be shorter than the Long Sequence
We will select a 2 µs Sync Bit Duration to allow for the use of more bits in the Sync compared to 4 µs Sync bit duration
We will select a 8-bit sequence for
Padding Sequence is
The
  Duration of Long Sync is 128 µs
The
  Duration of Short Sync is 56 µs

## Slide 21: Correlator/Dual Aggregators – Correlation Metrics
Metric | Value
ACMetric(Short) | 3
CCMetric(Short, Long) | 3
ACMetric(Long) | 6.4
CCMetric(Long, Short) | 5.3
Correlation Plots provided in Backup

## Slide 22: Correlator/Dual Aggregators – PER Sim: Low Rate, Model D
Loss due to real Sync Detection and Timing = 1.01 dB

## Slide 23: Correlator/Dual Aggregators – PER Sim: High Rate, Model D
Loss due to real Sync Detection and Timing = 0.46 dB

## Slide 24: Correlator/Dual Aggregators – Sync Detector

## Slide 25: Correlator/Dual Aggregators – Long Aggregator
Sampling Rate = 4 MHz
Delay = 16 µs at 4 MHz = 64 samples

## Slide 26: Correlator/Dual Aggregators – Short Aggregator
Sampling Rate = 4 MHz
Delay = 20 µs at 4 MHz = 80 samples

## Slide 27: Correlator/Dual Aggregators – Computational Complexity
Parameter | Value
Duration of Correlator (µs) | 16
Sampling Rate (MHz) | 4
Length of Correlator (Samples) | 64
Number of Adds in Correlator | 64
Number of Adds in Long Aggregator | 8
Number of Adds in Short Aggregator | 3
Total Number of Adds Per Sample Time | 75
Number of Adds Per Second | 300 Million

## Slide 28: Comparison – Correlation Metrics
All three designs have high correlation metrics leading to low miss-classification rate
Design | Short Duration (µs) | Long Duration (µs) | Short AC Metric | Short CC Metric | Long AC Metric | Long CC Metric
Equal Duration | 128 | 128 | 5.3 | 8 | 5.3 | 8
Dual Correlators /Aggregator | 32 | 128 | 8 | 4 | 4 | 8
Correlator /Dual Aggregators | 56 | 128 | 3 | 3 | 6.4 | 5.3

## Slide 29: Comparison – Demodulation Performance
Design | Short Duration (µs) | Long Duration (µs) | Loss – Real Sync Detect Low Rate AWGN (dB) | Loss – Real Sync Detect High Rate AWGN (dB) | Loss – Real Sync Detect Low Rate Model D (dB) | Loss Real Sync Detect High Rate Model D (dB)
Equal Duration | 128 | 128 | 0.34 | 0.16 | 0.87 | 0.4
Dual Correlators /Aggregator | 32 | 128 | 0.32 | 0.90 | 1.01 | 1.28
Correlator /Dual Aggregators | 56 | 128 | 0.31 | 0.04 | 1.01 | 0.46
Long Sync duration of 128 µs gives around 1 dB loss (Model D), due to Sync detection and timing. To do better we would need to go to 256 µs, which is excessively long
Short Sync of 32 µs gives around 1 dB loss, while 56 µs gives around ½ dB loss. There seems to be no need to use 128 µs for the high data rate

## Slide 30: Comparison – Overhead and Complexity
Design | Short Duration (µs) | Long Duration (µs) | Complexity Million Adds Per Second
Equal Duration | 128 | 128 | 2048
Dual Correlators/Aggregator | 32 | 128 | 1040
Correlator/Dual Aggregators | 56 | 128 | 300
Design [3] | 64 | 128 | 1024
Design | Short Duration (µs) | Long Duration (µs) | Complexity Million Adds Per Second
Equal Duration | 128 | 128 | 2048
Dual Correlators/Aggregator | 32 | 128 | 1040
Correlator/Dual Aggregators | 56 | 128 | 300
Design [3] | 64 | 128 | 
The three designs covered in this presentation have satisfactory PER performance
The Dual Correlators/Aggregator and the Correlator/Dual Aggregators designs have both lower overhead and comparable or lower complexity than the Equal Duration design and the Design in [3]
Have not simulated the Design in [3]. The cross correlation metrics of the Long and Short is only 2 which is poorer than the other designs

## Slide 31: Summary
We recommend 128 µs Sync Field for the low data rate and a shorter duration (e.g. 32 or 56 µs) Sync Field for the high data rate
We recommend a structured sequence design for the long Sync Field to enable lower complexity implementations
All our designs have been simulated to demonstrate satisfactory performance

## Slide 32: Straw Poll #1
Do you support a Sync field duration of 128 µs for the low data rate?
Yes 30
No 0
Abstain 16

## Slide 33: Straw Poll #2
Do you support a Sync field duration less than 128 µs for the high data rate?
Yes 23
No 6
Abstain 17

## Slide 34: Straw Poll #2b
Do you support a Sync field duration less than or equal to 64 µs for the high data rate?
Yes 18
No 4
Abstain 23

## Slide 35: Straw Poll #3
Do you agree that the Long Sync Field design should be based on a hierarchal structured sequence to enable lower complexity implementation?
Note, examples of this approach are:
  Example 1: , as shown in Slide 11
  Example 2: As shown in Slide 20
  Example 3:
The exact structure is TBD
Yes 18
No 0
Abstain 36

## Slide 36: References
Steve Shellhammer, Bin Tian, Lochan Verma, “WUR Preamble Evaluation,” IEEE 802.11-17/1355r1, Sept 2017
Rui Cao, Hongyuan Zhang, “WUR Preamble SYNC Field Design,” IEEE 802.11-17/1343r0, Sept 2017
Shahrnaz Azizi, Juan Fang, Vinod Kristem, Thomas Kenney, “WUR Preamble Performance Study with Phase Noise and ACI,” IEEE 802.11-17/1442r1, Sept 2017

## Slide 37: Backup

## Slide 38: Equal Duration Sync – Long Sync Correlator Output
The Short Sync Correlator is the same as the Long Sync Correlator, we just look for negative peaks

## Slide 39: Equal Duration Sync – PER Sim: Low Rate, AWGN
Loss due to real Sync Detection and Timing = 0.34 dB

## Slide 40: Equal Duration Sync – PER Sim: High Rate, AWGN
Loss due to real Sync Detection and Timing = 0.16 dB

## Slide 41: Equal Duration Sync – PER Sim: Low Rate, UMi
Loss due to real Sync Detection and Timing = 0.97 dB

## Slide 42: Equal Duration Sync – PER Sim: High Rate, UMi
Loss due to real Sync Detection and Timing = 0.37 dB

## Slide 43: Dual Correlator/Aggregator – Long Sync Detector Output

## Slide 44: Dual Correlator/Aggregator – Short Sync Detector Output

## Slide 45: Dual Correlator/Aggregator – PER Sim: Low Rate, AWGN
Loss due to real Sync Detection and Timing = 0.32 dB

## Slide 46: Dual Correlator/Aggregator – PER Sim: High Rate, AWGN
Loss due to real Sync Detection and Timing = 0.90 dB

## Slide 47: Dual Correlator/Aggregator – PER Sim: Low Rate, UMi
Loss due to real Sync Detection and Timing = 1.10 dB

## Slide 48: Dual Correlator/Aggregator – PER Sim: High Rate, UMi
Loss due to real Sync Detection and Timing = 1.28 dB

## Slide 49: Correlator/Dual Aggregators – Long Aggregator Output

## Slide 50: Correlator/Dual Aggregators – Short Aggregator Output

## Slide 51: Correlator/Dual Aggregators – PER Sim: Low Rate, AWGN
Loss due to real Sync Detection and Timing = 0.31 dB

## Slide 52: Correlator/Dual Aggregators – PER Sim: High Rate, AWGN
Loss due to real Sync Detection and Timing = 0.04 dB

## Slide 53: Correlator/Dual Aggregators – PER Sim: Low Rate, UMi
Loss due to real Sync Detection and Timing = 1.09 dB

## Slide 54: Correlator/Dual Aggregators – PER Sim: High Rate, UMi
Loss due to real Sync Detection and Timing = 0.51 dB