## Slide 1: Consideration on WUR frame for Fast Scanning
Date: 2018-01-01
Authors:
Name | Affiliation | Address | Email
Li Nan | ZTE Corporation | No.9 Wu Xing Section Xi Feng Road Xi’an, Shaanxi Province P.R.China | li.nan25@zte.com.cn
Lv Kaiying |  |  | lv.kaiying@zte.com.cn
Sun Bo |  |  | sun.bo1@zte.com.cn
Wei Ning |  |  | wei.ning@zte.com.cn

## Slide 2: Background
  Usage model 9 Smart scanning :The mobile device passively scans through multiple channels using WUR, and collects basic information about nearby APs. The collected info can be used to facilitate the devices’ roaming decisions.
We futher discuss passive scanning using wake up radio in this proposal.

## Slide 3: Introduction
An WUR STA may perform passive scanning using its wake up radio during WUR mode as background scanning to collect information about neighbor BSSs or target BSS/ESS for the purpose of AP (re)selection.
However, it would be very inefficient and power consuming if an WUR STA does WUR scanning on several WUR channels first and then do PCR scanning on 20MHz channels.
To implement WUR scanning effectively, some information is suggested to be provided to a WUR STA:
  Neighbor WUR information can be provided to the STA to facilitate WUR scanning:
    WUR discovery channel, SSID/compressed SSID, and primary channel are proposed.
  Methods to advertise these information are also discussed.

## Slide 4: Proposed Scheme (1/3)
Information A: WUR discovery channel location
To help a STA in WUR mode performing WUR scanning with less power consumption, WUR discovery channel(s) of neighbor BSSs or target BSS(s)/ESS(s) could be provided to the STA by its associated AP.
  Only one WUR discovery channel per BSS /ESS needs to be advertised.
  WUR scanning will be limited to specific WUR discvoery channels.
  The STA can monitor its own WUR frame on its WUR channel during ON windows and perform WUR scanning on dedicated WUR discovery channels during OFF windows of duty cycles if needed.
Information Delivery method:
Opt 1: delivered in a neighbor WUR parameter element by PCR in 802.11 frame such as beacon/probe response frame
  Pros: Considering the overhead, it is more efficient to sent this information by PCR
  cons: Any change about WUR discovery channel location will be notified by waking up the STA.
Opt 2: delivered by WUR frame such as WUR beacon or WUR discovery frame
  Pros: Any change about WUR channel location can be notified without waking up the STA.
  cons: less efficient if the information of WUR discovery channel location is large.

## Slide 5: Proposed Scheme (2/3)
Information B: compressed SSID
Compressed SSIDs can assist STA to choose candidate AP(s) within the same ESS during WUR scanning.
  In some use case, for example, in a network of warehousing system, many freight companies may share the same warehouse. A plurality of APs of a specific company forms a separate ESS for the ease of network management.
  A STA may prefer to choose a candidate AP within the same ESS for fast BSS transition
Information Delivery method:
An AP can indicate the candidate compressed SSID to help the STA select a target AP in a neighbor WUR parameter element by PCR in 802.11 frame such as beacon/probe response frame
WUR frames such as WUR beacon/WUR discovery frame could also advertise its compressed SSID
  A compressed SSID is used to reduced the overhead. eg. 4byte as defined in 802.11ah.

## Slide 6: Proposed Scheme (3/3)
Information C: Primary channel of PCR
Once an WUR STA has already selected some APs as candidate APs through WUR scanning, the WUR STA turns on its main radio for AP discovery. It would be more efficient if it can use the result of WUR scanning for future association.
If the STA has no information about the candidate AP(s)' primary channel, then the STA still has to perform main radio scanning on each channel to find the candidate APs, which is certainly not efficient.
It's suggested that the primary channel of a target AP should be provided to the associated STA.
Information Delivery method:
Opt 1:deliverd in a neighbor WUR parameter element by PCR in 802.11 frame such as beacon/probe response frame
  Any change about primary channel location will be notified by waking up the STA.
Opt 2: delivered in WUR frame
  Any change about primary channel location can be notified without waking up the STA.

## Slide 7: Proposed Example (1/2)
Example 1:
  An AP advertises its own WUR parameter element in PCR including:
    its compressed SSID and/or BSS ID
    its WUR channel or primary WUR channel if the AP allocates more than one WUR channels
  The AP may also include a neighbor WUR parameter element in PCR to indicate the WUR configuration of target BSS(s) or ESS to assist STAs for fast WUR scanning, including:
    target compressed SSID and/or BSS ID
    (Primary) WUR channels of target BSS(s) or ESS
    Primary channel of target BSS(s) or ESS
  An WUR frame should indicate its compressed SSID and/or BSS ID to facilitate WUR STAs to scan the target BSS or ESS
    The WUR frame can be a unicast /multicast WUR packet or an WUR Beacon or a specific WUR frame for network selection
    WUR STAs scan the target WUR channels and match the scanned compressed SSID and BSS ID with the target one, and
    Turn on its PCR to scan the primary channels of target BSS(s)

## Slide 8: Proposed Example (2/2)
Example 2:
  An AP advertises its own WUR parameter element in PCR including:
    its compressed SSID and/or BSS ID
    its WUR channel or primary WUR channel if the AP allocates more than one WUR channels
  The AP may indicate in PCR the target BSS(s) or ESS to assist STAs for network selection, including:
    target compressed SSID(s) and/or BSS ID(s)
    target WUR channel list
  An WUR frame should indicate its primary channel and its compressed SSID and/or BSS ID to facilitate WUR STAs to scan the target BSS or ESS on the indicated primary channel
    The WUR frame can be an WUR Beacon or a specific WUR frame for network selection
    WUR STAs scan the target BSS or ESS through target WUR channels, and
    Acquire the primary channel info of the target PCR from WUR frame
    Turn on its PCR to scan the primary channels of target BSS(s)

## Slide 9: Summary
We discussed the WUR parameters of neighbor BSSs/ESS that are needed for improving power consumption with WUR scanning
  WUR discovery channel location
  Compressed SSID
  primary channel
The method of advertising these parameters has also been discussed.
  By using 802.11 message such as Beacon frame or probe response frame
  By using wake up frame such as WUR unicast /multicast packet, WUR beacon or WUR discovery frame.

## Slide 10: Straw Poll 1
Do you agree the following information shall be notified to a WUR STA to assist WUR scanning and network selection?
WUR discovery channel location
  Y
  N
  A
Compressed SSID
  Y
  N
  A
Primary channel
  Y
  N
  A

## Slide 11: Straw Poll 2
Do you agree WUR discovery channel location should be sent through:
  PCR
    Y
    N
    A
  WUR
    Y
    N
    A
  Both
    Y
    N
    A

## Slide 12: Straw Poll 3
Do you agree compressed SSID should be sent through:
  PCR
    Y
    N
    A
  WUR
    Y
    N
    A
  Both
    Y
    N
    A

## Slide 13: Straw Poll 4
Do you agree primary channel should be sent through:
  PCR
    Y
    N
    A
  WUR
    Y
    N
    A
  Both
    Y
    N
    A

## Slide 14: Straw poll 5
Proposed text in SFD:
R.4.8.A:[Assigned D0.1] Define a type of WUR frame as WUR Discovery frame to assist the STAs to discover the BSS.
R.4.8.B:primary channel and compressed SSID of the AP should be provided to a WUR STA for WUR smart scanning operation in WUR Discovery frame .Other information is TBD.
  WUR discovery channel location, primary channel, and compressed SSID of neighbour APs could be sent through PCR messages such as Beacon frame, probe response frame.
    Y
    N
    A

## Slide 15: Straw poll 6
Proposed text in Draft
TGba Editor: Change the paragraphs below of this subclause as follows :
9.10 WUR frame formats
9.10.3.3 WUR Discovery frame format
  The Frame body field of the WUR Discovery frame contains primary channel and compressed SSID of the AP. WUR discovery channel location, primary channel, and compressed SSID of neighbour APs are provided by PCR messages such as Beacon frame, probe response frame.
    Y
    N
    A

## Slide 16: References
[1]11-17-0029-10-00ba-wur-usage-model-document
[2]11-17-0575-06-00ba-spec-framework