## Slide 1: Discussion on SLS with different Tx and Rx antennas
Date: 2017-11
Authors:

## Slide 2: Background
In 802.11-2016 10.36.5:
Within a CBAP a STA with multiple DMG antennas should use only one DMG antenna in its frame transmission, CCA and frame reception, except if it is the initiator or responder in an SLS (10.38). The algorithm to select a DMG antenna and switch the active DMG antenna is implementation dependent. Within CBAPs a STA that changed to a different DMG antenna in order to transmit should perform CCA on that DMG antenna until a frame is detected by which it can set its NAV, or until a period of time equal to the dot11DMGNavSync has transpired, whichever is earlier.
When a STA operates in SISO mode, the above requirement makes it difficult for a STA transmitting and receiving using different antennas

## Slide 3: Background
  11ay allows STA to receive TXSS with multiple antennas
    The CDOWN fed back to the initiator from the responder doesn't indicate which rx antenna the responder used to receive the selected initiator sector, e.g., Antenna 1
  In SSW FBCK, the initiator may select a responder tx sector which belongs to a different responder antenna, e.g., Antenna 2

## Slide 4: Initiator avoids having different Tx/Rx Antennas
Initiator selects responder link based on the feedback from RSS
Initiator link: From I to R using ant 1 to ant 1?
Before responder link transmission, the responder may perform CCA using ant 1, but it will transmit using ant 2, which may create interference

## Slide 5: Suggested improvement
  Allow responder to switch antenna between SSW FBCK and SSW Ack. Add a requirement that the initiator sector indicated in SSW-Ack must belong to the same initiator DMG antenna which transmits SSW FBCK

## Slide 6: Example

## Slide 7: Straw Poll
Do you agree to include the changes described in 11-17-1622-01-00ay?