## Slide 1: WUR Action Frame Format Follow up
Date: 2017-11-06
Name | Affiliation | Address | Phone | Email
Po-Kai Huang | Intel | 2200 Mission College Blvd., Santa Clara, CA 95054, USA | +1-408-765-8080 | po-kai.huang@intel.com
Daniel F Bravo |  |  |  | 
Noam Ginsburg |  |  |  | 
Robert Stacey |  |  |  | 

## Slide 2: Abstract
We propose to have WUR action frame in [1]
We continue the design for WUR action frame format in this presentation to have enough materials for draft 0.1.

## Slide 3: General WUR Action Frame Format
    Category field indicates WUR Action
    WUR Action field includes appropriate action
    Dialog Token field is defined in 9.4.1.12
    WUR Mode Element includes necessary WUR parameters
 | Category | WUR Action | Dialog Token | WUR Mode Element
Octets | 1 | 1 | 1 | TBD

## Slide 4: General WUR Mode Element Format
    Element ID and Element ID Extension fields indicate WUR Mode Element
    Length field is defined in 9.4.2.1
    Action Type field indicates appropriate type of WUR action
    WUR Mode Response Status field
 | Element ID | Length | Element ID Extension | Action Type | WUR Mode Response Status | TBD WUR Parameters
Octets: | 1 | 1 | 1 | 1 | 1 | TBD

## Slide 5: Indication
We think signaling is required to allow two way handshake for WUR Mode Setup [3]
  Action Type field in WUR Mode element includes the following indication: Enter WUR Mode Request and Enter WUR Mode Response
    As a result, the WUR Mode element can be piggybacked in other request/response procedure to achieve WUR Mode Setup.
  WUR Action field in WUR Action frame includes the following indications: WUR Mode Setup
  WUR Mode Response Status field in WUR Mode element includes the following indications: Enter WUR Mode Accept and Denied
We think signaling is required to allow one way WUR Mode Teardown
    WUR Action field includes the following indications: WUR Mode Teardown

## Slide 6: State Machine and Flow diagram
Two way Setup
One way Teardown
WUR Mode
No WUR
One way Teardown
Two-way Setup
AP
Non-AP STA
Request
Response
Ack
Ack
AP
Non-AP STA
WUR Mode Teardown
Ack
AP
Non-AP STA
WUR Mode Teardown
Ack

## Slide 7: Consideration of Defining WUR Mode Suspend
There has been comments to define corresponding signaling to only negotiate WUR parameters and enter WUR Mode later [2]
  The benefits is to avoid renegotiation after exiting WUR Mode and Enter later
This basically defines additional WUR Mode Suspend state
  Corresponding design detail is shown in the following slides
We see the motivation because non-AP STA may want to resume PCR negotiated schedule for PCR operation, which can only be achieved by existing WUR Mode
The complexity of additional transition can be avoided if non-AP STA chooses not to do it.

## Slide 8: Updated State Machine
WUR Mode
No WUR
One way Teardown
Two-way Setup
WUR Mode
WUR Mode Suspend
No WUR
One-way Teardown
One-way Teardown
Two-way Setup
One-way enter
One-way enter
Two-way Setup
Without WUR Mode Suspend
With WUR Mode Suspend

## Slide 9: Definition of WUR Mode Suspend
Existing definition of WUR Mode:
  Non-AP STA is available through WURx in doze state
  negotiated WUR parameters is maintained
  negotiated PCR schedule (if any) is suspended
No WUR:
  negotiated WUR parameters is discarded
  negotiated PCR schedule (if any) is active and is not suspended
Define WUR Mode Suspend:
  STA may turn off the WURx
  negotiated WUR parameters is maintained
  negotiated PCR schedule (if any) is active and is not suspended

## Slide 10: Corresponding Signaling to Enable WUR Mode Suspend
In Action type field of WUR Mode element, include the following indication:
  Enter WUR Mode Suspend Request,
  Enter WUR Mode Suspend Response,
  Enter WUR Mode Suspend
  Enter WUR Mode
In WUR Mode Response Status field of WUR Mode element, include the following indication
  Enter WUR Mode Suspend Accept

## Slide 11: Conclusion
We discuss the frame format of WUR Action frame
We discuss signaling to enable two way WUR Mode setup and one way WUR Mode teardown
We discuss the definition of WUR Mode Suspend and the signaling to enable the new state

## Slide 12: Straw Poll #1
  Do you support the following?
  The frame body of WUR Action frame can include the following:
    Category field that indicates WUR Action
    WUR Action field that includes the following indications: WUR Mode Setup and WUR Mode Teardown
    Dialog Token field
    WUR Mode Element includes necessary WUR parameters

## Slide 13: Straw Poll #2
  Do you support the following?
  The WUR Mode element can include the following:
    Element ID and Element ID Extension fields that indicate WUR Mode Element
    Length field
    Action Type field that includes the following indications: Enter WUR Mode Request, Enter WUR Mode Response
    WUR Mode Response Status field that includes the following indications: Enter WUR Mode Accept and Denied
    WUR parameters field that includes the indication for WUR parameters

## Slide 14: Straw Poll #3
  Do you support the following?
Define WUR Mode Suspend, and if an non-AP STA is in WUR Mode Suspend, then
  The negotiated WUR parameters between AP and non-AP STA is maintained
  Non-AP STA may turn off the WURx
  Note that negotiated PCR schedule (if any) is active and is not suspended

## Slide 15: Straw Poll #4
Do you support to add the following signaling in WUR Mode element?
  In Action type field of WUR Mode element, include the following indication:
    Enter WUR Mode Suspend Request
    Enter WUR Mode Suspend Response
    Enter WUR Mode Suspend
    Enter WUR Mode
  In WUR Mode Response Status field of WUR Mode element, include the following indication: Enter WUR Mode Suspend Accept

## Slide 16: Reference
[1] 11-17-342-04-00ba WUR Negotiation and Acknowledgement Procedure Follow up
[2] 11-17-1302-04-00ba WUR Mode Operation Procedures
[3] 11-17-1316-00-00ba WUR Mode Signaling