## Slide 1: Solving Status mismatch
Date: 2017-11-06
Authors:

## Slide 2: Background: IEEE 17/1015r2 - Status mismatch problem in WUR transmission procedure
If STA’s main transceiver is already turned on before the transmission of Wake-up packet, the new transmission procedure may not be started
  The transition to power save mode is not mandatory, STA may stay in awake state
  AP assumes that the STA is in sleep state, and transmits Wake-up packet in order to transmit the downlink packet
  Since STA’s main transceiver cannot decode the wake-up radio, STA cannot transmit the response frame to the wake-up packet
  AP retransmits the wake-up packets and STA cannot transmit the response frame to the wake-up packet repeatedly, causing the inefficiency of data transmission
  Straw Poll: TGba should consider mechanism to combat the inefficiency in case AP transmits wake-up frame to STA in awake state: Y/N/A=8/0/18

## Slide 3: Example
Unscheduled wake up
WUR reentry
STA’s PCR is not able to decode WUR PPDU
STA’s PCR is not able to decode WUR PPDU
Off
On
On
Off
Off
On
Off
On
On
Off

## Slide 4: Proposal (1/3)
The WUR Mark field (OFDM waveform) includes information to help WUR STAs’ PCR identify WUR PPDUs addressed to the STA.

## Slide 5: Proposal (2/3)
 | WUR ID | Purpose | CRC | BCC tail bits
Bits | 12 | 2 | 4 | 6
Acts as signature to identity WUR PPDU. A matching ID differentiates WUR PPDUs from legacy 802.11a/g packets.
WUP Payload
L-STF
L-LTF
L-SIG
802.11 Legacy preamble
WUR PPDU
WUR Mark
802.11 waveform (OFDM)
WUR waveform (OOK)
BPSK
Indicates the intended purpose of the WUR PPDU. May be based on the Type/Purpose field carried in the WUR Frame
Purpose
Fields | Number of bits | Description
WUR ID | 12 | Acts as the signature to differentiate the WUR PPDU from legacy 802.11 PPDUs. In unicast WUR PPDUs, the WUR ID is set to the destination STA’s ID (e.g. AID12). In broadcast or multicast WUR PPDUs, the WUR ID is set to the identifier of the BSS or the identifier of the AP. The WUR ID also implicitly differentiates unicast WUR PPDUS from broadcast/multicast WUR PPDUs.
Purpose | 2 | Indicates the purpose of the WUR PPDU.
CRC | 4 | Cyclic redundancy check over the preceding 14 bits.
BCC tail bits | 6 | Set to all zeroes to terminate the BCC.

## Slide 6: Proposal (3/3)
Example encoding of the Purpose field in the WUR Mark:
Purpose Field value | Purpose of the WUR PPDU | Expected STA’s Action
0 | Notification of pending broadcast DL transmission | No response is required. Wait for DL PPDU.
1 | Notification of buffered data (Normal PS mode) | Transmit a PS-Poll frame
2 | Notification of buffered data (APSD) | Transmit a trigger frame (either a Data frame or a QoS Null frame with the delivery- enabled AC).
3 | Solicitation of UL Data frame. | Transmit a UL Data frame
Broadcast/Multicast WUR PPDU
Purpose Field value | Purpose of the WUR PPDU | Expected STA’s Action
0 | WUR time synchronization | No response is required.
1 | Notification of pending broadcast DL transmission | No response is required. Wait for DL PPDU.
2 | Notification of pending multicast DL transmission | No response is required. Wait for DL PPDU.
3 | Notification of pending trigger frame transmission to solicit multi-user UL transmission | Prepare UL frame and wait for trigger frame.
If the WUR ID field matches neither the STA’s ID, nor the ID of its BSS or AP, the STA will treat the WUR PPDU as legacy packet.
Unicast WUR PPDU

## Slide 7: Summary
In this presentation we proposed:
The WUR Mark field (OFDM waveform) includes information to help WUR STAs’ PCR identify WUR PPDUs addressed to the STA.
The WUR Mark field also includes additional information regarding the intended purpose of the WUR PPDUs to help WUR STAs decide the next action.

## Slide 8: Straw Poll 1
Do you agree that the WUR Mark field (OFDM waveform) includes information to help WUR STAs’ PCR identify WUR PPDUs addressed to the STA?
Y/N/A

## Slide 9: Straw Poll 2
Do you agree that the WUR Mark field (OFDM waveform) includes information regarding the intended purpose of the WUR PPDUs to help WUR STAs decide the next action?
Y/N/A

## Slide 10: References
[1] IEEE 802.11-17/1015r2 - Status mismatch problem in WUR transmission procedure
[2] IEEE 802.11-17/0675r0 - WUR Coexistence and Packet Format
[3] IEEE 802.11-17/037r6 – Purpose Indication of WUR Packets
[4] IEEE 802.11-17/0574r4 - Specification Framework for TGba