## Slide 1: A proposal for enabling the use of IEEE 802.11ax-stye Spatial Reuse under EN 301 893
2 November 2017
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: EN 301 893 can be refined to allow 802.11ax-style SR with dual threshold
Situation
EN 301 893 is an ETSI BRAN standard that provides a means of conforming to the R-ED requirements
Spatial reuse is a concept that well aligned with the efficient use goals of the RE-D
Problem
EN 301 893 will need to be revised to enable 802.11ax-style SR
The challenge is to revise EN 301 893 in a way that balances 802.11ax-style SR against other goals
Answer
One solution is for EN 301 893 to allow the potential “victim” of SR to decide if the medium is occupied
A second variation is for a device to allow simultaneous transmissions within its own MCOT
The proposed SR rules enable innovation, maintain technology neutrality & minimise complexity
Assumption
ETSI BRAN agrees to 802.11 WG’s request to enable dual threshold for 802.11ax

## Slide 3: EN 301 893 is an ETSI BRAN standard that provides a means of conforming to the R-ED requirements
  EN 301 898 is a Harmonised Standard covering the essential requirements of article 3.2 of Directive 2014/53/EU
    Directive 2014/53/EU is also known as RE-D
  Article 3.2 of the RE-D encourages effective & efficient use of the spectrum and the avoidance of harmful interference
    Radio equipment shall be so constructed that it both effectively uses and supports the efficient use of radio spectrum in order to avoid harmful interference
  EN 301 893 has been developed & revised by ETSI BRAN over many years to allow one voluntary means of conforming to the essential requirements
    The current version of EN 301 893 is v2.1.1 and was ratified in May 2017
    ETSI BRAN have just adopted a WI to revise EN 301 893 again, with the adaptivity clauses representing one significant focus

## Slide 4: EN 301 893 defines two threshold methods to support the effective use goals of RE-D
  The adaptivity clauses in EN 301 893 v2.1.1 were mainly designed to encourage fair sharing of the 5GHz band by all technologies
    Fair sharing promotes effective use of spectrum
  The sharing mechanism specified by the adaptivity clause is based on an LBT mechanism derived from 802.11 EDCA, using two threshold methods to determine whether the medium is “busy”
    Energy Detection threshold of -72 dBm (the threshold actually varies depending on tx power); OR
    Energy Detection threshold of -62 dBm, as long as the system is conformant with IEEE 802.11-2016 (including its Preamble Detection threshold of -82 dBm)
  The first method was included mainly for use by LTE based technologies, while the second method was included mainly for use by 802.11a/n/ac
    The current version of EN 301 893 specifies the first method must be used for any systems not conformant with IEEE 802.11-2016
    Therefore, 802.11ax systems must currently use the first method

## Slide 5: It is hoped the two threshold methods will enable fair sharing between 802.11 & LTE technologies
  The two threshold methods driving LBT in EN 301 893 represent a compromise hammered out in ETSI BRAN during 2015-16 by stakeholders from the Wi-Fi & LAA communities
  The two threshold methods may enable “fair” sharing between 802.11a/n/ac & LAA in at least some environments
    3GPP simulations show “fair” sharing between LAA & 802.11ac in a number of specific scenarios, although the simulations have known flaws that have been noted by IEEE 802 in multiple LS’s to 3GPP RAN1
  It is likely both threshold methods, or refinements, will become the basis for some level of “fair” sharing between all technologies
    There are no proposals to fundamentally change EN 301 893’s LBT mechanism
    802.11 WG has proposed that EN 301 893 be refined to allow any technology (incl 802.11ax) to use the second method (denoted the dual threshold method)
    Few 802.11ax/LTE technology coexistence simulations have been published but it is hoped the two threshold methods will enable some level of “fair” sharing

## Slide 6: Spatial reuse is a concept that well aligned with the efficient use goals of the RE-D
  IEEE 802.11ax will include two spatial reuse (SR) mechanisms to enable some simultaneous transmissions by 802.11 in dense deployments
    OBSS_PD-based spatial reuse
    SRP-based spatial reuse
  SR, such as that proposed for 802.11ax, when designed and implemented well, should enable more efficient use of limited spectrum resources
  As such, SR is well aligned with R-ED Article 3.2, which encourages efficient use of spectrum

## Slide 7: Assumption: ETSI BRAN agrees to 802.11 WG’s request to enable dual threshold for 802.11ax
  IEEE 802.11 WG has requested ETSI BRAN to refine EN 301 893 to allow 802.11ax to use a dual threshold option similar to that specified in IEEE 802.11-2016
  This proposal to enable 802.11ax-style SR is based on an assumption that that ETSI BRAN agrees to this request
  If ETSI BRAN do not agree to the request (thus forcing 802.11ax to use the single threshold option of ED = -72 dBm or less) then
    SR is enabled for ED less than -72 dBm
    802.11ax may have less access to the medium than both 802.11ac and LAA in certain circumstances

## Slide 8: EN 301 893 will need to be revised to enable 802.11ax-style SR
  The current version of EN 301 893 was specified with a bias towards ensuring fairness between systems (effective use) rather than efficiency
    Fairness between 802.11ac & LAA was the focus over the last two years
    SR was not considered in developing the current version of EN 301 893
  However, the dual threshold mechanism will need some refinement to enable the use of 802.11ax-style SR
    Essentially, an exception to the PD = -82 dBm threshold is required to enable 802.11ax-style SR
  The challenge is to revise EN 301 893 in a way that balances 802.11ax-style SR against other goals

## Slide 9: The challenge is to revise EN 301 893 in a way that balances 802.11ax-style SR against other goals
Maintain fairness
Develop rules for SR in EN 301 893 that maintains fair access for all technologies, similar to current version of EN 301 893
Enable innovation
Minimise restrictive rules for SR in EN 301 893, thus enabling future innovation without needing to revise EN 301 893 again
Limit complexity
Refine EN 301 893 to allow SR in a way that focuses on general principles rather than relying on detailed & complex rules
Support technology neutrality
Rather than specifying technology-specific rules in EN 301 893, specify rules than can apply to any technology
Goals for revising EN 301 893 to allow 802.11ax-style SR

## Slide 10: One solution is for EN 301 893 to allow the potential “victim” of SR to decide if the medium is occupied
  One possible concept to enable SR in the context of EN 301 893 (and achieve the other goals on the previous page) is:
    A device may consider the medium to be not occupied if it has a reasonable basis to believe the current transmitter would consent to the device transmitting simultaneously
  One obvious reasonable basis would be if the device followed rules for SR that had been adopted by the transmitting device
    For example, if the device determined that the transmitting device was an 802.11 device (possibly by decoding the preamble and/or MAC header) then one could reasonably argue that simultaneous transmission was allowed in circumstances defined by the SR rules in 802.11ax
  There is no reason an LTE based systems could also not use this mechanism too
    Using this mechanism would probably require decoding preambles & possibly MAC headers

## Slide 11: The proposed new rule in EN 301 893 increases the possibility of simultaneous transmissions
  The proposed new rule for enabling SR allows the medium to be considered not occupied if the transmitting device consents to simultaneous transmissions
  A device assuming the medium to be not occupied will allow the LBT mechanism to continue counting down and the device to transmit earlier than normal
  While this rule will enable simultaneous transmissions in many cases, it will not necessarily do so, depending on the state of the LBT countdown
  However, it is important to allow the LBT mechanism to continue operating as normal to avoid collisions between multiple other independent devices (a common situation in unlicensed spectrum)

## Slide 12: A second variation is for a device to allow simultaneous transmissions within its own MCOT
  Discussions related to 3GPP NR-Unlicensed at a recent workshop suggest that these systems will often be coordinated & synchronised
  Therefore, these NR systems will not always need LBT to coordinate access and avoid collisions
  This observation suggests a second option should be introduced in EN 301 893 that allows immediate simultaneous transmission in some circumstances
    A device may transmit during an MCOT of the current transmitter if it has a reasonable basis to believe the current transmitter would consent to simultaneous transmissions
  While this proposed option was inspired by NR discussions, there is no reason future versions of 802.11 could not take advantage of this option too

## Slide 13: The proposed SR rules enable innovation, maintain technology neutrality & minimise complexity
  The proposal is that EN 301 893 be modified to incorporate two rules to enable spatial reuse
    A device may consider the medium to be not occupied if it has a reasonable basis to believe the current transmitter would consent to simultaneous transmissions
    A device may transmit during an MCOT of the current transmitter if it has a reasonable basis to believe the current transmitter would consent to simultaneous transmissions
  These rules are conceptual; the actual text in EN 301 893 will depend on other refinements to EN 301 893
  However, the proposed rules are sufficiently high level that they enable behaviour that supports the efficiency goals of EN 301 893 …
  … while also enabling future innovation in various standards, maintaining technology neutrality and minimising EN 301 893 complexity

## Slide 14: The IEEE 802.11 Coexistence SC will discuss this proposed solution
Questions
  Does 802.11 WG still want to promote the use of dual thresholds for 802.11ax?
    At least some would be happy for 802.11ax to use ED = -72 dBm at all times with no PD restrictions; this would resolve the SR issue but potentially cause fairness issues with 802.11ac and/or LAA
  Do we want to allow 802.11ax-style SR in a system that uses dual thresholds?
    Maybe it is sufficient to enable SR only in an environment that relies on ED = -72 dBm
  Assuming we want SR with traditional dual thresholds:
    Are these proposed rules good enough to enable 802.11ax-style SR?
    Do these proposed rules have any unintended consequences?
  …