## Slide 1: WUR frame format follow-up
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Taewon Song |  |  |  | taewon.song@lge.com

## Slide 2: Introduction
The following concepts for WUR frame were agreed in 11ba SFD[1]
  The basic format of WUR frame [2]:
    MAC header is fixed size
    It is optional for a STA to support reception of a frame with nonzero length Frame Body.
  An AP assigns a WUR identifier to a STA with WUR capability through PCR WUR negotiation procedure [3]
  AP can send a broadcast wake-up frame before sending a broadcast/multicast data [4]
  11ba spec shall define a mechanism to wake up multiple WUR mode STAs [5]
This contribution proposes the further details of WUR frame format

## Slide 3: WUR frame format (1/2)
Frame control (FC, 1 bytes) + Address (2 bytes) + TD Control ( 2bytes) + Frame Body (0 or variable) + FCS (2 bytes)
Frame control (FC, 1 bytes)
  Type (3 bits)
    E.g.,) 0: WUR Beacon, 1: Broadcast Wake-up frame, 2: Unicast Wake-up frame, 3: Multi-user Wake-up frame, 4: Vendor specific frame[7], 5: Discovery frame[11], 6~7: reserved
  FB(Frame Body) Length (2 bits)
    0: no Frame body
    1: 2 bytes,
    2: 4 bytes,
    3: more than 4 bytes, Extended FB length field is included in Frame body, for vender specific frame
  Reserved (2 bits)
Address (2 bytes): TA (12 bits, BSS Color or PBSSID), Reserved (4 bits)

## Slide 4: WUR frame format (2/2)
TD Control (2 bytes)
  If Type =0 or 1, Partial TSF (12 bits) [12], Counter (2 bits) [8], Broadcast Data presence (1 bit) [9], Reserved (1 bits)
  If Type =2, Unicast WID (8 bits), Reserved (8 bits)
  If Type =3, Group ID (8 bits), Reserved (8 bits)
    AP may assign one or more Group IDs to a STA through WUR negotiation
    If FB Length = 0, this frame is for all STAs in the group indicated by Group ID
    If FB Length > 0 & Group ID = a special value (e.g., 0), WID list is included in Frame body [6]
      E.g., if 2bytes length, 2 unicast WIDs, if 4 bytes length, 4 unicast WIDs
    Otherwise (i.e., FD length > 0 & Group ID > 0), WID Bitmap is included in Frame Body (See appendix)
      E.g., if 2bytes length, 2 bytes WID Bitmap, if 4 bytes length, 4 bytes WID Bitmap
MAC header
Frame Body
FCS
Type=11, Length = 4 byte, Group ID = 0
4 WIDs

## Slide 5: Reference
[1] 17/575r4, TGba SFD
[2] 17/1004r4, Considerations on WUR frame format
[3] 17/0977r4, Address structure in unicast wake-up frame
[4] 17/124r4, WUR MAC and Wakeup Frame
[5] 17/0054r3, WUR MAC issus
[6] 17/1004r4, Considerations on WUR frame format
[7] 17/1334r0, Vendor Specific WUR Frame Follow up
[8] 17/1368r2, BSS parameters update notification
[9] 17/1356r3, Duty cycle mode STA’s PS follow-up
[10] 17/1641r0, WUR Frame Format for Smart Scanning
[11] 17/1608r0, WUR Discovery Frame for Smart Scanning
[12] 17/1384r0, WUR synchronization

## Slide 6: Straw Poll 1
Do you agree the following?
  TBD bits Type field is included in the Frame control field of MAC header with the following mapping of the Type field:
    0 assigned to WUR Beacon
    1 assigned to Wake-Up frame
    2 assigned to Vendor specific frame

## Slide 7: Straw Poll 2
Do you agree the following?
  AP may assign one or more Group IDs to a STA through PCR
    The assigned Group ID is used in a wake-up frame
    The details for group ID (e.g., ID allocation procedure (e.g., WUR Action frame or others similar to 11ac procedure), ID structure, etc.) are TBD

## Slide 8: Straw Poll 3
Do you agree the following?
  A Wake Up frame with variable length may contain the information for the multiple STAs in the Frame Body
    The detailed information of multiple STAs (e.g., bitmap, ID list) is TBD

## Slide 9: Appendix
Multi-user wake-up using Group ID & WID Bitmap
  STA’s position in the Bitmap is Bit N where N is value of (STA’s WID mod the bit size of Bitmap)
    E.g.,) If STA X/Y’s WID = 3/32 & Size of Bitmap = 16 bits, then Bit 3/0(=3/32 mode 16) for STA X/Y
  The received Group ID also should be equal to one of the assigned Group IDs (i.e., if group ID is not equal, the frame is ignored)
  Some STAs may be located at the same position (Bit N) of the bitmap (i.e., not unique position)
  This can be solved by AP’s implementation
    Ex 1) AP can assign those STAs to different groups (e.g., Group 1 for WID = 16, Group 2 for WID = 32)
    Ex 2) AP can assign those STAs to different On durations (e.g., Group 1 and 1st On duration for WID = 8, Group 1 and 2nd On duration for WID=16)
    Ex 3) AP can use WID Bitmap considering only STAs which have the capability of variable frame length
    ...
  Note that the variable Frame Body is optional feature in STA
B0
B1
B2
B3
B4
B5
B6
B7
STA X
STA Y
For this, AP assigns only Group ID to a STA