## Slide 1: WUR Frame Format for Smart Scanning
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Taewon Song | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | taewon.song@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
In [1], a specific WUR frame format have been proposed
A new usage model, smart scanning has been added to WUR usage mode document [2], [3]
  In [4], a concept of the WUR discovery frame and discovery channel have been proposed
In this contribution, we propose a detailed WUR frame format for scanning

## Slide 3: Information for WUR scanning
Channel information
  Information of PCR channel and WUR operating channel
BSS Capability and Load information
  AP can advertise the network’s capabilities and current load
(Partial) BSSID
(Partial) SSID
  It reduces false alarm probability of partial BSSID
  It may enable STAs to find and recognize unrecorded BSS
Other information is TBD

## Slide 4: Application Example
WUR Information can be conveyed via WUR Broadcast frame
Frame Body
FCS
MAC Header
Address
= (Partial) BSSID
Frame Control
TD Control
Type
Type = Broadcast
Information for scanning
Channel Information
Capability Information
BSS Load
(Partial) BSSID
(Partial) SSID

## Slide 5: Summary
We have discussed a detailed WUR frame format for scanning
This information can be included in any other WUR frames such as WUR Discovery frame [4]
Specifically, this concept can assist fast roaming in an enterprise, airport, station, or carrier Wi-Fi extended basic service set (ESS)

## Slide 6: Straw Poll 1
Do you agree to define that Partial SSID can be included in WUR frame for discovery?

## Slide 7: Straw Poll 2
Do you agree to define that channel information, capability information, or BSS load to assist scanning/roaming can be included in WUR frame?

## Slide 8: References
[1] “WUR frame format follow-up,” 17/1638r0
[2] “WUR usage model document,” 17/29r10
[3] “Examining 11ba usage models for mainstream devices,” 17/1386r7
[4] “WUR Discovery Frame for Smart Scanning,” 17/1608r0