## Slide 1: WUR frame format – Follow up
Authors:
Alfred Asterjadhi,
George Cherian,
Yanjun Sun

## Slide 2: Introduction
The general WUR frame format was defined in [1]:
With good progress on many of the structure/functionality details [1, 2, 3]:
  Length of the MAC Header is fixed and Frame Control field contains a Type subfield
    One value assigned to WUR Beacon and one value assigned to Wake Up frame
  Address field contains an identifier of the transmitter in the WUR Beacon [1] and of both the transmitter and receiver in the unicast Wake Up frame [2], with the receiver being identified by a WID provided by the AP [3]
  Type Dependent (TD) Control field contains type dependent control information
    The TD Control field of WUR Beacon contains the partial TSF
  The Frame Body field is optionally present (and optional in RX for a WUR STA)
  The FCS carries the CRC of the frame (length and computation of the FCS is TBD)
In this presentation we follow up with additional details:
  Accounting for the proposals that are being discussed and related to this topic [4, 5, 6, etc.]
  Aiming at finalizing some details on the content and length of certain frames and the size of its fields
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | TBD | TBD | TBD

## Slide 3: Frame Control
Frame Control field contains a Type subfield
  Motioned: One value assigned to WUR Beacon and one value to Wake Up frame
  Under discussion: WUR Vendor Specific frame[4], WUR Discovery frame[5]
  We would need 2 bits of Type field to accommodate these values
We need to indicate length of variable length (VL) WUR frames as well
  Option 1: The length was proposed to be signaled in the Frame Control field [1, 2]
    Pros: All information is contained in Frame Control, i.e., it serves its purpose of controlling the frame
    Cons: 3-4 bits more expensive for constant length (CL) WUR frames
  Option 2: A bit in FC (indicates VL WUR frame, and Length is in Frame Body)
    Pros: 3-4 bits less expensive for CL WUR frames.
    Cons: Information for controlling the frame is sparsed across the frame.
Note: Constant Length (CL) WUR frames don’t need a Length field
  Bits can be used for other purposes if Length field is located in the Frame Control field
 | Frame Control | Address | TD Control
Bits | TBD | TBD | TBD

## Slide 4: Frame Control (2)
Option 1: Frame Control field [8 bits]
  Type field identifies type and differentiates VL/CL WUR frames
  Frame length is signaled in the Length/Misc. field
    No Length field is present for CL WUR frames, instead these bits are used for other purposes
Option 2: Frame Control field [4 bits]
  Type field identifies the type and differentiates VL/CL WUR frames
  Length is signaled at the start of Frame Body field for VL WUR frames
    No Length field is present for CL WUR frames
Propose Option 1 since:
  Allows to have all structure signaling in one location and
  Allows 4 bits to be used for miscellaneous purposes for CL WUR frames
Straw Poll 1: Do you support Option 1 for the Frame Control?
YES, NO, ABS
 | Frame Control | Address | TD Control
Bits | 4 or 8 | TBD | TBD
 | Type | Reserved
Bits | 3-4 | rest
 | Type | Length/Misc. | Reserved
Bits | 3-4 | 3-4 | rest
Field sizes are an example

## Slide 5: Address field
Address field contains an identifier of:
  Transmitter in WUR Beacon [1] ,
  Transmitter and receiver in unicast Wake Up [2], etc.
Proposal: The Address field is 12 bits in length [1]
  If lower false alarm probability is needed for certain frame types
    Then use TD Control field to carry additional addressing information
    Or hide BSSID information in the FCS (see next slides)
Straw Poll 2: Do you support that the Address field is 12 bits?
  YES, NO, ABS
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | TBD | 12 | TBD

## Slide 6: Address field
WID is the WUR ID provided by the AP and contains an identifier of both RX and TX [2]
GID is the GROUP ID provided by the AP and contains an identifier of both RXs and TX [1]
TXID is a 12 bit subset of the BSSID and is decided by the AP
  Which bits and how they are selected is TBD (some contributions also point to the use of BSS Color [2])
OUI1 is the 12 MSBs of the OUI [4]
* & ** These WUR frame types are currently under discussion.
Straw Poll 3: Do you support that Address field has contents as defined in this slide (for those frames that are approved)?
  YES, NO, ABS
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | TBD | 12 | TBD
Address field [B0-B7] | Address field [B8-B11] | WUR frame
WID |  | Unicast Wake Up
GID |  | Multicast Wake Up
TXID |  | Beacon, Broadcast Wake Up, Discovery[5]*
OUI1 |  | Vendor Specific[4]**

## Slide 7: TD Control
TD Control field contains type dependent control information
  Motioned: WUR Beacon contains the partial TSF [1]
  Under Discussion: Wake Up frame contains packet number/partial TSF, …
    Depending on functionality and security protocol and is TBD [1, 7]
Proposal: The TD Control field is 12 bits in length
  For WUR Beacon contains 12 bits of partial TSF [1, 6]
Straw Poll 4: Do you support that the TD Control field is 12 bits?
  YES, NO, ABS
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | 8 | 12 | 12

## Slide 8: Frame Body
The Frame Body field is optionally present (and optional in RX)
  As such it should be present only in variable length WUR frames
    Length should be in multiple of octets to simplify frame parsing and upper bounded
  Long WUR frames use significant airtime at low rate (e.g., 16B uses ~2.1ms time@62.5 Kbps)
    Beneficial to put airtime limitations so that long WUR frames can be sent only at high data rate
Proposal:
  Frame Body field is not present in constant length WUR frames
  Frame Body field is present in variable length WUR frames
    The length of the Frame Body field is indicated by the Length field
    The length is in units of TBD octets, and is up to 8 or 16 (TBD) octets.
  There is a TBD max TX time duration for WUR PPDUs
Straw Poll 5: Do you support the proposal in this slide?
  YES, NO, ABS
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | TBD | 12 | TBD

## Slide 9: FCS
The FCS carries the CRC of the frame
  Length and computation of the FCS is TBD
To reduce false alarm probability we propose to “hide” additional BSSID info.:
  AP XORs BSSID info (e.g., BSSID[23:38]) with the FCS or,
  AP computes CRC assuming BSSID info is present in the frame but BSSID info is not sent
  STA successfully decodes only WUR frames generated by its AP
    WUR frames generated by other APs are received as corrupted
    CRC fails due to different BSSID info w.r.t. BSSID info expected by the STA
Straw Poll 6: Do you agree to additionally embed BSSID information in the FCS?
  How to embed the BSSID information in the FCS is TBD
  It is not applicable for pre-association WUR frames
  YES, NO, ABS
MAC Header | Frame Body | FCS
 | Frame Control | Address | TD Control
Bits | 8 | 12 | 12
CRC
TBD

## Slide 10: References
[1] 11-17/1004r4 Considerations on WUR frame format (A. Asterjadhi, et. al.)
[2] 11-17/1115r5 11ba wakeup frame format (L. Chu, et. al.)
[3] 11-17/977r4 Address structure in unicast wake-up frame (J. Kim, et. al.)
[4] 11-17/1008r0 Vendor Specific WUR Frame Follow up (P. Huang, et. al.)
[5] 11-17/1608r0 WUR Discovery Frame for Smart Scanning (G. Li, et. al.)
[6] 11-17/1384r0 WUR synchronization (Y. Seok, et. al.)
[7] 11-17/1368r2 BSS parameters update notification (M. Gan, et. al.)