## Slide 1: Beamforming for mmWave Distribution Networks
Date: 2017-11-01
Name | Affiliation | Address | Phone | Email
Oren Kedem | Intel |  |  | oren.kedem@intel.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Carlos Aldana | Intel |  |  | carlos.h.aldana@intel.com
George Cherian | Qualcomm |  |  | gcherian@qti.qualcomm.com
Assaf Kasher | Qualcomm |  |  | akasher@qti.qualcomm.com
Solomon Trainin | Qualcomm |  |  | strainin@qti.qualcomm.com

## Slide 2: Introduction and problem statement
The beamforming paradigm defined in 11ad/11ay assume that:
  Transmitted BF frames are always separated by a known interframe space (SBIFS, MBIFS, LBIFS)
  Initiator and responder training take place back to back (e.g., ISS->RSS->Feedback->Ack)
This paradigm is not suitable to networks employing the TDD channel access [1][2], given the strict delineation between TX and RX TDD-Slots
Therefore, in this presentation we propose a BF protocol suited to TDD channel access

## Slide 3: Outline
Review of beamforming approach described in [2]
  Asynchronous BF
  Synchronous BF
TDD beamforming proposal
  BF protocol
  Frame formats

## Slide 4: Asynchronous BF: assumptions
Asynchronous beamforming is the case when the frame and slot boundary timing is unknown to the Responder
  Responder starts in continuous sweep, switches to slotted sweep after being hit with a beam
The asynchronous BF procedure assumes reciprocity
Responder knows (provided through SME with)
  Number of Tx beams used by initiator
  Continuous sweep period

## Slide 5: Asynchronous BF
TrnReq packets continue to be transmitted until initiator decides to stop the training (i.e., multiple TrnRsp and TrnRspAck frames can be exchanged during beamforming.)
The size of two TrnReq messages is assumed to be the size of a slot (cannot be assumed by 11ay)
TrnReq are transmitted in every first slot of a frame; this assumption helps the CN to calculate the time to send the TrnRsp
The partition between TX/RX slots is assumed to be equal

## Slide 6: Synchronous BF
Synchronous beamforming is the case when the frame and slot boundary timing is known to the Responder
  Responder starts in slotted sweep, using a schedule
Initiator behavior does not change compared to asynchronous BF
SME indicates to responder when to start synchronous BF, so that the responder can start scanning
Rest of the procedure is nearly the same

## Slide 7: BF: implications to 11ay
In 11ay, the slot structure may vary between implementations
Hence, the 11ay asynchronous BF procedure can only assume:
  Reciprocity (antenna pattern)
  Number of RX sectors of responder
The 11ay asynchronous BF procedure cannot assume
  Frame size (TDD Slot)
  Split of frame TX and RX

## Slide 8: Outline
Review of beamforming approach described in [2]
  Asynchronous BF
  Synchronous BF
TDD beamforming proposal
  BF protocol
  Frame formats

## Slide 9: TDD beamforming: considerations & definitions
The cornerstone of all existing 11ad/11ay BF protocols are the SSW and BRP frames, which are used in the SLS and BRP beamforming phases
Attempting to reuse these frames or protocols to define the TDD beamforming protocol is impractical:
  Will lead to incorrect legacy (11ad) device behavior, since legacy devices will assume the traditional 11ad BF protocol
  Behavioral exceptions will have to be created in numerous places
  Complex to merge two disparate procedures
Propose to define a separate BF frame and protocol:
  Define new TDD Beamforming frame of subtype Control Frame Extension
  Define new TDD beamforming procedure

## Slide 10: New Control Frame Extension – TDD Beamforming
Type value B3 B2 | Subtype value B7 B6 B5 B4 | Control Frame Extension value B11 B10 B9 B8 | Subtype description
01 | 0110 (Control) | 1001 | SSW-Feedback
01 | 0110 (Control) | 1010 | SSW-Ack
01 | 0110 (Control) | 1011 | TDD Beamforming
01 | 0110 (Control) | 1100-1111 | Reserved

## Slide 11: TDD Beamforming frame format
TDD Beamforming frame defined as Control Frame Extension subtype
TDD BF frame includes the following fields:
  Duration - Set to the time until the end of the TDD slot where the TDD Beamforming frame is transmitted.
  RA - Contains the MAC address of the STA that is the intended receiver of the frame.
  TA - field contains the MAC address of the transmitter STA of the frame.
  TDD BF Control field –
    TDD BF Frame Subtype - Indicates the frame subtype
    End of Training – Indicates the end of BF training
 | Frame Control | Duration | RA | TA | TDD BF Control | Frame Body | FCS
Octets : | 2 | 2 | 6 | 6 | 1 | 6 | 4
 | TDD BF Frame Subtype | End of Training | Reserved
Bits: | 2 | 1 | 5
TDD Beamforming frame format
TDD BF Control field format
  TDD BF Frame Subtype subfield
    0 – TDD SSW
    1 – TDD SSW Feedback
    2 – TDD SSW Ack
    3 - Reserved

## Slide 12: TDD SSW frame
 | Frame Control | Duration | RA | TA | TDD BF Control | Frame Body | FCS
Octets : | 2 | 2 | 6 | 6 | 1 | 6 | 4
TDD Beamforming frame format
TDD SSW frame body content
 | B0 B9 | B10 B11 | B12 B26 | B27 B41 | B42 B45 | B46 B47
 | TX Beam Index | CDOWN | Responder Feedback Offset | Initiator Ack Offset | Periodicity | Reserved
Bits : | 10 | 2 | 15 | 15 | 4 | 2
TDD BF Control field format
Tx Beam Index - Indicates the beam index used by the initiator to transmit the frame.
CDOWN - Indicates the number of TDD SSW frames remaining to be transmitted within a TDD slot, such that the last transmitted TDD SSW frame in the TDD slot has this field equal to zero.
Responder Feedback Offset - Indicates the offset, in units of 1 µs, beginning immediately after the end of the TDD SSW frame, when the TDD SSW Feedback frame is transmitted by the responder station.
Initiator Ack Offset- Indicates the offset, in units of 1 µs, beginning immediately after the time indicated by the Responder Feedback Offset field when the TDD SSW Ack frame is transmitted by the initiator.
Periodicity – Indicates the offset, in units of TBD us, to the start of the next TDD slot used for TDD SSW transmission by the initiator.
 | TDD BF Frame Subtype | End of Training | Reserved
Bits: | 2 | 1 | 5

## Slide 13: TDD SSW Feedback frame
 | Frame Control | Duration | RA | TA | TDD BF Control | Frame Body | FCS
Octets : | 2 | 2 | 6 | 6 | 1 | 6 | 4
TDD Beamforming frame format
TDD SSW Feedback frame body content
 | TDD BF Frame Subtype = 1 (TDD SSW Feedback) | End of Training | Reserved
Bits: | 2 | 1 | 5
TDD BF Control field format
 | B0 B9 | B10 B19 | B20 B27 | B28 B47
 | TX Beam Index | RX Beam Index | SNR Report | Reserved
Bits : | 10 | 10 | 8 | 20
TX Beam Index - Indicates the beam index received from the initiator
RX Beam Index - Indicates the RX beam index used by the responder while it decoded the respective TDD SSW transmitted by the initiator in the indicated TX Beam Index.
SNR Report - Indicates the SNR achieved while decoding the respective TDD SSW transmitted in the indicated TX Beam Index.

## Slide 14: TDD SSW Ack frame
 | Frame Control | Duration | RA | TA | TDD BF Control | Frame Body | FCS
Octets : | 2 | 2 | 6 | 6 | 1 | 6 | 4
TDD Beamforming frame format
TDD SSW Ack frame body content
 | TDD BF Frame Subtype = 2 (TDD SSW Ack) | End of Training | Reserved
Bits: | 2 | 1 | 5
TDD BF Control field format
 | B0 B9 | B10 B17 | B18 B33 | B34 B41 | B42 B45 | B46 B47
 | TX Beam Index | SNR Report | Initiator Management Offset | Responder Management Offset | Periodicity | Reserved
Bits : | 10 | 8 | 16 | 8 | 4 | 2
TX Beam Index - Indicates the TX beam index received from the responder
SNR Report - Indicates the SNR achieved while decoding the TDD SSW Feedback frame received in the indicated TX beam index.
Initiator Management Offset- Indicates the offset, in units of 1 µs, beginning immediately after the end of the TDD SSW Ack frame when the Management frame carrying the network configuration is to be transmitted by the initiator.
Responder Management Offset - Indicates the offset, in units of 1 µs, beginning immediately after the time indicated by the Initiator Management Offset field when the responder is expected to respond to the Management frame sent by the initiator.
Periodicity – Indicates the offset, in units of TBD us, to the start of the next TDD slot used for retransmission of the initiator Management frames.

## Slide 15: TDD beamforming: Asyn/Sync procedure (0)
Initiator sends multiple TDD SSW frames indicating the Initiator TX Beam Index and the time to send TDD SSW Feedback response
Responder sends a TDD SSW Feedback frame with information on the decoded initiator beams.
In response, the initiator sends a TDD SSW Ack frame with indications on how the responder can obtain the network configuration parameters.
During the procedure, the TDD SSW frame is sent periodically and will typically span all of the initiator’s beam indexes.
For asynchronous beamforming, responder changes sweeping pattern from continuous to slotted when hit with a beam.

## Slide 16: TDD beamforming: Async procedure (1)
TDD BF Frame set to subtype TDD SSW may be sent in any TDD slot assigned to the initiator and includes the following indications:
  Tx Beam Index – Initiator Beam Index
  CDOWN – indicates the number of TDD SSW frames remaining to be transmitted within a TDD slot
  Responder Feedback Offset – Indicates to the responder when to send its training feedback. This value is updated at every TDD SSW transmission.
  Initiator Ack Offset - Indicates to the responder when initiator will send its feedback in response to the responder’s training feedback.

## Slide 17: TDD beamforming: Async procedure (2)
Initiator sends multiple TDD BF frame with subtype set to TDD SSW.
Upon reception of a TDD SSW frame, the responder sends a TDD BF frame with subtype set to TDD SSW Feedback and including the decoded TX beams from the initiator
After receiving the TDD SSW Feedback frame, the initiator sends a TDD BF frame with subtype set to TDD SSW Ack at the time as indicated in the Initiator Ack Offset subfield in the TDD SSW frame. The frame includes the decoded TX Beam of the responder and the offset time to exchange concluding management frames.
During the initiator’s TDD SSW Ack transmission, the responder adjusts its beam to the preferred antenna configuration as indicated by the RX Decoded Beam field.
If the expected TDD BF Frame was not received, the BF procedure is assumed to be unsuccessful and may be repeated

## Slide 18: TDD beamforming: Sync procedure
Sync BF may be initiated after Async BF is concluded or anytime when the STA is associated to network.
Sync BF is similar to Async BF with the following modifications
Initiator
  Starts with TXBeamIDx =0 after asynchronous BF has completed and ends with the maximum TXBeamIDx. (Antenna configuration may be communicated via TDD Beamforming frame (subtype TDD SSW Ack).
  Transmitted TDD BF frame in a TDD slot is done according to the periodicity as indicated in the TDD SSW frame.
Responder
  Responder is timestamp synchronized and knows the network TDD slot structure.
  Responder switches it RX beams according to the periodicity indicted in the TDD SSW frame.
  Responder responds with a TDD BF frame set to TDD SSW Feedback subtype at the time indicated in the Response Feedback Offset value.

## Slide 19: TDD Route element format
The TDD Route element is used to communicate the initiator TX beams as received by the STA during a TDD beamforming procedure
 | B0 B9 | B10 B17 | B18 B23
 | RX Decoded Beam Index | RX Decoded Beam Link Quality | Reserved
Bits : | 10 | 8 | 6
 | Element ID | Length | Element ID Extension | Number of TDD Routes | TDD Route 1 | …. | TDD Route N
Octets : | 1 | 1 | 1 | 2 | Variable |  | Variable
 | TX Beam Index | Number of Decoded RX Beam | Decoded RX Beam Information 1 | …. | Decoded RX Beam Information M
Octets : | 2 | 1 | 3 |  | 3
TX Beam Index - Indicates the beam index received from the DN
RX Decoded Beam Index - Indicates the RX beam index used by the responder while it decoded the respective TDD SSW transmitted in the respective TX Beam Index.
RX Decoded Beam Link Quality - Indicates the SNR achieved while decoding the respective TDD SSW transmitted in the indicated TX Beam Index. The first RX Decoded Beam Link Quality indication field indicates the preferred beam to be used by the initiator and responder

## Slide 20: TDD BF procedure (example 1)
TDD SSW
TDD SSW Feedback
TDD SSW
TDD SSW Ack
TDD SSW
TDD SSW
TDD SSW Ack
TDD SSW
TDD SSW Feedback
Management exchange (Probe, Information Request ..)
Includes TDD Route IE, TDD Slot IEs
End of Training = 1
End of Training = 1
End of Training = 1
Periodicity
Management exchange retries (Probe, Information Request ..)
Includes TDD Route IE, TDD Slot IEs
Periodicity
Initiator offset
Responder offset
End of Training = 0
Management exchange timings (including retries) are in the TDD SSW Ack frame with “End of Training” set to 1

## Slide 21: TDD BF procedure (example 2)

## Slide 22: Conclusions
This contribution proposes a BF procedure that can be used in networks that employ TDD channel access [2]
  Not meant to be applicable if TDD channel access is not in use
For the reasons and as described in [2], the BF procedure incorporates the concept of asynchronous and synchronous BF
We invite contributions to enhance this procedure

## Slide 23: Straw poll
Do you agree with the beamforming approach described in this presentation (slides 9-21) to be used during TDD SPs?
  Yes
  No
  Abstain

## Slide 24: References
[1] IEEE 802.11-17/1019r2 “mmWave Mesh Network Usage Model”
[2] IEEE 802.11-17/1321r0 “Features for mmW Distribution Network Use Case”

## Slide 25: Backup

## Slide 26: Can we use Channel Measurement IE for the responder feedback ?
Channel Measurement Feedback include the following parameters:
Using the Channel Measurement feedback as the TDD BF Responder FB issues:
  Channel Measurement FB IE list the number of TX Sector ID used by the initiator, while in TDD Route IE indicate the following:
  TX Beam Index x Number of Decoded RX Beam x (RX Sector ID (11bit) + SNR (9bits)
  Sector ID (6bit) + Antenna ID (2 bit)] are total of 8 bits which is not suffice for the 11bit TX Beam
Conclusion – Channel Measurement IE is not suitable for the TDD case
SNR | SNR (8bit) …x N meas
Channel Measurement | (I Component (8bit) + Q Component (8bit)) x N meas
Tap Delay | - Tap Delay (8bit) x N Tap
Sector ID | - [Sector ID (6bit) + Antenna ID (2 bit)] x N beam
NOTE: The format and size of the Channel Measurement Feedback element are defined by the parameter values specified in the accompanying DMG Beam Refinement element.