## Slide 1: Ack/BA for mmWave Distribution Networks
Authors:
Name | Company | Address | Phone | Email
George Cherian | Qualcomm |  |  | gcherian@qti.qualcomm.com
Lochan Verma | Qualcomm |  |  | lverma@qti.qualcomm.com
Solomon Trainin | Qualcomm |  |  | strainin@qti.qualcomm.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Carlos Aldana | Intel |  |  | carlos.h.aldana@intel.com
Oren Kedem | Intel |  |  | oren.kedem@intel.com
SungJin Park | LGE |  |  | allean.park@lge.com

## Slide 2: Introduction
TDD Channel Access in mmWave Distribution Network discussed in [1]
Need for scheduling of Ack/BA in mmWave Distribution Network discussed in [2]
Terminology | Example values
TDD-slot | 66us
TDD-interval | 400us
SP with TDD channel access | Bandwidth grant (25.6ms)
This contribution proposes Ack/BA mechanism for TDD Channel Access
BTI
A-BFT
ATI
CBAP1
SP1
SP with TD channel access
CBAP2
TDD-interval 1
TDD-interval 2
TDD-interval-n
…
TDD-slot0
TDD-slot1
TDD-slot2
TDD-slot3
TDD-slot4
TDD-slot5
E.g., for TX
E.g., for RX
Access assignment to STAs (CNs, DNs)

## Slide 3: Requirements for sending Ack/BA - I
1. Minimize the existing spec
  Would like to use the ‘Immediate Ack’ policy with the extensions identified in this contribution
2. A TDD-slot structure that consists of different slot-sizes to accommodate different traffic
  TDD-Slot structure should be flexible to address different traffic profiles
    Two extreme examples are (i) unidirectional traffic, and (ii) bi-directional traffic with equal volume on both directions
  In the case of unidirectional traffic, traffic on reverse direction is primarily acknowledgements (TCP Ack, and block-acks). So, having short slots allocated for reverse direction is preferred for efficiency reasons.
  Since the slot-structure is expected to be semi-static, a slot-structure that consists of short-slots should be usable in a bi-directional traffic as well.
    Since the small slot may not be able to carry a full data-MPDU, the scheduler should be able to send Block-Ack in a small slots
    This creates a situation, where a longer slot and a shorter slot is allocated to the same node, and the block-ack is sent in the shorter slot
TDD-interval 0
TDD-slot 0
TDD-slot 2
TX Polarity
TDD-slot 1
TDD-slot 3
TDD-slot 5
RX Polarity
TDD-slot 4
A->B
A->C
A->D
B->A
C->A
B->A
Ack sent at this slot

## Slide 4: Requirements for sending Ack/BA - II
3. Acknowledgement may be sent in a reverse TDD-slot that is in a different TDD Interval
  Scheduler may not be able to fit acknowledgement for different nodes in the same TDD-Interval
  Ack/BA for certain nodes may be sent at a later slot
TDD-Interval 0
TDD-slot 0
TDD-slot 2
TX Polarity
TDD-slot 1
TDD-slot 3
TDD-slot 5
RX Polarity
TDD-slot 4
A->B
A->C
A->D
B->A
C->A
D->A
Ack sent at this slot
(different TDD-Interval)
TDD-Interval 1
TDD-slot t11
……
B->A

## Slide 5: Proposal summary
Define a two category of TDD-Slots
  ‘Data-only TDD-Slots’: TDD-Slots that are permitted to carry only data frames
  ‘Basic TDD-Slots’: TDD-Slots that are permitted to carry any frame including Control frames and Management frames. The goal would be to prioritize the Control & Management frames if the TDD-Slot were to be shared with data frames
Ack/BA are sent at the next scheduled reverse TDD-Slot that permits the transmission of Ack/BA, after the transmission of Data frame
  So, Ack Timeout will be a variable value
  During the Basic slot, prioritize Ack/BA over Data/Management
Both eliciting node and responding node knows the ‘next scheduled reverse TDD-Slot that permits the transmission of Ack/BA’ from the ‘TDD Slot Schedule element’.
  No need to explicitly signal the time-out value

## Slide 6: What about other immediate control responses?
RTS/DMG CTS/DMG DTS
  Delayed response doesn’t help with the intended protection
  Will not be able to silence legacy devices due to CTSTimeout
Grant/Grant Ack
  Not needed for TDD-Slot mode, since schedule is transmitted through Announce frame
Response frame in ATI
  Not relevant for TDD-Slot mode

## Slide 7: Standards changes (high level)
Add a classification to each TDD-Slots
  Add a new field called ‘slot-category’ in the ‘TDD Slot Schedule element format’ with the following values:
    Basic TDD slot: A slot that has no restriction on the type of frames
    Data-only TDD slots: A slot that permits only QoS data frames
  The above field indicates what type of frames can be carried in the assigned slot
Change the Ack Timeout rule
  Current spec:
    “After transmitting an MPDU that requires an Ack or BlockAck frame as a response (see Annex G), the STA shall wait for an AckTimeout interval, with a value of aSIFSTime + aSlotTime + aRxPHYStartDelay, starting at the PHY-TXEND.confirm primitive”
  New rule for TDD Ack/BA (not the exact normative text):
    “After transmitting an MPDU that requires an Ack or BlockAck frame as a response, the STA shall wait for an AckTimeout interval, with a value of duration from the beginning of the slot that carried the MPDU to the end of the first available basic slot on the reverse direction, starting at the PHY-TXEND.confirm primitive”
      Do we need to add aSIFSTime + aSlotTime + aRxPHYStartDelay?
Changes on sending the Ack/BA (not exact normative text)
  A recipient of a QoS Data frame, or Management frame that solicits immediate acknowledgement shall respond with BlockAck/Ack frame in first reverse slot that permits Ack/BlockAck transmission (where the slot category is set to Basic slot).

## Slide 8: Standards change summary (contd)
10.36.7 - 10.36.9 : Dynamic allocation/truncation/extension of Service Period
  Prohibit Poll frame
Backoff procedure
  No exponential backoff when a transmission fails.

## Slide 9: Reference
IEEE 802.11-17/1323r2, ‘Scheduling for mmWave Distribution Networks’
IEEE 802.11-17/1065r1, ‘Ack and Block Ack Handling for mmWave Distribution Network Use Case’

## Slide 10: SP#1
Do you agree to add a new field called ‘slot-category’ in the ‘TDD Slot Schedule element format’ with the following values:
    Basic TDD slot: A slot that has no restriction on the type of frames
    Data-only TDD slots: A slot that permits only QoS data frames
  The above field indicates what type of frames can be carried in the assigned slot

## Slide 11: SP#2
Do you agree to define ACK/BA transmission rule when SP with TDD channel access is used as follows (not normative text below)
  A recipient of a QoS Data frame, or Management frame that solicits immediate acknowledgement shall respond with BlockAck/Ack frame in first reverse slot that permits Ack/BlockAck transmission (where the slot category is set to Basic slot).

## Slide 12: SP#3
Do you agree to define AckTimeout value when SP with TDD channel access is used as follows (not the exact normative text)
  “After transmitting an MPDU that requires an Ack or BlockAck frame as a response, the STA shall wait for an AckTimeout interval, with a value of duration from the beginning of the slot that carried the MPDU to the end of the first available basic slot on the reverse direction, starting at the PHY-TXEND.confirm primitive”