## Slide 1: WUR channel issue
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
We have presented WUR channel issues in previous meetings
  Channel switch
  Channel selection
  Multiple Channel
We will revisit WUR channel issues and gather groups opinion

## Slide 3: Channel switch
We have proposed channel switch for WUR in previous submission[1]
  We suggested reuse Channel Switch Announcement(CSA) element which is defined in IEEE 802.11-2016
  AP needs to have the ability to indicate channel switching information to WUR STAs which are operating in power saving mode

## Slide 4: Channel selection
Channelization for WUR would have an impact on performance of WUR and PCR
We have many options for WUR channelization, and we have analyzed in previous submission[2]
WUR channel is recommended for being defined in non-DFS channel
Also TG have discussed dual-band concurrent AP case [3]
  Dual-band concurrent AP can support 2.4 GHz band and 5 GHz band simultaneously

## Slide 5: Channel selection
Following options are possible in WUR channelization for single-band AP when the AP is operating in non-DFS channel
  Option 1: WUR channel should be defined on primary channel of PCR
  Option 2: WUR channel should be defined on primary or secondary channels of PCR
  Option 3: WUR channel should be defined on any non-DFS 20 MHz channels in same frequency band of PCR
  Option 4: WUR channel can be defined on any non-DFS 20 MHz channels in any frequency band

## Slide 6: Channel selection
Following options are possible in WUR channelization for single-band AP when the AP is operating in DFS channel
  Option 1: WUR channel should be defined on any non-DFS 20 MHz channels in 5 GHz band
  Option 2: WUR channel should be defined on any 20 MHz channels in 2.4 GHz band
  Option 3: WUR channel can be defined on any non-DFS 20 MHz channels in any frequency band

## Slide 7: Channel selection
Following options are possible in WUR channelization for dual-band concurrent AP
  Option 1: WUR channel should be defined in 2.4 GHz band
  Option 2: WUR channel should be defined in 5 GHz band
  Option 3: WUR channel can be defined in 2.4 GHz or 5 GHz band

## Slide 8: Multiple channel
WUR can define and use multiple sub-channels in 20 MHz channel

## Slide 9: Multiple channel
Following options are possible in multiple channel support in WUR
  Option 1: Define multiple WUR channels in 20 MHz channel and use multiple WUR channels for transmitting Wake-up packet
  Option 2: Define multiple WUR channels in 20 MHz channel and use one WUR channel for transmitting Wake-up packet
  Option 3: WUR doesn’t define multiple channels on 20 MHz channel

## Slide 10: Reference
[1] 11-17-0380-00-00ba-wur-channel-switch.pptx
[2] 11-17-0031-00-00ba-channel-issue-in-wur.pptx
[3] 11-17-1333-02-00ba-wur-operating-channel.pptx

## Slide 11: Straw poll 1
Do you support following sentences?
  11ba spec shall define a mechanism to indicate channel switch information for WUR STA
    Channel switch indication procedure reuses CSA element

## Slide 12: Straw poll 2
Which option do you prefer for WUR channel when a single-band AP is operating in non-DFS channel?
  Option 1: WUR channel should be defined on primary channel of PCR
  Option 2: WUR channel should be defined on primary or secondary channels of PCR
  Option 3: WUR channel should be defined on any non-DFS 20 MHz channels in same frequency band of PCR
  Option 4: WUR channel can be defined on any non-DFS 20 MHz channels in any frequency band

## Slide 13: Straw poll 3
Which option do you prefer for WUR channel when a single-band AP is operating in DFS channel?
  Option 1: WUR channel should be defined on any non-DFS 20 MHz channels in 5 GHz band
  Option 2: WUR channel should be defined on any 20 MHz channels in 2.4 GHz band
  Option 3: WUR channel can be defined on any non-DFS 20 MHz channels in any frequency band

## Slide 14: Straw poll 4
Which option do you prefer for WUR channel when a dual-band concurrent AP is operating in both 2.4 and 5 GHz band simultaneously?
  Option 1: WUR channel should be defined in 2.4 GHz band
  Option 2: WUR channel should be defined in 5 GHz band
  Option 3: WUR channel can be defined in 2.4 GHz or 5 GHz band

## Slide 15: Straw poll 5
Do you agree to add following text in SFD?
  AP decides the WUR operating channel in the band(s) supported by the associated non-AP STA operating in WUR Mode
    WUR operating channel should be defined on non-DFS channel
    WUR operating channel should not be defined in 5 GHz band when a PCR channel of AP is located in 2.4 GHz band

## Slide 16: Straw poll 6
Do you agree to add following text in SFD?
  11ba spec shall define multiple WUR channels in 20 MHz channel
    Number of multiple WUR channels in 20 MHz channel is TBD
    Use of multiple WUR channel is TBD