## Slide 1: WUR operation of WUR
Date: 2017-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Taewon Song |  |  |  | taewon.song@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Even though our SFD has been almost done, some of basic MAC procedures are still unclear
  We will address and make clear these unclearness

## Slide 3: MAC overall procedure

## Slide 4: 1. Association
WUR capability information will be delivered between AP and STA during association procedure
  Remaining resource for WUR operation at AP side (WUR ID space, etc...)
  Supported transmission rate for Wake-up packet
  Supported operating class for WUR channel
  Mode transition delay
  Optional features
    Nonzero-length Frame Body support
We may need a new IE for WUR capability

## Slide 5: 2. WUR mode signaling (entry)
Two management frames (WUR mode request/response) will be defined for WUR mode signaling
WUR mode signaling incorporates WUR negotiation
After WUR mode signaling, a STA can enter into PM-WUR mode by existing signaling

## Slide 6: 2. WUR mode signaling (entry)
Parameters for WUR mode signaling
  WUR mode request
    Mode indication (Entry or Termination)
    Timeout value for unicast wake-up packet
    Channel quality information
    Preferred duty cycle parameter (current power headroom, ON/OFF Duration, starting point)
  WUR mode response
    Status code (accept or deny with reason)
    WUR ID Allocation (Individual, group)
    Duty cycle information
    WUR channel information
    Transmission rate for unicast Wake-up packet
    TSF, WUR beacon information (Interval, TBTT)

## Slide 7: Issues - WUR mode signaling
Do we need WUR mode response frame for all WUR mode change?
  No, WUR response frame is mandatory for entry case but optional for termination case
Do we need a separated negotiation procedure before mode signaling for entry case?
  No, negotiation is embedded in WUR mode signaling

## Slide 8: 3. Data reception in WUR mode
If a STA received unicast Wake-up packet in PM-WUR mode, it shall response by PS-Poll (PM=0) in active-WUR mode
  It maintains active-WUR mode until the AP has transmitted all buffered DL data
After finishing all data reception, the STA will return to PM-WUR mode by existing signaling (PM=1)

## Slide 9: Issues - Data reception in WUR mode
Detail operation can vary depending on which existing power saving feature was used
  If TWT is used, for example, response frame of wake-up packet may be transmitted in service period
  However, it isn’t suitable and efficient
So we are proposing that an WUR STA follows rule in previous slide whatever existing power saving feature is used
  Multicast and broadcast wake-up packet case is TBD

## Slide 10: 4. WUR mode signaling (termination)
WUR mode response can be omitted in WUR mode signaling for termination
Once WUR mode is terminated, the STA can operate in existing PS mode or move to active mode

## Slide 11: Summary
In this submission, we reviewed MAC basic features and proposed detail operations
  WUR capability information element
  Two management frame for WUR mode signaling and negotiation
  Data reception method in WUR mode

## Slide 12: Straw poll 1
Do you agree to add following text in SFD?
  Define Information Element for WUR capability information
    Remaining resource for WUR operation at AP side (WUR ID space, etc...)
    Supported transmission rate for Wake-up packet
    Supported operating class for WUR channel
    Mode transition delay
    Optional features
      Nonzero-length Frame Body support
    Other information is TBD

## Slide 13: Straw poll 2
Do you agree to modify following text in the SFD?
  WUR mode signaling shall be defined for the WUR STA to enter the WUR mode by explicit signalling:
    WUR mode signaling is done on the Primary connectivity radio.
      An WUR STA shall send WUR Mode Request frame when it wants to enter or terminate WUR mode
      An AP that received WUR Mode Request frame may send WUR Mode Response frame to the STA
    Wake-up operating parameter is notified in WUR mode signalling:
      Detailed parameters are TBD.

## Slide 14: Straw poll 3
Do you agree to modify following text in the SFD?
  WUR mode signaling shall be defined for the WUR STA to enter the WUR mode by explicit signalling:
    WUR mode signaling is done on the Primary connectivity radio.
    Wake-up operating parameter is notified in WUR mode signalling:
      Detailed parameters are TBD.
      WUR mode request: Mode indication, Timeout value for unicast wake-up packet, Channel quality information, Preferred duty cycle parameter
      WUR mode response: Status code, WUR ID Allocation, Duty cycle information, WUR channel information, Transmission rate for Wake-up packet, TSF, WUR Beacon information

## Slide 15: Straw poll 4
Do you agree to add following text in SFD?
  WUR STA follows rules which are described in slide 8 whatever existing power saving feature is used
    Multicast and broadcast wake-up packet case is TBD