## Slide 1: False Radar Pulse Detection on WUR Signals in DFS Channel
Date: 2017-11-06
Authors:

## Slide 2: Overview
In document IEEE 802.11-17/0377r0 we showed a very high false radar pulse detection rate on Wake-Up Radio (WUR) signals in Dynamic Frequency Selection (DFS) channels, where radar detection is required for DFS Master Devices
Particularly when the WUR signal is received on a secondary subchannel of a DFS Master Device
The issue is that the L-SIG is not demodulated, an thus its length field is not honored, while the WUR On-Off-Keying (OOK) signal is rather narrowband and has many rising edges, which could easily trigger a radar detector

## Slide 3: Proposed Solution
In March 2017, TGba approved the following text in the SFD, in R.3.3.A:
  The operation in DFS channels is TBD
Since TGba has adopted OOK as modulation scheme for WUR signals, to mitigate false radar pulse detects, we propose to limit the operation of WUR to non-DFS channels
  A client with a WUR receiver is relieved from the burden of potentially frequent channel switching due to the DFS master’s radar detection outcome

## Slide 4: Straw Poll
Do you support changing
  The operation in DFS channels is TBD
to
  The operation in DFS channels is disallowed
in R.3.3.A of the SFD?
Y/N/Abstain:

## Slide 5: Motion
Move to make the following change to TGba SFD
Change
  The operation in DFS channels is TBD
to
  The operation in DFS channels is disallowed
Y/N/Abstain:

## Slide 6: Backup Slides

## Slide 7: Simulation Setup
1x1
80 MHz channel bandwidth
Primary20 on second subchannel from the left
WUR signal from OBSS on third subchannel from left
  WUR signal:
    has a 20 MHz 11a preamble with L-SIG rate at 6 Mbps and a length spoofing equivalent to 1 ms
    has a 1 ms On-Off Keying (OOK) payload with a bandwidth of 4 or 10 MHz, and 8 us symbols with a 4 us On and 4 us Off period or vice versa
WUR signal is received at -60 dBm
Radar detection enabled

## Slide 8: 4 MHz WUR Signal
Zoomed in at first 125 µs

## Slide 9: Simulation Results
In AWGN we see 94% false radar pulse detects on 4 MHz WUR signals
In D-NLOS we see 100% false radar pulse detects on 4 MHz WUR signals
In D-NLOS we see 52% false radar pulse detects on 10 MHz WUR signals
From experience we can say that such high false pulse detect rates sooner or later result in false pattern recognitions, leading to false radar detects
  Any false radar detect will force the WLAN network to vacate the DFS channel for 30 minutes