## Slide 1: MAC considerations for the V2P use case
Date: November 6 2017
Authors:
Name | Affiliations | Address | Phone | Email
James Lepp | BlackBerry Limited | 1001 Farrar Road, Ottawa, ON, Canada | (+1) 613-595-4156 | jlepp@blackberry.com

## Slide 2: Summary
Recap of the V2P usage model and OCB requirements
Recap of past presentations on IEs
  Comment on addressing for OCB
Recommendation for WUR address/identity for OCB
Strawpoll

## Slide 3: V2P Usage Model
Device uses the wake-up receiver to power up into the OCB mode (instead of the regular associated to an AP mode)
How is an OCB frame different from a regular 802.11 frame? The BSSID address field is FF-FF-FF-FF-FF-FF (aka all 1s).
Two types of OCB frames can be sent:
Group Addressed (Broadcast) addressed
Unicast between two STAs
OCB = Outside the Context of a BSS (originally from 802.11p)

## Slide 4: OCB usage
The operation of OCB and what goes in OCB frames is outside the scope of 802.11.
Other standards and specifications describe both what to put in the frames AND when to send the frames.
The goal with the OCB WUR is to similarly enable a WUR trigger frame to allow a low power wake up of devices that operate in the OCB mode.
Don’t need to specify when to send it, or what to do in response to receiving it in 802.11ba.

## Slide 5: Addressing in WUR frames
There have been two general proposals for addressing/identifiers in WUR frames.
From 11-17/977r4, two addresses: a shortened Transmitter Address (µTA) and shortened Receiver Address (µRA). Sometimes I see folks in this group confused between TA and BSSID and for the particular mgmt frame being discussed maybe it doesn’t matter.
From 11-17/1004r4, one address: have a single identification/address field that is unique to the sender-receiver link
In either case a reserved value can indicate OCB WUR frame. (e.g. all 1s). This aligns with how 802.11 identifies OCB today.
Alternatively a flag in the Frame Control could be used instead.

## Slide 6: Addressing of OCB WUR frames
May be desirable to have two reserved values, one for broadcast OCB, and another for unicast OCB.
To enable unicast OCB, an otherwise optional payload will need to contain 2 MAC addresses (or shorthand versions of MAC addresses).
The optional Frame Body described in 11-17/1004r4 can support this.
Based on the use case for V2P, it might be good enough just to define broadcast OCB, as a-priori knowledge of the address of the station you are waking up may be difficult.

## Slide 7: Strawpoll #1
Do you agree to add the following to the 802.11ba SFD:
“For indication of 802.11ba OCB, a reserved value for the address/identity field(s) is used.”
Y
N
A

## Slide 8: Strawpoll #2
Do you agree to add the following to the 802.11ba SFD:
“The reserved address to indicate 802.11ba OCB operation is all 1s (aka all Fs).”
Y
N
A