## Slide 1: Partial OOK – Generalizing the Blank GI Idea
Date: 2017-11-06
Authors:

## Slide 2: Abstract
As an alternative to textbook Manchester coded OOK, it has in e.g. [1] and [2] been proposed to zero-pad the ON part of the signal to further improve the performance
In this contribution we discuss what this gain comes from, how far this approach can be taken in practice, and what the corresponding gain is
Since the idea basically is to send OOK for only part of the time, and nothing during the remaining part, we refer to this as Partial-OOK

## Slide 3: Outline
Motivation
Discussion and estimation of theoretical gain
Discussion of practically achievable gains
Simulation Results
  AWGN – Receive window matched to pulse duration
  TGn channels – Receive window matched to pulse duration
  Discussion of receiver window size
Conclusions

## Slide 4: Motivation
Using “Waveform coding” or blank GI performance gain has been shown, but the potential gain has only been addressed by simulations and the shown results are not entirely consistent
This has motivated us to try to understand what causes the gain and how large the gain can be expected to be in practice
Since the approach allows for very simple implementations, this seems as an attractive approach to explore for TGba

## Slide 5: Discussion of the theoretical gain
In [1] and [2], a gain has been seen by using “wave-form coding” (WFC) or “blank GI”
One reason for this gain can be improved robustness to ISI. However, also for AWGN a substantial gain can be seen
Another point made is that the SNR in the receiver is increased since the noise energy for the decision statistics is reduced for the same signal energy
0
1
0
1
ON
OFF
OFF
ON
“WFC”

## Slide 6: Discussion of the theoretical gain - ISI
By introducing “guard-intervals” between the times where the signal is ON or OFF, ISI will be reduced
However, as has been shown in [3], ISI is not believed to be a problem. The reason being that the channel delay spread is very small compared to the symbol duration
The impact of ISI will be addressed further when the simulation results are presented

## Slide 7: Discussion of the theoretical gain - SNR
Keeping the sent bit energy constant, the received SNR will be inversely proportional to the accumulated noise. If and denote the time when the ON signal is zero and non-zeros respectively, we have
0
1
0
1
ON
OFF
OFF
ON
“WFC”
and

## Slide 8: The Theoretical Gain - SNR
The problem with this reasoning about increased SNR is that it does not take into account how the decision metric is generated, i.e., non-coherently
Instead, looking at the decision metric as a sum of N samples added non-coherently the loss of using more samples can be interpreted as the so-called non-coherent combining loss
The non-coherent combining loss when using diversity for improving the performance over fading channels have the following interesting properties
  It increases with decreased SNR
  Asymptotically, for SNR = -infinity dB, the loss is 10 log10(sqrt(N)), i.e., 1.5 dB for every doubling of N
Recall that the WUR is operating at rather low SNR

## Slide 9: Simple Estimation of the SNR Gain - 62.5 kb/s
Nsamples = 4*80;
for symbol = 1:nrOfSymbols
s(1:NZ) = 1/sqrt(NZ)*ones(1,NZ); % E[s^2] = 1
s(NZ+1:Nsamples) = zeros(1,Nsamples-NZ);
n = 1/(sqrt(Nsamples))*10^(-SNRdB/20)*(randn(1,Nsamples) + i*randn(1,Nsamples))/sqrt(2);
r = abs(s+n);
decision(symbol) = sum(r(1:NZ))<sum(r(NZ+1:2*NZ));
end
BER = sum(decision)/nrOfSymbols;
8 us
Nsamples = 4*80 = 320

## Slide 10: Simple Estimation of the SNR Gain - 62.5 kb/s
The gain by reducing T_NZ 2x is about 1.2 dB
If one would use T_NZ = 40 samples (2us) which is the same as in the 250 kb/s mode, a gain similar to BCC would be obtained
With T_NZ = 20 (1 us) the gain would be even higher, but with small T_NZ things like imperfect sampling will not make it practically feasible to use a correspondingly small receiver window

## Slide 11: Simple Estimation of the SNR Gain - 250 kb/s
Similar gains are seen since the gain comes from a relative decrease in the number of used samples
Practically, the gain becomes harder to obtain as
  Impact of sampling error becomes relatively larger
  The impact of delay spread can (eventually) not be ignored when RMS delay spread is not insignificant compared to T_NZ
We believe P-OOK is mainly of interest for the 62.5 kb/s mode

## Slide 12: Discussion of Practically Achievable Gains
The theoretical gain assumes that the TX power can be increased without limitations. There seems to be at least two reason why this is not possible
  Max TX power constraints. The PA designed based on max TX power and linear requirements for the 802.11 user data
  ACLR requirements. If the (instantaneous) TX power is increased the spectrum regrowth will eventually not meet the TX spectrum mask
OFDM
Shaping
PA
Spectrum analyzer

## Slide 13: Discussion of PA Model
The Rapp model with p = 3 is used, as agreed in [3]
According to [3], referring back to [4], the assumption is that the PA is designed such that the saturation is at 25 dBm, whereas the TX power should be limited to 17 dBm, resulting in an OBO of 8 dB
Based on simulations of 802.11ax [5], considerably less OBO is possible from a TX mask point of view for 11ax. From an EVM point of view, even larger OBO is needed for large MCS

## Slide 14: Discussion of practically achievable gains
If it suffice to fulfill the TX mask used for a 20 MHz channel, a 4 MHz wake-up signal will be no issue even with 0 dB OBO, see left figure
If one would take advantage of using a larger BW, as suggested in [6], a BW of 10 MHz is still feasible with 0 dB OBO, see right figure

## Slide 15: Discussion of practically achievable gains – 4 MHz BW
For a 4 MHz BW, the maximum average power would for PSD limited transmission be 16 dBm
With plain OOK, 19 dBm can be used for the ON part.
With P-OOK, it seems increasing this to 25 dBm is feasible based on the assumptions
This means T_NZ = 40 samples (2 us) for the 62.5kb/s mode

## Slide 16: Discussion of practically achievable gains – 8 MHz BW
8 MHz BW is here just taken as an example, but keeping in mind that this seems to still meet the TX mask also with saturated PA
The maximum average power would for PSD limited transmission be 19 dBm, which is close to the 20 dBm power limitation
With plain OOK, 22 dBm can be used for the ON part.
With P-OOK, it seems increasing this to 25 dBm is feasible based on the assumptions, resulting in T_NZ = 80 samples (4 us) for the 62.5kb/s mode

## Slide 17: Discussion of practically achievable gains – power limited
When there regulatory limitations for the average TX power does not result in a practical problem, i.e., the maximum practically TX power can be used irrespective of T_NZ, then plain OOK is preferred

## Slide 18: Simulation Results - AWGN
Two different simulations are performed, with ideal synchronization and with a practical synchronization algorithm
For T_NZ = 2us and larger, the performance is almost the same
If T_NZ is reduced too much the gain is diminished and may even cause a loss in the performance

## Slide 19: Simulation Results – TGn Channels
Similar performance gains are seen also for the TGnB and TGnD channels

## Slide 20: Simulation Results – Increase Receiver Window Size
For perfect synchronization and no delay spread, a receiver window matched to the sent pulse length gives the best result
For a channel with some delay spread, a somewhat increased receiver window may work equally well, and sometimes even better

## Slide 21: Conclusions
The potential gain of using shorter ON periods for OOK, referred to as P-OOK, was discussed, and it is argued that the gain can be viewed coming from a reduced non-coherent combining loss in the envelope detector
Simulation results supports this reasoning
Taking practical limitations regarding max TX power as well as non-perfect synchronization into account as well, a suitable length of the ON part in case of the 62.5 kb/s mode seems to be 2 us, resulting in a gain similar to the BCC
This choice would also match with the 250kb/s so that the same masking of the OFDM symbol may be applied

## Slide 22: Straw Poll
Do you believe that the idea of shortening the ON time, as discussed in this presentation, in order to allow for improved receiver implementations should be supported in 802.11ba?
Y/N/A:

## Slide 23: References
11-17/1390r1 “Blank GI choices under Timing Errors”, Junghoon Suh et al.
11-17/1347r3 “Symbol Structure”, Eunsung Park et al.
11-17/0188r10 “TGba Simulation scenarios and evaluation methodology document”, Shahrnaz Azizi et al.
11-14/0571r12 “11ax Evaluation methodology”, Ron Porat et al.
11-15/0865r0 “Discussion of ACI performance and ACI requirements for IEEE 802.11ax”, Leif Wilhelmsson
11-17/1017r2 “Variable signal bandwidth of the wake-up signal for enhanced WUR performance”, Leif Wilhelmsson