## Slide 1
Advanced MU-MIMO acknowledgement and PS flow
Authors:
Name | Affiliation | Address | Phone | Email
Ilya Bolotin | Intel | Turgeneva 30, Nizhny Novgorod, 603024, Russia | +7 (831) 2969444 | ilya.bolotin@intel.com
Oren Kedem | Intel |  |  | oren.kedem@intel.com
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Alexander Maltsev | Intel |  |  | alexander.maltsev@intel.com
Artyom Lomayev | Intel |  |  | artyom.lomayev@intel.com

## Slide 2: Legacy MU acknowledgment procedure
PSDU, bytes | BAR/BA exchange overhead, % |  |  |  | 
 | 64 bitmap BA | 256 bitmap BA | 512 Bitmap BA | 1024 Bitmap BA | 2048 Bitmap (25+256)
256 | 94.76 | 95.10 | 95.41 | 95.76 | 96.38
4096 | 93.92 | 94.31 | 94.66 | 95.07 | 95.78
65536 | 82.23 | 83.26 | 84.17 | 85.24 | 87.20
ISSUE 1: BAR/BA exchange causes large overhead increasing the duration of one MU cycle (MU PPDU transmission and its acknowledgement) and therefore significantly reducing throughput

## Slide 3: Legacy MU acknowledgment procedure
To reduce the BAR/BA exchange overhead the following flow could be used (allowed in 11ac):
BUT!!! adopted MU-MIMO power save does not allow such flow (see next slide)

## Slide 4: Legacy MU-MIMO power save
Each STA knows its specific order of BAR/BA exchange.
The BAR/BA order shall be the same as the AIDs appear in the group description present in the EDMG Group ID Set element corresponding to this MU group.
This ordered BAR/BA exchange sequence enables each STA to know when it should wake up to receive the corresponding BAR frame addressed to it.
ISSUE 2: Such approach limits the MU-MIMO acknowledgement flow to only one case: when all STAs are requested for BA after each MU PPDU

## Slide 5: Legacy MU-MIMO power save
MISSED (because STA2 in doze)
Example: PCP/AP elicits BA only from STA 1
STA 2 is not aware of the exact transmission start time of the next MU PPDU.

## Slide 6: Explicitly scheduled BA. MU acknowledgment and PS flow
To resolve both issues we propose the following MU-MIMO acknowledgement and PS flow:
BAR frames are removed from acknowledgement flow in order to reduce overhead. STAs transmit their BA during time slots scheduled by PCP/AP for each STA
PCP/AP schedules time slots for BA transmission for each STA considering knowledge about the BA type for each STA. AP informs each STA its BA Transmission Time (BATT) by including scheduling information into the same MU PPDU
The scheduling information allows STA to wake up exactly for its BA transmission and MU PPDU reception performing power save in the most effective and accurate way

## Slide 7: Explicitly scheduled BA. MU acknowledgment and PS flow
Scheduling information is STA specific and should include:
BATT Start offset which indicates the beginning of time slot provided by AP for STA to transmit its BA
Next PPDU Start offset which indicates the moment when STA should begin listening AP. At this moment AP may either start transmitting the next MU PPDU in current sequence of MU-MIMO transmission or transmit BAR to STA in case if solicited BA was not received.

## Slide 8: Explicitly scheduled BA. Scheduling signaling.
Subfields BATT Start Offset and Next PPDU Start offset indicate the corresponding values (defined previously) in microseconds.
The EOF flag indicates that the data part of A-MPDU is over and after correct reception of this Control frame STA may stop receiving
 | Frame Control | Duration | RA | TA | Block Ack Scheduling Information | FCS
Octets | 2 | 2 | 6 | 6 | 3 | 4
 | BATT Start Offset | Next PPDU Start offset | EOF | Reserved
Bits | 9 | 9 | 1 | 5
MU-MIMO Block Ack scheduling information can be delivered from AP to STAs by a special control frame included in the A-MPDU for corresponding STA

## Slide 9: Explicitly scheduled BA. Schedule signaling.
The main drawback of this method is low robustness: the Schedule frame may be lost in aggregation. The straightforward solution is repetition of this frame in different parts of A-MPDU (such reliability increase is already used for Block Ack in 11ad, see Table 9-425). E.g., it can be repeated in the beginning and in the end of A-MPDU, or it can be repeated several times in the end of A-MPDU as a rough padding to align durations of A-MPDU for different MU-MIMO streams.
Targeting 0.01 frame error rate we have 0.0001 probability that two Block Ack Schedule frames will not be received correctly
PSDU, bytes | Scheduling signaling overhead (two frames), %
256 | 0.19
4096 | 0.16
65536 | 0.05
Example of A-MPDU transmitted within EDMG MU PPDU

## Slide 10: Ack policy
Combination 01 in Ack Policy subfield of QoS Data frame is not used in 11ad
We propose to use Ack policy = 01 for QoS Data frames transmitted in EDMG MU-MIMO to indicate that BA should be sent by STA in a scheduled time slot

## Slide 11: Proposed vs. Legacy flow performance comparison
Assumptions:
Amount of data (PSDU) for all STAs in MU-MIMO is same
AP transmits each MU-MIMO stream using MCS 12 (4620 Mbps)
BAR and BA are transmitted using MCS 4 (1155 Mbps)
STAs send BA of minimal length (25+8 bytes)
Equivalent throughput gain of Proposed flow over Legacy flow
PS gain of Proposed flow over Legacy flow
The performance gains are lower for the cases when acknowledgement overhead is lower – small number of STAs in MU group and big size of data frames.

## Slide 12: Proposed vs. Legacy flow performance comparison
Equivalent throughput gain of Proposed flow over Legacy flow
PS gain of Proposed flow over Legacy flow
Assumptions:
Amount of data (PSDU) for all STAs in MU-MIMO is same
AP transmits each MU-MIMO stream using MCS 12 (4620 Mbps)
BAR and BA are transmitted using MCS 4 (1155 Mbps)
STAs send BA of maximal length (25+256 bytes)

## Slide 13: Proposed vs. Legacy flow MAX throughput estimation
Assumption:
STAs send BA of minimal length (25+8 bytes)
8 STAs in MU-MIMO
EDMG SC MCS20 (8662.5 Mbps) is used for all STAs in MU-MIMO
CB=4
PSDU, bytes | AP Throughput (Legacy flow), Gbps | AP Throughput (Proposed flow)*, Gbps | AP Throughput (Proposed flow+)*, Gbps
64 | 0.04 | 0.10 (+134%) | 0.35 (+758%)
256 | 0.17 | 0.39 (+134%) | 1.41 (+755%)
1024 | 0.66 | 1.54 (+133%) | 5.57 (+744%)
4096 | 2.62 | 6.06 (+131%) | 21.02 (+702%)
16384 | 10.20 | 22.74 (+123%) | 68.49 (+572%)
65536 | 36.74 | 73.00 (+99%) | 157.34 (+328%)
*Proposed flow – all 8 STAs are requested for BA
Proposed flow+ – only one STA is requested for BA (see Slide #3)

## Slide 14: Straw poll
Do you agree to include the text changes proposed in 11-17-1691-00-00ay-Draft text for advanced MU-MIMO acknowledgement and PS flow to the spec draft?
  Yes
  No
  Abstain