## Slide 1: Power Control for Multiuser Ranging
Date: 2017-11-07

## Slide 2: Background
P-matrix code multi-access is used by one of the MU ranging modes
In this case, Tx power control is needed for mitigating the near-far problem among the users
Trigger
UL NDP 1
UL NDP 2
AP
STA 1
STA 2
NDPA
DL NDP

## Slide 3: 11ax Power Control
11ax already defined a power control mechanism for MU UL data transmissions
  AP indicates target RSSI in User Info Field of Trigger Frame
  STA estimates the path loss using the Trigger Frame and sets Tx power to meet the target RSSI
Trigger
UL DATA 1
UL DATA 2
AP
STA 1
STA 2

## Slide 4: 11az Closed-loop Power Control
There is a polling phase before measurement phase in 11az MU.
Based on the AP’s actual RSSI in polling phase, the AP can further tune the target RSSI value for each STA in the TF for the measurement phase.
Support associated and unassociated STA
Trigger
UL NDP 1
UL NDP 2
AP
STA 1
STA 2
NDPA
DL NDP
Trigger
Poll resp. 1
Poll resp. 2
Round 1 power control
Round 2 power control
Polling phase
Measurement phase

## Slide 5: Reuse 11ax MU Features in 11az MU
For associated and unassociated STA, in addition to power control, the following features for trigger-based PPDU in 11ax MU should also be reused in 11az MU for protocol compatibility and implementation simplicity:
  Timing and frequency synchronization for uplink transmission
  Supported trigger subtypes for 11az trigger type :
    Trigger frame for polling
    Trigger frame for uplink channel sounding
    Trigger frame for LMR feedback
    Trigger frame for negotiation using random access

## Slide 6: Proposal
Reuse 11ax power control, timing and frequency synchronization as the one for 11az
  Minimize hardware changes

## Slide 7: Straw Poll
For 11az MU operation in the unassociated mode following mechanisms are reused and active:
  UL Power control.
  Timing and frequency synchronization for UL transmission.
  Supported trigger subtypes for 11az trigger type:
    TF Location -> Poll
    TF Location -> Uplink Sounding
    TF Location -> LMR
    TF Location -> (Loc. negotiation using RA) and behavior to follow RA access. Details TBD.
Note: this list may be extended in the future to accommodate OBSS operation.
Y: N: A:

## Slide 8: Motion
Move to adopt the text below to the 11az SFD, instruct the editor to include it in the TGaz SFD under the sub-section 3.2 (Protocol description) and grant editorial license to the SFD editor.
“For HEz operation in the unassociated mode the following mechanisms are reused and active:
  UL Power control.
  Timing and frequency synchronization for UL transmission.
  Supported trigger subtypes for 11az trigger type:
    TF Location -> Poll
    TF Location -> Uplink Sounding
    TF Location -> LMR
    TF Location -> (Loc. negotiation using RA) and behavior to follow RA access. Details TBD.”
Note: this list may be extended in the future to accommodate OBSS operation.
Y: N: A:

## Slide 9: Backup

## Slide 10: 11ax 28.3.14.2 Power Pre-correction
Tx power calculation
(28-113)
Path loss
Target RSSI indicated in Trigger Frame
Tx power used by user
Path loss calculation
(28-114)
AP Tx power indicated in Trigger Frame
DL received power measured by user
DL path loss

## Slide 11: 11ax 9.3.1.23 Trigger Frame Format