## Slide 1: On the issues with Odd and Even Node Polarity
Date: 2017-11-03
Name | Affiliation | Address | Phone | Email
Rob Sun | Huawei |  |  | Rob.sun@Huawei.com
Yan Xin |  |  |  | Yan.xin@Huawei.com
Edward Au |  |  |  | Edward.ks.au@huawei.com
Mengyao Ma |  |  |  | ma.mengyao@huawei.com

## Slide 2: Motivations
FB introduces the “Odd and Even Node Polarity” in [1] which defines the transmission pattern between DNs and CNs in the TDD sub-frames. The benefits are to improve the overall capacity and potentially reduce the interference.
However, we found this Odd and Even Node have the scalability and efficiency problem.
  Sinking Hole Problem (SHP)
  Uneven Traffic Problem (UTP)

## Slide 3: Precursory Assumptions
All the DNs and CNs are within the same BSS.
Each DN cannot receive multiple streams from different DNs simultaneously.
Realistically, Interference Cancellation is a hard problem.

## Slide 5: Problem Illustration (First TDD period)
DN0
DN1
DN2
DN3
O
E
CN0
CN1
CN2
CN3
E
E
O
O
O
E
DN1DN0
DN3DN2
DN1CN2
DN1CN3
CN0DN0
CN1DN0
Simultaneous
First TDD Sub-frame
1) Link DN1DN2 could be interfered from DN3 (inter-DN interference)
2) Link DN3-DN2 could also be interfered from DN1 (inter-DN interference)
DN1DN2

## Slide 6: Problem Illustration (Second TDD period)
DN0
DN1
DN2
DN3
O
E
CN0
CN1
CN2
CN3
E
E
O
O
O
E
O
DN0DN1
DN2DN3
DN0CN0
DN0CN1
CN0DN1
CN1DN1
Simultaneous
Second TDD Sub-frame
1) Link DN2 DN1 could be interfered by DN0 (inter-DN interference)
2) Link DN0DN1 could also be interfered by DN2 (inter-DN interference)
DN2DN1

## Slide 7: The Sinking Hole Problem (SHP)
Due to the Odd and Even Node polarity settings and the inter-node interference, the Link between DN1 and DN2 can not be active during the both first and second time slots (SPs)
The SHP only applies to the backhaul links.
One possible solution to avoid the sinking hole problem is to dedicate the time slots (SPs) for the link between DN1 and DN2.
  However, the latency will be noticeable.
  and the scheduling will be complex.
To generalized this problem, the Odd and Even Node polarity scheme cannot scale up in large network.

## Slide 8: Uneven Traffic Problem (UTP)
In this case, we are assuming DN0 is the end DN, DN1/DN2 are intermediate DNs, and DN3 is the portal to internet.
Also, we assume the Sinking Hole Problem could be solved.
We assume today’s traffic is uneven in both directions, i.e 80% of traffic are downlink and 20% of traffic are uplink.
We will observe the UTP due to the uneven traffic distribution.
Rob Sun, Huawei

## Slide 9: Uneven Traffic Problem (UTP) Illustration
DN0
DN1
DN2
DN3
O
E
CN0
CN1
CN2
CN3
E
E
O
O
O
E (Portal)
DN1DN0
DN3DN2
DN1CN2
DN1CN3
CN0DN0
CN1DN0
Simultaneous
First TDD Sub-frame
DN1DN2
Unused
Internet
DOWNLINK

## Slide 10: Uneven traffic problem (UTP) illustration
DN0
DN1
DN2
DN3
O
E
CN0
CN1
CN2
CN3
E
E
O
O
O
E(Portal)
O
DN0DN1
DN2DN3
DN0CN0
DN0CN1
CN0DN1
CN1DN1
Simultaneous
Second TDD Sub-frame
DN2DN1
Unused
Unused
Internet
UPLINK
Rob Sun, Huawei

## Slide 11: Potential Solution To UTP
Change the rule of Odd and Even polarity setting for DNs links.
  For instance, the Odd and Even polarity applies ONLY to DN-CN links.
  The DN-DN links should not follow the Odd and Even polarity settings.
Enable each DN to send and receive simultaneously from different sources (new methods/technologies should be introduced).

## Slide 12: Potential Solution Illustration (Downlink as Example)
DN0
DN1
DN2
DN3
O
E
CN0
CN1
CN2
CN3
E
E
O
O
O
E (Portal)
DN1DN0
DN3DN2
DN1CN2
DN1CN3
CN0DN0
CN1DN0
Simultaneous
First TDD Sub-frame
DN2DN1
Internet
DOWNLINK
Rob Sun, Huawei

## Slide 13: References
[1] IEEE 802.11-17/1321r1 “Features for mmW Distribution Network Use Case”